## Slide 1
TPC combined with channel allocation method for OBSS environment
Date: 2017-11-5
Authors:
Name | Affiliation | Address | Phone | Email
Hongyan Li | Xidian University | 2 South Taibai Road, Xi’an Shaanxi, 710071, P.R.China | +86-13709218225 | hyli@xidian.edu.cn
Ronghui Hou |  |  |  | rhhou@xidian.edu.cn
Xiaoyao Ma |  |  |  | str2num_mxy@126.com

## Slide 2: Background
The next generation WLAN is mainly used in high dense deployment scenario. There are many overlapped areas in this scenario. Therefore, the receivers in this area will suffer severe co-channel interference which leads to a decrease in throughput.
Channel allocation method can improve the co-channel interference. However, the number of the orthogonal channel is limited.
In many presentations, transmit power control has been proved that it can improve the spatial reuse and network performance.
In this contribution,
  A transmit power control combined with channel allocation method is proposed
  The comparison is shown in the simulation

## Slide 3: TPC combined with channel allocation method
Step 1: Each AP divides the STAs into two groups based on their RSSI.
  If RSSI > RSSI_Threshold, the STA is a central user
  If RSSI < RSSI_Threshold, the STA is an edge user

## Slide 4: TPC combined with channel allocation method
Step 2: AP divides the whole band into two channels.
  All the central users operate on the both channels
  The edge users of adjacent BSS operate on different channels

## Slide 5: TPC combined with channel allocation method
Step 3: AP sets two different transmit power level based on a target SINR of central users and edge users.
  When the receiver is in central area, the transmit power is
  When the receiver is in edge area, the transmit power is

## Slide 6: Simulation
Comparison between current WLAN, TPC and TPC + channel allocation.
Our method can increase the throughput by 47.28% compared to current WLAN.
Chart: Comparison of Throughput
| OBSS1 | OBSS2 | OBSS3
Current WLAN | 118.44 | 42.84 | 107.856
Only TPC | 131.796 | 96.516 | 107.856
TPC+Channel Allocation | 141.372 | 124.236 | 130.788
Parameter | Value
Num of STA | Each AP has 10 central users and 10 edge users
Num of AP | 3
CCA sensitivity level [dBm] | -62
MCS Selection | MCS2
Bandwidth | 160MHz
RTS/CTS | OFF

## Slide 7: Conclusion
In this presentations, we introduce a method called TPC combined with channel allocation to improve the network’s performance in dense scenario.
Performance of TPC and TPC combined with channel allocation has been compared.

## Slide 8: Simulation Setup details
Parameter | Value
Node | (AP x 1, STA x 20) x 3 (Half of STAs are central STA, and others are edge STA)
Traffic Model | UDP (Full Buffer)
Access Category | [EDCA, AC_BE with default parameters] [CWmin = 15, CWmax = 1023, AIFSn=2 ]
MCS Selection | MCS2
Packet Length (byte) | 63000
ACK Rate | 6.0Mbps
RTS/CTS | OFF
CCA level [dBm] | -62
AP number of antennas | 1
STA number of antennas | 1
Bandwidth | 160MHz
Tx gain | 0
Rx gain | 0