## Slide 1: Ranging ID Management
Date: 2017-11-03
Authors:

## Slide 2: Background
Association ID-like value (Ranging ID) assigned to an unassociated STA by an rSTA to facilitate the negotiation phase and subsequently the ranging phase. [1]

## Slide 3: Discussion
Similar to the Association ID (AID), the Ranging ID is also assigned when an HEz FTM session setup is completed.
  The ID for ranging operation for an unassociated STA used for measurement phase will be in the FTM Response frame. [1]
The AID and the Ranging ID do the same roles as the below:
  For identifying an intended user in the Trigger frame and the NDPA frame.
  For identifying a recipient of an RU in an HE MU PPDU.

## Slide 4: Discussion
But, differently with the Association ID, a non-AP STA may maintain one or more Ranging IDs.
  Because a non-AP STA has one Ranging ID for each AP STA with which the non-AP STA has an HEz FTM session.
  In IEEE 802.11 spec, a non-AP STA has an association with only single AP STA.

## Slide 5: Discussion
Usually, the AID is released when an association is terminated.
  Upon receipt of a Disassociation frame from a STA.
  Upon transmission of a Disassociation frame to a STA.
It would be natural to follow the same rule to release the Ranging ID.
  When an HEz FTM session is terminated, the Ranging ID corresponding to the HEz FTM session is released.

## Slide 6: Discussion
Although a termination protocol of an HEz FTM session is TBD, an explicit or an implicit HEz FTM session termination rule can be defined as an extension of the fine timing measurement termination (11.24.6.6).
  An FTM session may be terminated before then through one of the following:
    At any time during the FTM session when the responding STA is permitted to transmit a Fine Timing Measurement frame (see 11.24.6.4 (Measurement exchange)), the responding STA sends a Fine Timing Measurement frame with the Dialog Token field set to 0. [Explicit termination]
    At any time during the FTM session when the initiating STA is permitted to transmit a Fine Timing Measurement frame (see 11.24.6.4 (Measurement exchange)), the initiating STA sends a Fine Timing Measurement Request frame with the Trigger field set to 0. This frame shall not include: [Explicit termination]
      a Measurement Request element
      a Fine Timing Measurement Parameters element
    At any time during the FTM session when the initiating STA is permitted to transmit a Fine Timing Measurement frame (see 11.24.6.4 (Measurement exchange)), the initiating STA terminates the current session and requests a new session with modified Fine Timing Measurement parameters (see 11.24.6.5 (Fine timing measurement parameter modification)). [Explicit termination]
    After the number of burst instances indicated in the Number of Bursts Exponent field in the initial Fine Timing Measurement frame has been reached. [Implicit termination]

## Slide 7: References
[1] https://mentor.ieee.org/802.11/dcn/17/11-17-0462-08-00az-11-az-tg-sfd.docx

## Slide 8: SP1
Do you support the following SFD text?
When an HEz FTM session is terminated, an Ranging-ID assigned for a MU ranging operation of an unassociated STA is released.