## Slide 1: Secure Ranging Measurement
Date: 2017-11-03
Authors:

## Slide 2: Background
Spoofing attack in PHY level has been discussed in [1].
  Proposed solution was to encode the LTF sequence by applying variable CSD.
Additionally, suppressing spoofing attack in PHY level has been discussed in [2].
  Proposed solution was to replace the known LTF sequence by a random binary sequence that is unknown to an attacker.
    Sequence generation key is exchanged and encrypted before a ranging measurement.
Both contributions are saying that the LTF sequence in NDP have to be encoded in the unknown to an attacker.

## Slide 3: Replay Attack Problem
Even though a LTF sequence in a NDP is encoded, once a NDP was transmitted, an attacker can use the exposed NDP as a replay attack.
  In the below figure, the attacker transmits a fake UL-NDP (i.e., UL-NDP1) when a victim transmits an UL-NDP2 transmission.
  Because an AP didn’t notice that a victim transmitted an UL-NDP1, it considers the fake UL-NDP as a valid frame sequence.
NDPA1
UL-NDP1
AP
Victim
Attacker
Fake UL-NDP1
(In more strong TX power)
NDPA2
UL-NDP2
Jamming a PHY header of UL-NDP1
DL-NDP2
LMR
Copied

## Slide 4: Replay Attack Problem
Even though a LTF sequence in a NDP is encoded, once a NDP was transmitted, an attacker can use the exposed NDP as replay attack.
  In the below figure, the attacker transmits a fake DL-NDP (i.e., DL-NDP1) in more strong transmit power.
  Because a victim didn’t notice that an AP transmitted an DL-NDP1, it considers the fake DL-NDP as a valid frame sequence.
AP
Victim
Attacker
Fake DL-NDP1
(in more strong TX power)
DL-NDP2
LMR
UL-NDP2
NDPA2
DL-NDP1
LMR
Copied
NDPA1
UL-NDP1
Jamming a PHY header of DL-NDP1

## Slide 5: Replay Attack Problem
For avoiding such replay attack, a mechanism to verify whether a LTF sequence of a received NDP comes from the valid STA is necessary.
For example,
  In slide 3, after receiving the NDPA2 and the fake UL-NDP1, an AP shall have a mechanism to verify the received UL-NDP1 is not valid.
  In slide 4, after receiving the fake DL-NDP1 and the LMR, a STA shall have a mechanism to verify the received DL-NDP1 is not valid.

## Slide 6: Replay Attack Solution
Possible solutions – Option 1
  An UL NDP and a DL NDP include the key values for determining LTF sequences at the end of frame.
  A Location Measurement Report (LMR) frame includes key values for indicating the LTF sequences carried in the received UL NDP and transmitted DL NDP.
[Key=Key1, TOA of UL NDP] [Key=Key2, TOD of DL NDP]
NDPA
UL NDP
LMR
LTF1
Key1
DL NDP
LTF2
Key2

## Slide 7: Replay Attack Solution
Possible solutions – Option 1
  If the key values of the UL NDP and DL NDP used in a ranging measurement from the AP is not matched with those of the transmitted and received NDPs on the STA, the received LMR is not valid.
  In the below figure, a STA can figure out that the LTF sequence of the UL NDP used in the TOA calculation is different. (Key1 ≠ Key3)
[Key=Key3, TOA of UL NDP] [Key=Key2, TOD of DL NDP]
NDPA
UL NDP
LMR
LTF1
Key1
DL NDP
LTF2
Key2
UL NDP
LTF3
Key3
Attacker

## Slide 8: Replay Attack Solution
Possible solutions – Option 2
  A NDPA includes the key values for determining LTF sequences used in a following UL NDP and DL NDP.
    Key1 value in NDPA indicates that the UL NDP uses LTF1 sequence.
    Key2 value in NDPA indicates that the DL NDP uses LTF2 sequence.
  Comparing Option 1, because key values are opened before the NDP transmission, a nonlinear mapping function between key and LTF sequences have to devised and STA and AP have to exchange related security parameters.
[TOA of UL NDP] [TOD of DL NDP]
NDPA
UL NDP
LMR
LTF1
DL NDP
LTF2
Key1
Key2

## Slide 9: Replay Attack Solution
Possible solutions – Option 2
  If an attacker doesn’t know the LTF sequences derived from Key1 or Key2, an AP may consider the LTF sequence received from the attacker as a noise signal.
  But, considering a worst case that a nonlinear mapping function between key and LTF sequences is broken by an attacker, a LMR frame carrying key values for indicating the LTF sequences in Option 1 can be helpful.
[TOA of UL NDP] [TOD of DL NDP]
NDPA
UL NDP
LMR
LTF1
DL NDP
LTF2
Key1
Key2
UL NDP
LTF3
Attacker

## Slide 10: Replay Attack Solution
Possible solutions – Option 3
  Comparing Option 1 and Option 2,
    Option 1 does not need a significant change of a security protocol but it needs additional complexity in the PHY layer.
    Option 2 does not need a significant change of a PHY but it needs a major change of a security protocol and can increase a protocol overhead.
  Based on pros and cons of Option 1 and Option 2, another Option 3 is that a STA provides key values for each ranging measurement sequences through a new Protected Ranging Measurement Key Management frame or a Protected FTM Response frame.

## Slide 11: Replay Attack Solution
Possible solutions – Option 3
  Protected Ranging Measurement Key Management (RMKM) frame includes one or more pairs of a Sounding Dialog Token Number and key values (up to 64 entries) for determining LTF sequences used in an UL NDP and a DL NDP for subsequent ranging measurement sequences.
  In each ranging measurement sequence, LTF sequences used in an UL NDP and a DL NDP are identified by a Sounding Dialog Token Number (SDTN) in a NDPA frame.
NDPA SDTN=0
UL NDP
LMR
LTF1
DL NDP
LTF2
NDPA SDTN=1
UL NDP
LMR
LTF5
DL NDP
LTF6
RMKM
ACK

## Slide 12: Conclusion
This document discusses the replay attack problem and possible solutions.

## Slide 13: References
[1] https://mentor.ieee.org/802.11/dcn/17/11-17-0780-02-00az-ranging-phy-security.pptx
[2] https://mentor.ieee.org/802.11/dcn/17/11-17-0795-03-00az-phy-level-security-protection.ppt