## Slide 1: Wi-Fi Time Sensitive Networking
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | NRU HSE; IITP RAS |  |  | khorov@frtk.ru

## Slide 2: Motivation
Gaming
Wireless Remote Control
Robotics
Need delays of <1ms (defined for 5G low latency communications)

## Slide 3: IEEE 802.1 Activities
Published Standards for Time-Sensitive Networking:
IEEE Std 802.1Qbu-2016 - IEEE Standard for Local and Metropolitan Area Networks -- Bridges and Bridged Networks -- Amendment 26: Frame Preemption. It allows a Bridge Port to suspend the transmission of non time critical frames while one or more time critical frames are transmitted.
IEEE Std 802.1Qbv-2015 - IEEE Standard for Local and Metropolitan Area Networks -- Bridges and Bridged Networks -- Amendment 25: Enhancements for Scheduled Traffic. It specifies time aware queue draining to schedule the transmission of frames relative to a known time scale.
IEEE Std 802.1Qca-2015 - IEEE Standard for Local and Metropolitan Area Networks -- Bridges and Bridged Networks -- Amendment 24: Path Control and Reservation. It extends the application of Intermediate System to Intermediate System (IS-IS) to bridged networks in order to provide explicit trees for data traffic.
They are being rolled into 802.1Q by the ongoing P802.1Q-REV project.

## Slide 4: IEEE 802.1 Activities
Audio Video Bridging Standards:
IEEE Std 802.1AS-2011 - Timing and Synchronization for Time-Sensitive Applications in Bridged Local Area Networks. It provides a Layer 2 time synchronizing service that is appropriate for the most stringent requirements of consumer electronics applications. This was done in cooperation with the IEEE 1588 working group, and so the point-to-point 802.3 sublayer of 802.1AS is a specific profile of IEEE Std 1588-2008. IEEE Std 802.1AS specifies the generalized Precision Time Protocol (gPTP).
IEEE Std 802.1Qat-2010 - Virtual Bridged Local Area Networks - Amendment 14: Stream Reservation Protocol (SRP). Ongoing P802.1Qcc project specifies enhancements to SRP.
IEEE Std 802.1Qav-2009 - Virtual Bridged Local Area Networks - Amendment 12: Forwarding and Queueing Enhancements for Time-Sensitive Streams, which specifies the Credit Based Shaper.
IEEE Std 802.1BA-2009 - Audio Video Bridging (AVB) Systems. It specifies a set of usage-specific profiles to help interoperability between networked devices using the AVB specifications.

## Slide 5: What makes Wi-Fi not Time Sensitive
Packet Delay = Queueing Delay + Packet Transmission Time
A TSN packet shall wait while at least the head-of-line packet is being transmitted
Maximal PPDU duration in 11ax exceeds 5 ms
Packet Transmission Time includes channel access time and PPDU duration (plus retries, if any)
Because of unlicensed spectrum, the channel may be busy with transmission of other devices

## Slide 6: Reducing Queueing Delay
Main idea: Stop transmitting a non-TSN frame when a TSN frame arrives.
This is similar to IEEE Std 802.1Qbu-2016
Open issues:
Shall the transmission of the non-TSN frame be considered as unsuccessful transmission attempt?
How to save partially transmitted data?
How can the receiver of the TSN frame microsleep during non-TSN transmissions for other STAs?

## Slide 7: Reducing Packet Transmission Time
Main idea: reduce channel access time using another radio, adaptively choose robust MCS and protect transmission from collisions

## Slide 8: Reducing Channel Access Time
Main idea: use dual radio, similarly to WUR (802.11ba)
The main radio is used for usual transmission.
The auxiliary radio is used to ask neighboring STAs to stop ongoing non-TSN transmissions.
Radios operate in different bands
The auxiliary radio cannot be used for data transmission.
It can be combined with WUR or extend WUR.
It can be also used to wake-up the intended receiver from microsleep or doze state.

## Slide 9: Simple Example of WTSN Handshake
Backoff
STA2 Receives TSN Notification and stops its transmission
TSN Frame arrives in the queue
STA1
TSN Notification
TSN Frame
STA2
Ongoing Transmission
Cancelled Transmission
AIFS
Sent with auxiliary radio
AP
ACK

## Slide 10: Straw Poll
Should the WG address this problem?
Yes
No
Abstain