## Slide 1: Pre-Association Security Negotiation (PASN) for 11az
1
Date: 2017-10-16
Authors:
Name | Affiliations | Address | Phone | email
Nehru Bhandaru | Broadcom Ltd. | 190 Mathilda Place, Sunnyvale CA 94086 | +1 408-922-5924 | nehru.bhandaru@broadcom.com
Matthew Fischer | Broadcom Ltd. | 190 Mathilda Place, Sunnyvale CA 94086 | +1 408-543-3370 | matthew.fischer@broadcom.com
Jonathan Segev | Intel |  |  | jonathan.segev@intel.com
Chittabrata Ghosh | Intel |  |  | chittabrata.ghosh@intel.com
Benny Abramovsky | Intel |  |  | 
Ido Ouzieli | Intel |  |  | 

## Slide 2: Introduction
TGaz FRD 16/0424r7 - r38 – Requires support for PASN
  One secured mode that provides Authentication, Key Management, Encryption and Message Integrity in unassociated state
TGaz SFD 11-17/0462r5
  Security setup optional, but prior to 11az Protocol Negotiation
  Out of band keys may be used
  Fields over which range measurements are performed are protected
2

## Slide 3: Discussion – PASN Protocol
Before 802.11 association; which may or may not happen
Needs to work with existing RSN mechanisms
  PSK, 802.1x, PMK Caching, FILS, FT
A PMK may or may not exist
  May be negotiated out of band (See SFD)
  OWE (RFC 8110)
Leverage existing mechanisms
  Can not be too complex
SFD needs high level agreement and a section on PASN
  discovery and signaling
  What frames to use
  Where PMK comes from
  Whether to support negotiation w/o a PMK i.e. derive as part of PASN
  Whether high level, unspecified authentication protocols are supported
  How PASN may support 11az security
3

## Slide 4: Straw Poll 0
Add to SFD Security section
  PASN Authentication
  PASN authentication allows message authentication, encryption, and message integrity to be provided for selected 802.11 frames that require such protection. Whether such protection is required for a frame is determined by the security parameters negotiated for the exchange (e.g. 11az Protocol Negotiation) to which the frame belongs
  Y: N: A:
4

## Slide 5: Discussion – PASN Discovery
Options
  Use extended capabilities in beacons and probe responses
  Use RSNE to advertise PASN AKM
  Other
Use of RSNE seems sufficient
5

## Slide 6: Straw Poll 1
Add to SFD PASN Authentication section
An AP indicates PASN support by advertising a TBD PASN AKM in RSNIE that is included in Beacons and Probe Responses, and also in neighbor reports and reduced neighbor reports where supported.
A non-AP STA selects use of PASN authentication based on the security requirements of features that need pre-association security. 11az protocol security for an un-associated STA requires PASN.
Y: N: A:
6

## Slide 7: Discussion – PASN Framing
What frames are used
  Authentication Frames
  Public Action Frames
PASN is best delivered as an authentication algorithm
  Like FILS
  Define a new authentication algorithm to drive the frame exchange
7

## Slide 8: Straw Poll 2
Add to SFD PASN Authentication section
An non-AP STA and an AP use 802.11 authentication frames with the Authentication algorithm number set to TBD (PASN Authentication) for the protocol exchange.
Y: N: A:
8

## Slide 9: Discussion – Where does PMK come from
What is the PMKID used, if any
  PASN need not have any prior PMK or PMKID
  PASN can use PMKID defined by another AKM
    PASN possibly needs to carry that AKM
PASN needs to provide support PMKID exchange and DH exchange
  Leverage existing IEs.
    Most of what is needed should already be there
  Keep NONCEs in derivation or migrate to DH for freshness
Options
  Prior PMK via PSK, FILS, FT, 802.1x, OWE, Out of Band etc.
  Derived as part of PASN
    No authentication, use DH exchange (Similar to OWE)
  Unspecified exchange – e.g. Wrapped Data, Vendor Specific
9

## Slide 10: Straw Poll 3
Add to SFD PASN Authentication section
An non-AP STA optionally, via PASN protocol, proposes to an AP a base AKM and PMKID(s) used to identify the PMK used for derivation of PTK for key confirmation and frame protection.
An AP optionally, via PASN protocol, indicates to the non-AP STA, a base AKM and PMKID corresponding to the PMK used for derivation of PTK for key confirmation and frame protection.
A non-AP STA and AP exchange ephemeral public keys to derive protection keys via PASN.
The PTK for the exchange is derived from PMK, if any, and the shared secret from the ephemeral key exchange.
Y: N: A:
10

## Slide 11: Discussion - what else needs protection
When optional security is used
  11az Protocol Negotiation
    Integrity protection is important
    Privacy could be optional
  LMR/Measurement Reports
    Integrity protection is important
    Privacy could be optional
11

## Slide 12: Straw Poll 4
Add to SFD Security section
  802.11az protocol negotiation and measurement reports shall be integrity protected and (optionally?) encrypted for privacy.
  Y: N: A:
12

## Slide 13: Discussion – How 11az frames are protected
Negotiation Frames
  Use PMF
Measurement Frames
  Keys derived from existing SA
  Protection Scheme
LMR
  Protected using PMF
  How to protect in MU case
Triggers etc.
  Do they need protection?
  NDPA/NDP
    No control frame protection, but measurement (LTF) sequence is negotiated/protected
13

## Slide 14: References
IEEE P802.11-REVmdTM/D0.1, May 2017
11-15-0030-09-0ngp-ngp-par-draft
11-15-0262-04-0ngp-csd-working-draft
11-16-0137-00-00az-ngp-use-case-document
11-16-0424-07-00az-functional-requirements-for-11az
11-17-1127-01-00az-comments-on-11az-functional-requirements
11-16/1643-00-00az-preassociation-negotiation-of-management-frame-protection
Slide 14