## Slide 1: MU Ranging Sequence
Date: 2017-11-08
Authors:

## Slide 2: Motivation/Background
Need to specify some of the details in the MU ranging sequence, like:
  Polling phase
  STA to AP LMR feedback
  ACK-ing of LMR feedback
  Sequence specification

## Slide 3: MU Ranging Sequence (1)
Polling:
  We only need a single polling phase prior to the measurement phase.
STA to AP LMR feedback:
  Desirable to have STA to LMR feedback as an option for network centric use cases
  To be negotiated at service establishment.
ACK-ing of LMR feedback:
  The AP is responsible for scheduling measurement opportunities interval that meets the refresh rate negotiated by STA, accounting for possible loss of packages.
  => No need for acknowledgment or retransmissions of either AP to STA or STA to AP LMR feedback.

## Slide 4: MU Ranging Sequence (2)
Sequence:
  [TF Poll -> Poll Rsp. -> (TF Sound -> UL NDP) x N -> DL NDPA -> DL NDP -> AP2STA LMRs] x M
where:
  The arrow ‘->’ denotes a SIFS interval
  The AP2STA LMRs are unicast report frames
    Supported PHY frame formats TBD
  M is the number of MU ranging groups and is constraint by availability window size.
  N is the number of STA groupings, separated in time for UL sounding.

## Slide 5: MU Ranging Sequence (3)
Sequence with for STA to AP LMR feedback:
  [TF Poll -> Poll Rsp. -> (TF Sound -> UL NDP) x N -> DL NDPA -> DL NDP -> AP2STA LMRs -> TF LMR -> STA2AP LMRs]
Note:
  AP to STA LMR feedback are carried in an HE MU PPDU.

## Slide 6: Straw Poll
Polling:
  There is a single polling phase prior to the measurement phase.
STA to AP LMR feedback:
  STA to LMR feedback is supported.
  Is negotiated at service establishment.
ACK-ing of LMR feedback:
  AP to STA or STA to AP LMR feedback is neither acknowledged or retransmitted
Sequence:
  [TF Poll -> Poll Rsp. -> (TF Sound -> UL NDP) x N -> DL NDPA -> DL NDP -> AP2STA LMRs] x M
where:
  The arrow ‘->’ denotes a SIFS interval
  The AP2STA LMRs are unicast report frames
    Supported PHY frame formats TBD
  M is the number of MU ranging groups and is constraint by availability window size.
  N is the number of STA groupings, separated in time for UL sounding.
Sequence with for STA to AP LMR feedback:
  [TF Poll -> Poll Rsp. -> (TF Sound -> UL NDP) x N -> DL NDPA -> DL NDP -> AP2STA LMRs -> TF LMR -> STA2AP LMRs]
Note:
  AP to STA LMR feedback are carried in an HE MU PPDU.
We support the following specifications for MU ranging:
Y: N: A:

## Slide 7: Motion
Polling:
  There is a single polling phase prior to the measurement phase.
STA to AP LMR feedback:
  STA to LMR feedback is supported.
  Is negotiated at service establishment.
ACK-ing of LMR feedback:
  AP to STA or STA to AP LMR feedback is neither acknowledged or retransmitted
Sequence:
  [TF Poll -> Poll Rsp. -> (TF Sound -> UL NDP) x N -> DL NDPA -> DL NDP -> AP2STA LMRs] x M
where:
  The arrow ‘->’ denotes a SIFS interval
  The AP2STA LMRs are unicast report frames
    Supported PHY frame formats TBD
  M is the number of MU ranging groups and is constraint by availability window size.
  N is the number of STA groupings, separated in time for UL sounding.
Sequence with for STA to AP LMR feedback:
  [TF Poll -> Poll Rsp. -> (TF Sound -> UL NDP) x N -> DL NDPA -> DL NDP -> AP2STA LMRs -> TF LMR -> STA2AP LMRs]
Note:
  AP to STA LMR feedback are carried in an HE MU PPDU.
Move to adopt the text in the TGaz SFD and grant the SFD editor editorial license:
Y: N: A:
For MU ranging:

## Slide 8
Thank You