## Slide 1: Frame Responding Rules for NDP Ranging
Date: 2017-11-05
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Ln, Santa Clara, Santa Clara |  | liwenchu@marvell.com
Feng Jiang | Intel | 3600 Juliette Ln, Santa Clara, CA 95054 |  | feng1.jiang@intel.com
Christian Berger | Marvell | 5488 Marvell Ln, Santa Clara, Santa Clara |  | crberger@marvell.com
Niranjan Grandhe | Marvell | 5488 Marvell Ln, Santa Clara, Santa Clara |  | ngrandhe@marvell.com
Qinghua Li | Intel | 3600 Juliette Ln, Santa Clara, CA 95054 |  | qinghua.li@intel.com

## Slide 2: Recap of SU and MU NDP Ranging
  The measurement + LMR (location measurement report) report phase for SU NDP ranging has the following frame exchange sequence.
    UL NDPA-->UL NDP-->DL NDP-->DL LMR Report
  Immediate LMR report and delay LMR report are allowed for SU NDP ranging.
  The measurement + LMR report phase for MU NDP ranging has the following frame exchange sequence:
    (DL Trigger--> UL NDP)xN->DL NDPA-->DL NDP--> (DL MU) AP2STA LMR Report--> DL Trigger ->(UL MU) STAs2APLMR Report
  Immediate or Delayed LMR report is used for MU NDP ranging.
  Potentially TOA+TOD and CSI can be used for LMR.
    We need to define which one should be used for NDP ranging.
Note: --> is SIFS

## Slide 3: MU NDP Ranging Report Content
  Discussion:
    The overhead of TOA+TOD is low.
    CSI does not scale well to MU usages because the CSI message size linearly increases with the number of transmit and receive antennas and the number of STAs.
    AP can handle the calculation of TOA, TOD.
      AP has enough time to prepare the delayed MU LMR report.
  Proposal: TOA and TOD LMR report are allowed for MU NDP ranging only.

## Slide 4: SU NDP Ranging Report Content
  Discussion:
    As defined by MU NDP ranging, AP already support the calculation of TOA, TOD.
      TOA+TOD report should be mandatory.
    If CSI is used in SU NDP ranging, one CSI report is not as high as MU CSI report.
      CSI report should be allowed as an optional feature.
  Proposal: For SU NDP ranging, the following LMR is defined:
    TOA + TOD LMR report is mandatory
    the support for CSI report is optional for both ISTA and RSTA and the use of CSI is agreed upon during negotiation.

## Slide 5: BW and MCS/Rate Reus of Immediate SU LMR Ranging Feedback
  For NDPA+ NDP+NDP + immediate Ranging Report, Ranging Report is prepared by hardware.
    NDPA can be 11a/g/HT/VHT/HE PPDU and different bandwidth.
  To simplify the responding implementation:
    The data rate/MCS of Ranging Report should be decided by the AP.
    The bandwidth of ranging report should be no wider than the bandwidth of the soliciting NDPA.

## Slide 6: Straw Poll 1
  Do you agree to add the following text to 11az SFD:
    For MU Ranging AP2STA LMR feedback consists of TOA and TOD reporting only
    For MU Ranging STA2AP LMR feedback consists of TOA and TOD reporting only
    Y:
    N:
    A:
.

## Slide 7: Straw Poll 2
  Do you agree to add the following text to 11az SFD:
    for RSTA2ISTA SU LMR feedback, support of TOA and TOD is mandatory and CSI report is optional for both ISTA and RSTA and agreed upon during negotiation
      Y:
      N:
      A:
.

## Slide 8: Straw Poll 3
  Do you agree to add the following text to 11az SFD:
    The bandwidth and the MCS/rate of the immediate SU NDP ranging report are defined by:
      The data rate/MCS of Ranging Report is solely decided by the RSTA.
      The bandwidth of ranging report is not wider than the bandwidth of the soliciting NDPA.
.
.
      Y:
      N:
      A:
.

## Slide 9: Motion 1
  Move to add the following text to 11az SFD:
    For MU Ranging AP2STA LMR feedback consists of TOA and TOD reporting only
    For MU Ranging STA2AP LMR feedback consists of TOA and TOD reporting only
    Y:
    N:
    A:
.

## Slide 10: Motion 2
  Move to add the following text to 11az SFD:
    for RSTA2ISTA SU LMR feedback, support of TOA and TOD is mandatory and CSI report is optional for both ISTA and RSTA and agreed upon during negotiation
      Y:
      N:
      A:
.

## Slide 11: Motion 3
  Move to add the following text to 11az SFD:
    The bandwidth and the MCS/rate of the immediate SU NDP ranging report are defined by:
      The data rate/MCS of Ranging Report is solely decided by the RSTA.
      The bandwidth of ranging report is not wider than the bandwidth of the soliciting NDPA.
.
.
      Y:
      N:
      A:
.