## Slide 1: Further Scalable Location Performance Analysis
Date: 2017-11-08
Authors:

## Slide 2: General Simulation Procedure
AS1
AS2 (x2,y2)
Client
(x0,y0)
Unknowns:
AS clock offsets n1, n2, …, n6 (w.r.t. client clock, i.e. n0=0)
Client coordinates x0,y0
Modeling of imperfections:
For simplicity
  Clock offsets ni =0 but unknown
  No clock drifts modeled
1 ns stdev Gaussian clock gitter
Abs of (1 m stdev Gaussian) multipath error
0.33 ns residual error when clock knowledge assumed
AS3
AS4
AS5
AS6
Setup:
6 ASs in circle with 50 m radius
1 client

## Slide 3: DToA Simulation Procedure
AS1
AS2 (x2,y2)
Client (x0,y0)
Measurements:
One transmission in each direction between each pair of ASs
Client listens to transmissions
Location estimation:
E.g. iteration with Newton’s method to solve for least squares solution to non-linear system of equations for measured DToAs.
When specified, showing average of 10 realizations of each client drop
AS3
AS4
AS5
AS6
Not all transmissions depicted!
AS to AS multipath error same in both directions.

## Slide 4: CToA Simulation Procedure
AS1
AS2 (x2,y2)
Client (x0,y0)
Measurements:
One transmission in each direction between each pair of ASs
Client listens to transmissions
Location estimation:
E.g. iteration with Newton’s method to solve for least squares solution to non-linear system of TOD/TOA equations position.
When specified, showing average of 10 realizations of each client drop
For method using tracked clock knowledge, a first estimation of the clock offsets are computed from 10 realizations.
AS3
AS4
AS5
AS6
Not all transmissions depicted!

## Slide 5: DToA and CToA w/o client tracking
Call in comment::
CToA here outperforms DToA when NOT considering client position tracking.
Client outside circle
Multipath error
  Proxy - Abs of Gaussian
  MU-ranging protocol uses symmetric AS to AS multipath errors
‘Tracked’ clocks are initialized using average of 10 other measurements

## Slide 6: DToA and CToA w/o client tracking
CToA with tracked clocks

## Slide 7: DToA and CToA with client tracking
Client outside circle
Multipath
  Proxy - Abs of Gaussian
  MU-ranging protocol uses symmetric AS to AS multipath errors
Client location ‘tracking’ modeled by averaging 10 measurements
‘Tracked’ clocks are initialized using average of 10 other measurements
Call in comment::
DToA here outperforms (or equals) CToA when considering client position tracking.

## Slide 8: DToA and CToA with client tracking
Note elongated shape of location error also for ‘CToA’ with tracked clocks.

## Slide 9
Thank You

## Slide 10
Appendix

## Slide 11: Newton’s method for solving non-linear equation
x
x1
x3
x2
etc.
Solve equation:

## Slide 12: Solving of non-linear system of equations
Use Newton’s method for multiple variables:
Iterate according to:
Non linear system of equations:
Linearization:
where
Over-determined non-linear system of equation to solve for Dx:
Least squares solution for iterative step:
- solve for x*

## Slide 13
DToA
‘Differential Time-of-Arrival’
Location
See [1,2 and 3]

## Slide 14: Propagation paths and time stamps
AP1
AP2
Client
Illustrating timing diagram showing double sided feedback of time-stamps:
t2
t1
t4
t3
DL NDP
UL MU NDP
t5
t6
t2, t3
t1, t4
‘AP to STA feedback’
‘STA to AP feedback’

## Slide 15: Double-Sided Differential Distance Calculation
The client STA listens to the exchanges between the AP1 and AP2 and records the time t5 when it receives the UL MU NDP from AP2 and the time t6 when it receives the DL NDP from AP1.
The client also listens to the relayed t2 and t3 from AP1 and the relayed t1 and t4 in the feedback from AP2.
The differential distance between the client STA and AP1 vs. AP2 can now be calculated as follows:
  D_01 = [t6 – t5 – (t3 – t2 + T_12)] * c
  Using T_01 = [(t4 – t1) – (t3 – t2)]/2
  We get D_01 = [t6 – t5 – (t3 – t2 + 0.5*t4 – 0.5*t1 – 0.5*t3 + 0.5*t2)]*c
  Or finally:
Note that the above expression for the differential distance D_12 does not depend on the ToF, T_12, between AP1 and AP2. Thus this method of calculating D_12 is insensitive to LOS obstructions between AP1 and AP2.
D_12 = [t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1]*c

## Slide 16: DToA Location Estimation Calculations
AP1
AP2
AP3
Client
(x0,y0)
Unknowns:
Client coordinates x0,y0
2 unknowns
Equations:
Differential ToF equations
  DToA12 = (R01-R02)/c
  DToA13 = (R01-R03)/c
  DToA23 = (R02-R03)/c
3 equations
Rij
R02(x0,y0)
In two dimensions with 3 APs:
(x3,y3)
Solve for location, e.g. with Newton iterations – described in following slides.
t1
t5
t2
t3
t4
t6
DTOF12 = t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1

## Slide 17: Solving of non-linear system of equations
Use Newton’s method for multiple variables:
Iterate according to:
Non linear system of equations:
Linearization:
where
Over-determined non-linear system of equation to solve for Dx:
Least squares solution for iterative step:
- solve for x*

## Slide 18: Our derivatives
To simplify the equations, measure time in light seconds - the distance light travels in one second.

## Slide 19: Iterative solution for client position (x0,y0)
Iterations:
Step calculation. LS solution to:
Note: Time in units of light seconds

## Slide 20
Joint Clock Offsets and
Client Location Estimation
See [4,5 and 6]

## Slide 21: Joint Clock Offsets and Client Location and Estimation Calculations
We are here using the CToA method [4,5 and 6] only to do joint AP clock offset and client position estimation. We are not modeling nor tracking any drift in the clocks. We are not using the Kalman filter approach for the calculations described in [4,5 and 6] here.

## Slide 22: Joint Clock Offsets and Client Location Estimation
AP1
AP2
AP3
Client
(x0,y0)
Unknowns:
AP clock offsets n1, n2 and n3 (w.r.t. client clock, i.e. n0=0)
Client coordinates x,y
5 unknowns
Equations:
AP to AP propagations:
  TOAi - ni = TODj - nj + Rij/c
AP to client propagations:
  TOA0 = TODj - nj + R0j(x,y)/c
9 equations
TOD1
TOA2
TOA0
Rij
R02(x0,y0)
In two dimensions with 3 APs:
(x3,y3)
Solve for location, e.g. with Newton iterations – described in following slides.

## Slide 23: Solving of non-linear system of equations
Use Newton’s method for multiple variables:
Iterate according to:
Non linear system of equations:
Linearization:
where
Over-determined non-linear system of equation to solve for Dx:
Least squares solution for iterative step:
- solve for x*

## Slide 24: Our derivatives
To simplify the equations, measure time in light seconds - the distance light travels in one second.

## Slide 25: Iterative solution for client position (x0,y0)
Iterations:
Step calculation. LS solution to:
Note: Time in units of light seconds

## Slide 26
References

## Slide 27: References
[1] “Client Positioning using Timing Measurements between Access Points”, Erik Lindskog, Naveen Kakani, Raja Banerjea, Jim Lansford and Jon Rosdahl, IEEE 802.11-13/0072r1.
[2] “A Low Overhead Receive Only Wi-Fi Based Location Mechanism”, Erik Lindskog, Hong Wan, Raja Banerjea, Naveen Kakani and Dave Huntingford, Proceedings of the 27th International Technical Meeting of The Satellite Division of the Institute of Navigation (ION GNSS+ 2014), Tampa, Florida, September 2014, pp. 1661-1668.
[3] “Passive Location”, Erik Lindskog, Naveen Kakani and Ali Raissinia, IEEE 802.11-17/0417r0.
[4] “Scalable Location Protocol”, Erik Lindskog, Naveen Kakani and Ali Raissinia, IEEE 802.11-17/0417r0.
[5] “High-Accuracy Indoor Geolocation using Collaborative Time of Arrival (CToA) - Whitepaper”, Leor Banin, Ofer Bar Shalom, Nir Dvorecki, Yuval Amizur, IEEE 802.11-17/1387r0.
[6] “Collaborative Time of Arrival (CToA)”, Ofer Bar Shalom, Yuval Amizur, Leor Bani, IEEE 802.11-17/1308r0.
[7] “Scalable Location Performance”, Erik Lindskog, Naveen Kakani and Ali Raissinia, IEEE 802.11-17/1372r1.
[8] “CToA Protocol Analysis”, Ofer-Bar Shalom, Yuval Amizur, Leor Banin and Nir Dvorecki, IEEE 802.11-17/1309r0.