## Slide 1: Discussion on detection schemes and thresholds
November, 2017
Authors:
Name | Company | Phone | email
Shubhodeep Adhikari | Broadcom |  | shubhodeep.adhikari@broadcom.com
Sindhu Verma | Broadcom |  | sindhu.verma@broadcom.com
Vinko Erceg | Broadcom | +1 858 208 6982 | vinko.erceg@broadcom.com

## Slide 2: Concerns on 802.11ax using an ED threshold at -72dBm
EN 301 893 has the following options for the CCA threshold:
      Option 1: ED = -62dBm for 802.11ac and earlier 802.11 devices
      Option 2: ED = -72dBm (at 23dBm tx power) for all others
So, 802.11ax is forced to use Option 2.
However, if 802.11ax uses Option 2, it will get lower channel access in presence of legacy 802.11 and also in presence of other unlicensed technologies (such as LAA), for the following reasons:
      In order to ensure backward compatibility, 802.11ax must defer to own-BSS nodes at -82dBm or lower. Additionally, it must use an ED threshold at -72dBm. This means, 802.11ax will use the same PD threshold as legacy 802.11 but use an ED threshold 10dB lower than legacy 802.11. Due to this “imbalance” in CCA thresholds, 802.11ax will get a lower proportion of channel access in presence of legacy 802.11.
      802.11ax will use the same ED threshold at -72dBm as LAA, but additionally use a lower PD threshold at -82dBm to defer to at least own-BSS nodes. However, LAA will use the same higher ED threshold for all other nodes. Hence, in the presence of LAA, 802.11ax will get a lower proportion of channel access.

## Slide 3: Concerns regarding an ED-only threshold at -72dBm
    An ED-only detection threshold at -72dBm exists only because it was shown by simulations, primarily in 3GPP, that by using ED = -72dBm LAA can be fair to 802.11 which uses ED = -62 dBm and PD = -82dBm.
    Hence, determination of ED = -72dBm involved the following factors:
      Co-channel 802.11 using ED = -62dBm and PD = -82dBm
      Fairness criterion defined by 3GPP for LAA
      The 3GPP simulation configuration (which has been argued by many entities including IEEE, to not being reflective of the reality of 802.11 deployments, due to miniscule % of links below -72dBm)
      Compromises among companies whose simulation results showed a wide difference in the value of LAA ED threshold which would be fair to co-channel 802.11
    There have been no evaluations regarding the fairness if 802.11 were to use an ED of -72dBm along with a PD of -82dBm
    Hence, ED = -72 dBm cannot be technically justified except when it is used by only LAA

## Slide 4: Advantages of the 802.11 scheme with a higher ED and a dynamically adjustable PD
The ED threshold = -62dBm is a much higher value that is used as a fallback if a device is not able to detect preambles from another 802.11 device.
The PD threshold is varied dynamically based on policy:
      Lower than -82dBm in order to protect weaker links, often below -92dBm till the point a device can decode another devices’ preamble.
      Higher than -82dBm to enable spatial reuse if the corresponding increase in parallel transmission is estimated not to harm the network.
      This dual threshold mechanism has been found to be efficient and fair in the numerous 802.11 deployments over many years.
On the contrary, the above dynamic behavior cannot be achieved by ED, since it is not feasible to set the ED threshold very low. This is also acknowledged by 3GPP in their LS to IEEE “RAN1 recognized the technical difficulties in operating at a very low energy threshold”.
Even simulations in 3GPP RAN1 had shown that if both 802.11 and LAA use the dual threshold option it provides the best and most balanced performance for both 802.11 and LAA

## Slide 5: Proposal
802.11ax be allowed to use Option 1 in EN 301 893 i.e. a dual threshold mechanism (PD = -82dBm and ED = -62dBm). This should be done by either:
Preferred option: Add a reference to 802.11ax in EN 301 893
      Adding such a reference previously had opposition in ETSI
      However, it is believed that this position may be softening as a) there is a realization that there is no other clear way to fairly accommodate 802.11 and b) other options may be significantly more complicated and controversial.
Other option: Use a common detection-only preamble for all technologies
      The least disruptive option is to use 802.11 preamble