## Slide 1: Beamforming protocol differences for mmWave Distribution Networks
Date: 2017-12-13
Name | Affiliation | Address | Phone | Email
Payam Torab | Facebook | 1 Hacker Way, Menlo Park, CA 94025, USA |  | ptorab@fb.com
Krishna Gomadam |  |  |  | kgomadam@fb.com
Djordje Tujkovic |  |  |  | djordjet@fb.com

## Slide 2: Overview
We presented a general description of a multi-purpose beamforming protocol for mmWave Distribution Networks in [1]-[3]
  We identified asynchronous and synchronous protocol flavors – referring to Responder’s initial sector sweep behavior, with Initiator behavior largely the same
    Asynchronous: Responder sweeps its receive beams asynchronously from Initiator, until it is hit with an initiator beam, when it shifts its sweeping pattern to align with TDD slots
      Applications: Adding a new STA to the Distribution Network
    Synchronous: Responder is aware of (provided with) a sweeping schedule (TDD slots) from the beginning, sweeping receive sectors in alignment with TDD slots
      Applications: Beam refinement, interference scan
We review the 802.11ad sector sweep performance with directional receive to illustrate the benefits of the proposed protocol

## Slide 3: Need for sector sweep with directional receive
In Distribution Networks, link budget for MCS 0 with omni receive can be easily larger than MCS 12 with directional receive
Further, MCS 0 often needs to be de-sensed for practical issues such as early weak interference (narrowing the SNR gap with MCS 12)
Assumptions: 802.11ad Channel 2, 25 Celsius temperature, EIRP limit 40 dBm, Transmit antenna gain 27.59 dBi, Receive antenna gain 0 dBi or 27.59 dBi (36 elements with 3 dBi gain per element), P1dB -1 dBm, Noise figure 8 dB, implementation loss 4 dB (analog) and 4 dB (digital), light fog and moderate rain assumed.
200 m
250 m
Link operable at MCS 12 but cannot close at MCS 0 with omni receive
500
MCS 0 SNR
MCS 12 SNR
~25 dB
Receive antenna gain
> 25 dBi
130 m
~20 dB
MCS 0 SNR
(de-sensed by 5 dB)
MCS 12 SNR
802.11ad and 802.11ay (so far) have assumed link viability with omni receive at MCS 0
Protocol proposal in [3, 4] addressed this limitation for Distribution Networks

## Slide 4: Beamforming with directional receive A-BFT procedure (beacons and SSW frames)
A-BFT
BTI
Simplifications (to focus on key points): Responder knows the BI duration, packet field width limitations (e.g., FSS) ignored, no TRN-R appended to beacons
BI
BI
Sweep ISTX
of ITX transmit beams
A-BFT
BTI
BI
Sweep RSTX
of RTX transmit beams
Listen on one of RRX receive beams
Listen on one of IRX receive beams
Parameter | Value | Scenario | Unit
Longest data interruption | D = BTI plus A-BFT duration | 530 | µs
Beamforming completion time |  | 15,376 | Beacon Intervals
Total time spent on beamforming |  | 8,142 | msec
Parameter | Value | Scenario | Unit
Longest data interruption | D = BTI plus A-BFT duration | 530 | µs
Beamforming completion time |  | 15,376 | Beacon Intervals
Total time spent on beamforming |  | 8,142 | msec
Initiator
Responder
A-BFT
BTI
BI
BI
Sweep ISTX
of ITX transmit beams
A-BFT
BTI
BI
Keep transmitting on reciprocal beam
Listen on one of RRX receive beams
Initiator
Responder
Listen on reciprocal beams
(RSTX = ISTX)
Parameter | Value | Scenario | Unit
Longest data interruption | D = BTI plus A-BFT duration | 530 | µs
Beamforming completion time |  | 124 | Beacon Intervals
Total time spent on beamforming |  | 66 | msec
Parameter | Value | Scenario | Unit
Longest data interruption | D = BTI plus A-BFT duration | 530 | µs
Beamforming completion time |  | 124 | Beacon Intervals
Total time spent on beamforming |  | 66 | msec
No
reciprocity
With
reciprocity
Parameter | Description | Scenario
IRX | Initiator receive beams | 31
ITX | Initiator total transmit beams | 31
ISTX | Initiator transmit beams swept in each iteration (BTI) | 8
RRX | Responder receive beams | 31
RTX | Responder total transmit beams | 31
RSTX | Responder transmit beams swept in each iteration (A-BFT) | 8

## Slide 5: Beamforming with directional receive SLS procedure (SSW frames)
R-TXSS
I-TXSS
BI
BI
Sweep ISTX
of ITX transmit beams
R-TXSS
I-TXSS
BI
Sweep RSTX
of RTX transmit beams
Listen on one of RRX receive beams
Listen on one of IRX receive beams
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-TXSS, R-TXSS, SSW-Feedback and SSW-Ack durations + 3×MBIFS | 316 | µs
Beamforming completion time |  | 15,376 | Beacon Intervals
Total time spent on beamforming |  | 4,860 | msec
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-TXSS, R-TXSS, SSW-Feedback and SSW-Ack durations + 3×MBIFS | 316 | µs
Beamforming completion time |  | 15,376 | Beacon Intervals
Total time spent on beamforming |  | 4,860 | msec
Initiator
Responder
R-RXSS
I-TXSS
BI
BI
Sweep ISTX
of ITX transmit beams
R-RXSS
I-TXSS
BI
Listen on one of RRX receive beams
Initiator
Responder
Listen on reciprocal beams
(RSTX = ISTX)
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-TXSS, R-TXSS, SSW-Feedback and SSW-Ack durations + 3×MBIFS | 316 | µs
Beamforming completion time |  | 124 | Beacon Intervals
Total time spent on beamforming |  | 39 | msec
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-TXSS, R-TXSS, SSW-Feedback and SSW-Ack durations + 3×MBIFS | 316 | µs
Beamforming completion time |  | 124 | Beacon Intervals
Total time spent on beamforming |  | 39 | msec
No
reciprocity
With
reciprocity
Parameter | Description | Scenario
IRX | Initiator receive beams | 31
ITX | Initiator total transmit beams | 31
ISTX | Initiator transmit beams swept in each iteration (ISS) | 8
RRX | Responder receive beams | 31
RTX | Responder total transmit beams | 31
RSTX | Responder transmit beams swept in each iteration (RSS) | 8
Simplifications (to focus on key points): Responder knows the BI duration, packet field width limitations (e.g., FSS) ignored
SSW-Feedback and SSW-Ack follow I-TXSS and R-TXSS
(not shown in the figure)
SSW-Feedback and SSW-Ack follow I-TXSS and R-TXSS
(not shown in the figure)
Keep transmitting on reciprocal beam

## Slide 6: Protocol performance
11ad sector sweep model is generally not a good fit for Distribution Networks
  Overhead increased with directional receive
  Reciprocity (already available through geometric beamforming) is not utilized to reduce overhead
  BTI + A-BFT: Dependency on beacon interval, which is decided administratively and based on different metrics (discoverability, overhead, network synchronization)
  SLS through SSW frames: RSS phase can be wasteful when directional receive beam is not hit
The sector sweep protocol in [3] addresses these shortcomings
Assumptions: Initiator and responder having 31 transmit and 31 receive beams, only one ISS + RSS exchange during each beacon interval, beacon interval 100 TUs (102.4 ms), TDD Interval 400 µs, TDD SSW+ TDD SSW + TDD SSW Feedback + applicable IFS’s 47 µs
Beamforming protocol in [3] using packets in [4]
With reciprocity
Without reciprocity
Completion time dependent on beacon interval

## Slide 7: Optimizing for reciprocity: SLS with RSS removed
Beamforming protocol proposed in [3] is essentially the above protocol with frame transmissions spread out in time to reduce latency
R-RXSS
I-TXSS
BI
BI
Sweep ISTX
of ITX transmit beams
R-RXSS
I-TXSS
BI
Listen on one of RRX receive beams
Initiator
Responder
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-TXSS, R-TXSS, SSW-Feedback and SSW-Ack durations + 3×MBIFS | 316 | µs
Beamforming completion time |  | 124 | Beacon Intervals
Total time spent on beamforming |  | 39 | msec
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-TXSS, R-TXSS, SSW-Feedback and SSW-Ack durations + 3×MBIFS | 316 | µs
Beamforming completion time |  | 124 | Beacon Intervals
Total time spent on beamforming |  | 39 | msec
SLS with
RSS
FB
I-RXSS
BI
BI
Transmit on a single transmit beam
BI
Transmit on the (single) reciprocal beam
Sweep RRX receive beams
Initiator
Responder
Listen on reciprocal beam for feedback and transmit the Ack on the original beam
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-RXSS, SSW-Feedback and SSW-Ack durations + 2×MBIFS | 181 | µs
Beamforming completion time |  | 31 | Beacon Intervals
Total time spent on beamforming |  | 6 | msec
Parameter | Value | Scenario | Unit
Longest data interruption | D = I-RXSS, SSW-Feedback and SSW-Ack durations + 2×MBIFS | 181 | µs
Beamforming completion time |  | 31 | Beacon Intervals
Total time spent on beamforming |  | 6 | msec
SLS with
RSS removed
Keep transmitting on reciprocal beam
Ack
FB
I-RXSS
Ack
Transmit on a single transmit beam
Listen on reciprocal beam for feedback and transmit the Ack on the original beam
FB
ACK
FB
ACK
Listen on reciprocal beams
(RSTX = ISTX)

## Slide 8: Summary
In Distribution Networks even MCS 0 links need directional receive
  ~25 dB SNR gap between MCS 0 and MCS 12 is less than a receive array gain
  New beamforming protocols needed, especially when reciprocity is available
  11ay additions such as appending training fields to Beacon frames are not practical with directional receive
Beamforming protocol proposed in [3] is essentially an SLS with RSS removed and frame transmissions spread out in time to reduce latency

## Slide 9: References
[1] IEEE 802.11-17/1019 “mmWave Mesh Network Usage Model”
[2] IEEE 802.11-17/1321 “Features for mmW Distribution Network Use Case”
[3] IEEE 802.11-17/1679 “Beamforming protocol reuse for mmWave Distribution Networks”
[4] IEEE 802.11-17/1646 “Beamforming for mmWave Distribution Networks”

## Slide 10: Backup

## Slide 11: Asynchronous beamforming
Initiator – synchronized to network timing
  Sweeping total of N Tx beams (e.g., N=31)
  Using the same Tx beam during a beamforming window of N frames (F frame duration)
    Duration per Tx beam N×F, (e.g., 31×400 µs = 12.4 milliseconds)
  Each Tx beam used once during a designated slot in each of the frames 0, …, N-1 within a beamforming window to send multiple TDD SSW packets (typically two)
  Rx Slot 0 in Frame (N-1)/2 of beamforming window W used to receive on the Rx beam that matches the TX beam in beamforming window W-1
Responder – continuously sweeping at the beginning
  Sweeping receive beams continuously back to back, keeping each Rx beam for a programmable “Single Rx beam index duration”
    For example twice the TDD SSW duration + IFS
  Switching from back to back sweeping pattern to slotted (once per “Periodicity”) when first TDD SSW packet successfully received

## Slide 12: Protocol description (1)
Initiator
Beamforming window 1
(Transmit on Tx beam 1)
Beamforming window 30
(Transmit on Tx beam 30)
One complete Tx sector sweep
(384.4 ms)
TDD SSW
TDD SSW
Every Tx slot filled with two or more TDD SSW packets
IFS options (RIFS, SBIFS, SIFS or programmable) under study
 | Receive slots |  |  | Transmit slots |  | 
 |  |  |  | Tx beam 24 |  | 
 | Transmit slots |  |  | Receive slots |  | 
Frame 0 | Tx beam 0 |  |  |  |  | 
Frame 1 | Tx beam 0 |  |  |  |  | 
… | Tx beam 0 |  |  |  |  | 
0 + 15 | Tx beam 0 |  |  | Reserved |  | 
… |  |  |  |  |  | 
0 + 30 | Tx beam 0 * |  |  |  |  | 
31 | Tx beam 1 |  |  |  |  | 
32 | Tx beam 1 |  |  |  |  | 
… |  |  |  |  |  | 
31 + 15 | Tx beam 1 |  |  | Rx beam 0 |  | 
… |  |  |  |  |  | 
31 + 30 | Tx beam 1 * |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
31 x 30 | Tx beam 30 |  |  |  |  | 
931 |  |  |  |  |  | 
… |  |  |  |  |  | 
930 + 15 | Tx beam 30 |  |  | Rx beam 29 |  | 
… |  |  |  |  |  | 
930 + 30 | Tx beam 30 * |  |  |  |  | 
961 | Tx beam 0 |  |  |  |  | 
962 | Tx beam 0 |  |  |  |  | 
… | Tx beam 0 |  |  |  |  | 
961 + 15 | Tx beam 0 |  |  | Rx beam 30 |  | 
… | Tx beam 0 |  |  |  |  | 
961 + 30 | Tx beam 0 ¦30 |  |  |  |  | 
… | Tx beam 1 |  |  |  |  | 
Beamforming window 0
(Transmit on
Tx beam 0)
(12.400 ms)
200 µs
200 µs
Rx beam 0 matching the Tx beam 0 direction
(different AWV in general)
Rx beam 30 matching the Tx beam 30 direction
( different AWV in general)
Responder starts in continuous sweep mode, unaware of the transmit pattern and timing
Assuming there is at least one Tx-Rx beam combination that will close the link, it can be shown that responder will be hit for any phase difference in sweeping if all of the following are true:
Receive “Single Rx beam index duration” (50 µs in this example) counts the transmit periodicity (400 µs in this example)
Number of transmit beams and number of receive beams are the same
Number of beams is a prime number
Responder
0
1
2
3
4
5
6
7
7
8
9
10
11
12
13
14
Responder continuously sweeping Rx beams, camping on each Rx beam for “Single Rx beam index duration”
Responder switches to a slotted Rx beam sweep (following the initiator periodicity) after receiving the first training frame (TDD SSW)
Training frame needs to indicate (1) Initiator offset and transmit period, (2) when responder can send a response if hit with a Tx beam transmission
First Tx/Rx beam hit, switching to slotted sweeping
Sweeping 31 Rx beams
(12.400 ms)
[all 31 Rx beams are scanned every 31 frames in arbitrary order, eg, one way to implement f(k)=mod(x+k*8,30)+1 to make Rx sweep follow the original pattern]
Continued (next slide)
7
Responder sweep start time asynchronous (power ON upon installation)
Tx beam 30/ Rx beam 24 hit happened, offset for response (TDD SSW Feedback) and ack communicated in TDD SSW
x=24
Rx beam f(k=1)
Rx beam f(k+14)
Rx beam f(k+29)
Rx beam f(k+30)
Rx beam f(k+60)|24
Rx beam f(k+45)
TDD SSW
TDD SSW
(Last Tx slot in beamforming window)
Tx slot filled with two or more TDD SSW packets and one or more TDD SSW Ack packets if training response received from responder
IFS options (RIFS, SBIFS, SIFS or programmable) under study
Responder will switch the Rx beam after TDD SSW duration to receive TDD SSW Ack (in case hit with previous beamforming window happened)
TDD SSW Ack (sent using the Tx beam in the previous beamforming window, responder needs to switch the beam to receive TDD SSW Ack)

## Slide 13: Protocol description (2)
Beamforming window
(Transmit on Tx beam 1)
Beamforming window
(Transmit on Tx beam N)
Tx sector sweep continues until stopped by initiator (SME/ administrative)
TDD SSW
TDD SSW
(Last Tx slot in beamforming window)
Tx slot filled with two or more TDD SSW packets and one or more TDD SSW Ack packets
IFS options (RIFS, SBIFS, SIFS or programmable) under study
TDD SSW Ack (sent using the Tx beam in the previous beamforming window, responder needs to switch the beam to receive TDD SSW Ack)
TDD SSW
TDD SSW
Every Tx slot filled with two or more TDD SSW packets
IFS options (RIFS, SBIFS, SIFS or programmable) under study
Initiator
Beamforming window
(Sweeping all Rx beams)
Responder
 | Receive slots |  |  | Transmit slots |  | 
Frame 0 |  |  |  |  |  | 
Frame 1 |  |  |  |  |  | 
… |  |  |  |  |  | 
0 + 15 |  |  |  |  |  | 
… |  |  |  |  |  | 
0 + 30 |  |  |  |  |  | 
31 |  |  |  |  |  | 
32 |  |  |  |  |  | 
… |  |  |  |  |  | 
31 + 15 |  |  |  |  |  | 
… |  |  |  |  |  | 
31 + 30 |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
31 x 30 |  |  |  |  |  | 
931 |  |  |  |  |  | 
… |  |  |  |  |  | 
930 + 15 |  |  |  |  |  | 
… |  |  |  |  |  | 
930 + 30 |  |  |  |  |  | 
… | Management frame receive --- Using best Rx beam to Initiator |  |  | Management frame transmit --- Using best Tx beam to Initiator |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
 | Transmit slots |  |  | Receive slots |  | 
Frame F | Tx beam 0 |  |  |  |  | 
Frame F + 1 | Tx beam 0 |  |  |  |  | 
… | Tx beam 0 |  |  |  |  | 
F + 15 | Tx beam 0 |  |  | Reserved |  | 
… |  |  |  |  |  | 
F + 30 | Tx beam 0 * |  |  |  |  | 
F + 31 | Tx beam 1 |  |  |  |  | 
F + 32 | Tx beam 1 |  |  |  |  | 
… |  |  |  |  |  | 
F + 31 + 15 | Tx beam 1 |  |  | Rx beam 0 |  | 
… |  |  |  |  |  | 
F + 31+ 30 | Tx beam 1¦0 |  |  |  |  | 
… | Tx beam Z |  |  |  |  | 
… |  |  |  |  |  | 
F + 31N | Tx beam N |  |  |  |  | 
F + 31N + 1 |  |  |  |  |  | 
… |  |  |  |  |  | 
… | Tx beam N |  |  | Rx beam 29 |  | 
… |  |  |  |  |  | 
F + 31N +30 |  |  |  |  |  | 
… | Management frame transmit --- Using best Tx beam to Responder |  |  | Management frame receive --- Using best Rx beam to Responder |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
… |  |  |  |  |  | 
Beamforming window
(Transmit on
Tx beam 0)
(12.400 ms)
Beamforming window
(Sweeping all Rx beams)
(12.400 ms)
200 µs
200 µs
Rx beam 0 matching the Tx beam 0 direction
(different AWV in general)
Responder switches the sweeping mode to slotted, synchronized with initiator
End of training is administrative (decided by Initiator SME)
At the end of training, full list of Tx-Rx beams in both directions, and other configuration parameters are exchanged using management frames, and using the same slots that were used for beamforming
200 µs
200 µs
All request and ack frames indicate end of training
End of beamforming; full beam list (route) and other configuration parameters exchange, all using management frames, and using the same slots that were used for beamforming
Tx beam matching the direction of the Rx beam that was hit, if any (different AWV in general)
Rx beam f(k)
Rx beam f(g+30)|f(l)
Rx beam f(k+30)
Rx beam f(k+45)
Rx beam f(k+75)|f(k+15)
Rx beam f(k+60)
Rx beam f(l)
Rx beam f(k+15)
Tx beam f(k+15)
Tx beam f(l)
Rx beam f(g)
Tx beam matching the direction of the Rx beam that was hit, if any (different AWV in general)
Tx beam N|Z
Tx beam 0/ Rx beam f(k+15)
hit happened, offset for response and ack communicated in TDD SSW
Responder will switch the Rx beam after TDD SSW duration to receive urTrnResAck
Tx beam Z/ Rx beam f(l)
hit happened, offset for response and ack communicated in TDD SSW