## Slide 1: Extending WUR sync sequence
Date: 2017-12-08
Authors:

## Slide 2: Abstract
Increasing number of WUR frame types is a potential power drain to simple and very low power devices that are interested in only a small fraction of the frames
This presentation discusses the possibility to extend the sync sequence of the WUR frame to support design and operation of simple devices

## Slide 3: Motivation
The motivation of having WUR is to save power as much as possible
Detecting a frame from the sync sequence (running a correlator) may consume less power than receiving and decoding a WUR payload
All the WUR receivers are not supposed to wake up their PCR from all the WUR frames
  With various WUR frame types, such as beacons, discovery frames and wake-up frames, it may even be that most of the WUR frames are not in interest of some WUR devices
  In dense deployments, several beacons and discovery frames per second can be imagined and this could become a challenge if a few dedicated WUR channels are specified

## Slide 4: Current view on the WUR sync sequence
WUR sync sequence is used by receiver for:
  frame detection,
  synchronization, and
  signaling MCS
It seems that the 802.11ba group is heading to have 2 sync sequences (one for each MCS) [1]
If the WUR receiver does not detect correct kind of signature, it ignores the frame
  This may be also due to that the WUR receiver does not support the MCS of the frame, meaning that it only tries to detect one of the sequences

## Slide 5: Extending the signature sequences
From power consumption perspective, it would be desirable to have means to identify as early as possible and as low in the stack as possible whether the WUR frame is relevant for the device
  This could be achieved by including some extra information to the sync sequence
  This extra information could be frame type (or even partial WID in some form, some kind of color code of the WUF or a paging group)
Could the signature signal include this extra information in addition to the used MCS?
  This would mean that there could be e.g. 4 or 8 sync sequences instead of 2
This might make the sync sequence longer in time
  The length of the WUF could still be the same

## Slide 6: Summary
Increasing number of WUR frame types is a potential power drain to simple and very low power STAs that are interested in only a small fraction of the frames
Filtering out most of the WUR frames already in frame detection phase would save power in such STAs
Extending the sync sequence is a way to do it

## Slide 7: References
[1] 11-17-0575-06-00ba-spec-framework