## Slide 1: Pre-association Security Negotiation for 11az SFD Follow up
1
Date: 2017-12-14
Authors:
Name | Affiliations | Address | Phone | email
Nehru Bhandaru | Broadcom Ltd. | 250 Innovation Drive San Jose, CA 95134 | +1 408-922-5924 | nehru.bhandaru@broadcom.com
Matthew Fischer | Broadcom Ltd. | 250 Innovation Drive San Jose, CA 95134 | +1 408-543-3370 | matthew.fischer@broadcom.com
Jonathan Segev | Intel |  |  | Jonathan.segev@intel.com
Chittabrata Ghosh | Intel |  |  | 
Benny Abramovsky | Intel |  |  | 
Ido Ouzieli | Intel |  |  | 

## Slide 2: Introduction
TGaz FRD 16/0424r7 - r38 – Requires support for PASN
  One secured mode that provides Authentication, Key Management, Encryption and Message Integrity in unassociated state
TGaz SFD 11-17/0462r5
  Security setup optional, but prior to 11az Protocol Negotiation
  Out of band keys may be used
  Fields over which range measurements are performed are protected
TGaz 11/1737r0 outlines the proposed SFD text
  Contained straw poll(s) for possible SFD text
This submission
  Few discussion items
  Update based on additional feedback
  Consolidated motion to be considered
2

## Slide 3: Straw poll results during IEEE Nov 2017 meeting
Straw poll #0:
Add to SFD Security section:
“PASN Authentication
PASN authentication allows message authentication, encryption, and message integrity to be provided for selected 802.11 frames that require such protection. Whether such protection is required for a frame is determined by the security parameters negotiated for the exchange (e.g. 11az Protocol Negotiation) to which the frame belongs.”
Results: Y: 22, N: 0, A: 6
3

## Slide 4: Straw poll results during IEEE Nov 2017 meeting
Straw poll #1:
Add to SFD PASN Authentication section: “An AP indicates PASN support by advertising a TBD PASN AKM in RSNIE that is included in some of the Beacons and in Probe Responses, and also in neighbor reports and reduced neighbor reports where supported. A non-AP STA selects use of PASN authentication based on the security requirements of features that need pre-association security. 11az protocol security for an un-associated STA requires PASN.”
Results: Y: 20, N: 0, A: 4
4

## Slide 5: Strawpoll results during IEEE Nov 2017 meeting
Straw poll #2:
Add to SFD PASN Authentication section: “A non-AP STA and an AP use 802.11 authentication frames with the Authentication algorithm number set to TBD (PASN Authentication) for the protocol exchange.”
Results: Y:18, N:0, A: 6
5

## Slide 6: Straw poll results during IEEE Nov 2017 meeting
Straw poll #3: Add to SFD PASN Authentication section:
“A non-AP STA optionally, via PASN protocol, proposes to an AP a base AKM and PMKID(s) used to identify the PMK used for derivation of PTK for key confirmation and frame protection. An AP optionally, via PASN protocol, indicates to the non-AP STA, a base AKM and PMKID corresponding to the PMK used for derivation of PTK for key confirmation and frame protection.
A non-AP STA and AP exchange ephemeral public keys to derive protection keys via PASN. The PTK for the exchange is derived from PMK, if any, and the shared secret from the ephemeral key exchange.”
Results: Y: 18, N: 0, A: 4.
6

## Slide 7: Straw poll results during IEEE Nov 2017 meeting
Straw poll #4:
Add to SFD Security section: “802.11az protocol negotiation and measurement reports shall be integrity protected and optionally encrypted for privacy.
Results: Y: 22, N: 0, A: 1.
7

## Slide 8: Discussion Items
Use of E911/11u Mechanisms to generate pre-association keys
  E911 mechanisms for RSN described in Annex R5/R5.3/R5.3 of [1]
  Either Open association or Uses 11u Interworking Element
  802.1x port protection is bypassed, “cryptographic keys are not exchanged”
  Feedback
    Feedback during Nov meeting may be about need to provide E911 bypass for 11az security
      That would be addressed by 11az negotiation; PASN is about establishing security association if required.
    Is this about 11az E911 requirements
      No. If there are any requirements they are to be addressed separately
8

## Slide 9: Discussion Items
Should privacy be optional for measurement reports
  Optional privacy requires non-PMF mechanism
  Suggest LMRs requiring both integrity and privacy
9

## Slide 10: Discussion Items
What Base AKMs do we need to support
  Can we just mandate a subset?
    Just FILS?
    FILS shared key + FT (using PMKr1)
    PSK modes less useful for pre-association security
  Feedback
    Base AKMs – why only FILS and FT
      FILS fastest, gaining traction and is likely to be adopted by the time 11az is available. One message exchange to setup SA
      FT already in market – PMKr0 SA already exists, leverage PMKr1 without additional negotiation
      Perhaps FILS + Any other AKM w/ PMK (including PSK modes)
10

## Slide 11: Motion
Move to adopt the following text in the TGaz SFD under Section 6 – Security - and grant the SFD editor editorial license:
Pre-association Security Negotiation (PASN) authentication allows message authentication, encryption, and message integrity to be provided for selected 802.11 frames that require such protection.
Whether such protection is required for a frame is determined by the security parameters negotiated for the exchange (e.g. 11az Protocol Negotiation) to which the frame belongs.
An AP indicates PASN support by advertising a [TBD] PASN AKM in RSNIE that is included in some or all of the Beacons and in Probe Responses, and also in neighbor reports and reduced neighbor reports where supported.
A non-AP STA selects use of PASN authentication based on the security requirements of features that need pre-association security. 11az protocol security for an un-associated STA requires PASN.
11

## Slide 12: Motion – Contd..
A non-AP STA and an AP use 802.11 authentication frames with the Authentication algorithm number set to [TBD] (PASN Authentication) for the protocol exchange.
A non-AP STA optionally, via PASN protocol, proposes to an AP a base AKM and PMKID(s) used to identify the PMK used for derivation of PTK for key confirmation and frame protection.
An AP optionally, via PASN protocol, indicates to the non-AP STA, a base AKM and PMKID corresponding to the PMK used for derivation of PTK for key confirmation and frame protection.
PASN protocol allows a FILS base AKM using shared key (See 12.12.2.3 of [1])
PASN protocol allows any base protocol with a PMK – e.g. FT base AKM using PMKr1
12

## Slide 13: Motion – Contd..
A non-AP STA and AP exchange ephemeral public keys to derive protection keys via PASN.
The PTK for the exchange is derived from PMK, if any, and the shared secret from the ephemeral key exchange.
If 11az measurement security for type A or a type B attackers is required, the IEEE 802.11az negotiation protocol and measurement reports shall be integrity protected and encrypted for privacy.
If 11az measurement security for type B attacker is required, the fields over which measurements are performed shall be protected (e.g. LTF sequence derived using the keys from PASN protocol).
Moved:
Seconded:
Results:
13

## Slide 14: References
IEEE P802.11-REVmdTM/D0.3, September 2017
11-15-0030-09-0ngp-ngp-par-draft
11-15-0262-04-0ngp-csd-working-draft
11-16-0137-00-00az-ngp-use-case-document
11-16-0424-07-00az-functional-requirements-for-11az
11-17-1127-01-00az-comments-on-11az-functional-requirements
11-16/1643-00-00az-preassociation-negotiation-of-management-frame-protection
11-17/1737r0 - Pre-association Security Negotiation for 11az
Slide 14