## Slide 1: BQRP BQR LCTS DL MU
Date: 2017-12-04
Authors:

## Slide 2: Abstract
To improve efficiency
Establish the sequence:
  BQRP (a Trigger for BQR, or generally, any Trigger)
  HE TB BQR (i.e. elicited HE TB PPDU response)
  Non-HT CTS and/or non-HT DUP CTS (TX by non-AP STA)
    Optional overlapping CTS2SELF transmitted by the AP
  DL MU PPDU
  BA
Insertion of a command bit within the Trigger
  New POLL-CTS subfield which is used to elicit non-HT CTS SIFS after the elicited HE TB PPDU
Also consider ER implications

## Slide 3: CID 13827
13827 | Yasuhiko Inoue | 243.27 | 27.5.2 | "A STA may send BQRs to an AP to assist DL MU and UL MU resource allocation in an efficient way." This text is ambiguous compared to the other sentence in this subclause. | Improve the text, e.g., "A non-AP HE STA may send BQRs to the AP with which it is associated to assist DL MU and UL MU resource allocation in an efficient way." | Revise – Tgax editor to include L-CTS transmission option within BQR sequence by implementing the changes shown in 11-18/0056r0

## Slide 4: CID 14328
14328 | Zhou Lan | 226.30 | 27.2.5.2 | MU-RTS procedure doesn't provide sufficient support for range extension mode operation. A near edge STA after receive MU-RTS frame from AP may not be able to succesfully deliever CTS back to AP. As a consequence AP cannot use ER SU PPDU for DL transmission to the near edge STA. Need to enhance the MU-RTS/CTS operation to enable ER SU PPDU transmission. | as in the comment | Revise – Tgax editor to include L-CTS transmission option within trigger sequence by implementing the changes shown in 11-18/0056r0

## Slide 5: CID 12593
12593 | Mark RISON | 324.48 | 27.16.5 | ER beacons don't work for the same reason they didn't work with STBC (and got obsoleted): the AP typically has higher tx power so the AP can reach STAs but STAs can't reach the AP. The slight advantage conferred by the ability of the STA to use 10 MHz transmissions is not sufficient to overcome this | Delete Subclause 27.16.5 | Revise – Tgax editor to include L-CTS transmission option within ER sequence by implementing the changes shown in 11-18/0056r0

## Slide 6: Comments on the CIDs
The CIDs touch on several issues
  Efficiency of BQR-BQRP
    Especially when Legacy Protection is desired
  ER operation
    AP vs non-AP STA TX power mismatch
      Implications regarding normal operation
      Implications regarding legacy protection

## Slide 7: Comments on the CIDs
Power difference between AP and non-AP STA can largely be covered by TGax features
  Narrow RUs extend to 2.2 MHz, i.e. 9 dB gain
  ER PPDU = 3 dB
  Total 12 dB gain (excluding preamble consideration)
Problem of NAV coverage for reception at non-AP STA locations persists
Propose non-HT CTS transmission by non-AP STAs
  Propose mechanism for AP to direct the CTS transmissions so that both parties are aware of the timing
  Require preceding sequence to establish medium control
    E.g. BQRP, BQR

## Slide 8: Existing Situation
ER mode and narrow RUs allow communications with non-AP STA that are at extended range
UL PPDU are protected by protection established at the AP
DL PPDU need protection to be established by DL recipients
  i.e. non-AP STAs need to establish protection
  Normally, this protection is established through an RTS-CTS exchange

## Slide 9: Normal Recipient Protection
CTS transmitted by DATA PPDU recipient protects recipient during DL PPDU reception
AP_B
STA_B1
AP_G
RTS
STA_G1
CTS
CTS

## Slide 10: DL HE MU PPDU Needs Protection
Trigger protects AP, no one protects DL PPDU recipients
Non-HT Trigger BQRP
HE TB PPDU BQR
HE TB PPDU BQR
HE TB PPDU BQR
Un-protected DL HE MU PPDU
HE TB PPDU cannot provide protection for next DL PPDU from non-HE STA
HE TB PPDU BA
HE TB PPDU BA
HE TB PPDU BA
Un-protected DL PPDU !

## Slide 11: MU-RTS to Protect DL HE MU PPDU
Using MU-RTS, this only works for non-ER STA!
HT Trigger BQRP
HE TB PPDU BQR
HE TB PPDU BQR
HE TB PPDU BQR
Un-protected DL HE MU PPDU
Non-HT CTS protects next DL PPDU from non-HE STA
HE TB PPDU BA
HE TB PPDU BA
HE TB PPDU BA
Protected DL PPDU !
Non-HT CTS
Non-HT CTS
Non-HT CTS
BQRP Trigger includes signaling bit to elicit CTS
Non-HT Trigger MU-RTS
Non-HT CTS transmitted by ER STA not heard by AP, so the sequence FAILS

## Slide 12: More efficient and fixes ER problem
AP indicates use of L-CTS to protect DL PPDU
Non-HT Trigger BQRP
HE TB PPDU BQR
HE TB PPDU BQR
HE TB PPDU BQR
Un-protected DL HE MU PPDU
Non-HT CTS protects the DL HE MU PPDU from non-HE STA interference
HE TB PPDU BA
HE TB PPDU BA
HE TB PPDU BA
Protected DL PPDU !
Non-HT CTS
Non-HT CTS
Non-HT CTS
Trigger includes signaling bit to elicit CTS
HE TB response confirms the TXOP

## Slide 13: PHY Parameters of LCTS
LCTS is meant to protect the DL PPDU reception at the non-AP STA (i.e. recipient location)
  TX Power of LCTS should be at normal (max) TX power to allow maximum protection
    i.e. do not send LCTS at a TX power which is adjust for the Target RSSI as indicated in the Trigger frame
      The LCTS is not intended for the AP
      BQRP response confirms the TXOP is established, LCTS is for protection at LCTS transmitter location
  Other parameters, e.g. MCS, are determined by normal MU-RTS response (see 27.2.5.3 CTS Response to MU-RTS)
    E.g. Rate = 6 Mbps

## Slide 14: ER Hidden LCTS
When all users are ER, it is possible that the AP does not hear any of the LCTS that are transmitted
  Need allowance for AP to proceed in case when LCTS is not heard
  I.e. if AP sets POLL-CTS bit in a Trigger frame, then
    If AP receives HE TB PPDU, it waits for SIFS + LCTS + SIFS and then proceeds with TXOP sequence, regardless of whether it heard LCTS or not
    See other possible options in 11-18/0030r0, which discusses this concept in the context of the existing MU-RTS exchange

## Slide 15: Failed Trigger Response
In the case when the HE TB PPDU response to the initial Trigger is not heard by the AP
  AP must wait for a timeout of:
  SIFS + HE TB PPDU Duration + SIFS + LCTS + SIFS + aRxPHYStartDelay
  To avoid colliding with an LCTS on retry

## Slide 16: POLL-CTS Subfield Location (1)
Change B63 Reserved of Common Info field to POLL-CTS
  When POLL-CTS == 1, recipient transmits LCTS SIFS after transmission of elicited HE TB PPDU

## Slide 17: POLL-CTS Subfield Location (2)
Change B39 Reserved of User Info field to POLL-CTS
  When POLL-CTS == 1, recipient transmits LCTS SIFS after transmission of elicited HE TB PPDU

## Slide 18: MU-RTS Trigger
MU-RTS Trigger already elicits LCTS
POLL-CTS subfield for MU-RTS shall always be 0

## Slide 19: Straw poll #1
Do you support the addition of a new subfield POLL-CTS to be added to the Common|User Info field of the Trigger frame and the addition of AP behavior rules and non-AP STA rules to accompany the subfield which elicits a non-HT CTS that is transmitted SIFS after the HE TB PPDU elicited by the Trigger?
  Y
  N
  A

## Slide 20: References
[1] 802.11-2016.pdf
[2] Draft P802.11ax_D2.0.pdf
[3] 11-18-0056-00-00ax-CR-CID-14328.docx
[4] 11-18-0030-00-00ax-ER-DL-protection-sequence.pptx