## Slide 1: MIB TruthValue Usage Patterns Presentation
Date: 2018-01-15
Authors:

## Slide 2: Abstract
This presentation provides an overview of 11-15/0355r13 (note the year!), to aid the 802.11 Working Group in understanding the proposals in that document.
11-15/0355 makes a number of proposals for a common and consistent pattern of use for MIB attributes in 802.11, of type “TruthValue”. It is proposed that these usage patterns be adopted by the Working Group for future amendments, and incorporated in the MDR process.
11-15/0355 is presented on behalf of the 802.11 ARC SC.

## Slide 3: Why do I care what is in the MIB?
Most vendors do not implement the MIB, literally. Instead, a proprietary method of device/system management is provided, with similar (and probably subset) function.
HOWEVER, …
The MIB is used as a reference within 802.11 activities, and by other standards organizations, to help understand the behavior intention of the Standard.

## Slide 4: What’s the big deal about consistency?
Example 1: dot11QBSSLoadImplemented
  A test: what does this attribute mean?
  You probably all got this correct
  Answer:
    This attribute, when true, indicates that the AP implementation is capable of generating and transmitting the BSS load element in the Beacon and Probe Response frames. The capability is disabled, otherwise.

## Slide 5: What’s the big deal about consistency?
Example 2: dot11TxSTBCOptionImplemented
  Next test: what does this attribute mean?
  Answer:
    This attribute, when true, indicates that the entity is capable of transmitting frames using STBC option.
  Seems okay, right?
dot11TxSTBCOptionActivated:
    This attribute, when true, indicates that the entity is capable of transmitting frames using STBC option.
  So, reading “when dot11TxSTBCOptionImplemented is true” would probably lead you to a bad assumption that STBC was actually being used (was also Activated).
OK, that’s a potential for confusion…
Is it “Implemented” or “Activated” that matters, each time?

## Slide 6: What’s the big deal about consistency?
Example 3: dot11RSNAConfigPairwiseCipherImplemented
  Next test: what does this attribute mean?
  Answer:
    This is an OCTETSTRING.
    This attribute is the selector of a supported pairwise cipher. It consists of an OUI or CID (the first 3 octets) and a cipher suite identifier (the last octet).
  Ugh, this is getting messy …

## Slide 7: What’s the big deal about consistency?
Example 4: dot11AssociateInNQBSS
  Next test: what does this attribute mean?
  Answer:
    This attribute, when true, indicates that the station may associate in a non-QoS BSS. When false, this attribute indicates that the station does not associate in a non-QoS BSS.
  So, some don’t have “Implemented” or “Activated” at all …

## Slide 8: What’s the big deal about consistency?
Example 5: dot11SpectrumManagementRequired
What does that mean – “Required”??
  Answer:
    A STA uses the defined TPC and DFS procedures if this attribute is true; otherwise it does not use the defined TPC and DFS procedures.
  Oh, okay, so it is really “Activated”!
  So, some attributes don’t have “Implemented” or “Activated” at all …
  (But, it turns out this one is even messier…)

## Slide 9: What’s the big deal about consistency?
Consistency means everyone reading the Standard can learn some simple patterns of use, and assume the correct pattern applies when reading the text.
Lack of consistency means we all get confused at times about what a reference means, and we end up searching through the Standard’s text or the MIB to make sure we guessed right this time.
Waste of time …
Leads to errors and confusion …

## Slide 10: What do we care about, in the patterns of use?
First, let’s limit the discussion to attributes of type “TruthValue”. These are ‘true’ or ‘false’ items.
Then, consider the following:
  Is it ‘hard-coded’, like a capability of the implementation?
  Or, can it be switched on and off, and if so when and what happens at the transitions?
  Some (like dot11SpectrumManagementRequired) are dictated by a ‘primary’ device, and have to be enabled (or learned) by a ‘secondary’ device to enable interoperation.
  And, for the above, can the primary change the state? If so, when, and what happens?
  Or, some that can be switched on and off don’t get signaled, but just enable local behavior, such a policy rules.
  Finally, some just don’t need to be in the MIB at all, and were meant as a “short-hand” for saying the device is capable of, or has enabled, some specific behavior. But the “short-hand” resulted in 20 lines of definition for what could be said in a few words.

## Slide 11: Define patterns for each of those
For each of the types of use described on the previous slide, choose a descriptive suffix that helps recall the pattern, and be consistent in the use. For example:
  “Implemented” – for a static capability
  “Activated” – when it can be switched on and off
  “Required” – when a primary dictates the behavior to a secondary
  “Directed” – when a primary tells the secondary what to do, and can change those instructions over time
  “PolicyActive” – for things that are purely local behavior depending on the on/off setting

## Slide 12: Guidance on how to choose, what to do
Document 11-17/0355r13 provides:
A description of each pattern, and when it applies
A format to use for the MIB attribution definition for that pattern, including the ‘suffix’ to use
An example of an attribute in 802.11-2016 that fits the pattern, and how it would appear.

## Slide 13: Recommendations
Use these patterns for all TruthValue MIB attributes
  Start using the patterns in all new work (new amendments)
  Consider whether to update existing attributes and use to match the patterns (REVmd)
Remove MIB attributes with inefficient “short-hand”, and replace with in-line text
The attribute name suffixes defined in 11-15/0355r13 should only be used for TruthValue MIB attributes. Other types of MIB attributes should use different name suffixes.

## Slide 14: Follow-on
Look at the “changes text effect” language in the MIB, especially “changes take effect at the next MLME-START [or MLME-JOIN].” We suspect there are a lot of cut-and-paste errors, and other inconsistency in this language as well.
Look at attributes of other types, beyond ‘TruthValue’, for other consistency problems – but only if they lead to real-world confusion or misunderstanding of the Standard. Let’s not waste our time…

## Slide 15: For today
Please review the document
Motion for Friday:
  Request the 802.11 Working Group approves the use of 11-15/0355r13 as part of the Mandatory Draft Review process.

## Slide 16: References
11-09/0427r1 – ARC MIB recommendations
11-09/0533r1 – Recommendation re MIB types and usage
11-14/1068r0 – MIB Attributes Design Pattern background
11-14/1281r4 – MIB Attributes Analysis
11-15/0355r13 – MIB TruthValue usage patterns
11-17/0475r9 – MIB pattern analysis