## Slide 1: WUR Dual SYNC Design Follow-up: SYNC bit Duration
Date: 2018-01-14
Authors:

## Slide 2: Introduction
In IEEE November meeting, long-short dual SYNC design structure is agreed [1, 2] with
  250kbps uses 64us SYNC
  62.5kbps uses 128us SYNC
The SYNC sequence and each SYNC bit duration is not decided
In this contribution, we evaluate the impact of SYNC bit duration.

## Slide 3: Recap: Long-short Dual SYNC Design
Dual sequence design
  Design one base sequence S of length N (sequence of 1s and 0s).
  High-rate (250kbps) uses complementary [1-S] of duration 64us
  Low-rate (62.5kbps) uses [S S] of duration 128us
For the same duration, WUR SYNC can use different combinations of bit duration and sequence length, for example:
  4us with 16 bit S sequence
    shorter S sequence may save receiver local correlator template storage
  2us with 32 bit S sequence
    twice longer S sequence can provide better correlation properties: higher peak-to-sidelobe ratio and faster correlation peak roll-off.
    Provide better carrier sensing/timing performance, and potentially easier receiver tuning: large range of good SYNC detection ratio

## Slide 4: Examples of SYNC Sequences
Only consider SYNC bit duration of 2us and 4us:
  WUR OOK modulation already has “ON” waveform definition of both for Manchester coding
  No need to redefine “ON” waveform for these two durations
Sequence design criteria: good correlation property
  S is designed from an M-sequence of length N-1.
  Add one extra 1 or 0 to achieve zero DC receiver correlator template and good cross-correlation and auto-correlation properties [3].
Two examples:
  N= 32 and 2us bit duration
    Z = [1 0 1 1 1 0 0 0 1 0 1 0 1 1 0 1 0 0 0 0 1 1 0 0 1 0 0 1 0 1 1 1];
  N= 16 and 4us bit duration
    Z = [0 1 1 1 0 0 0 1 0 0 1 1 0 1 0 1];

## Slide 5: Simulation Settings
WUR Packet
  WUR Data signal uses center ~4MHz in 20MHz bandwidth
  Payload: 48 bits, Manchester Coding
  2ms noise appended before the WUR packet
SNR defined on 20MHz noise
CFO = 20ppm, fc = 2.4GHz, No phase noise
Receiver
  Realistic AGC: entire packet is normalized to certain gain target
    Noise portion normalized based on the noise power
    WUR portion normalized by 20MHz preamble power
  3th order 4MHz butterworth filter with 2.5MHz cutoff frequency
  4MHz sampling rate with in-phase path
  CS detection threshold is chosen to have <1% Pfalse rate
LSTF
LLTF
LSIG
WUR SYNC
WUR Data
BPSK
Symbol
2ms noise

## Slide 6: Channel: AWGN
  62.5kbps: 2us SYNC has slightly better performance than 4us SYNC
  250kbps: 2us SYNC is ~1.6dB better than 4us SYNC

## Slide 7: Channel: DNLOS
  62.5kbps: 2us SYNC has slightly better performance than 4us SYNC
  250kbps: 2us SYNC is ~0.8dB better than 4us SYNC

## Slide 8: Channel: UMi-NLos
  62.5kbps: 2us SYNC has slightly worse performance than 4us SYNC
  250kbps: 2us SYNC has slightly higher error floor, due to long delay spread

## Slide 9: Sensitivity Comparison
 | AWGN |  |  |  |  | 
 | 62.5kbps |  |  | 250kbps |  | 
 | Pmiss | PER | delta | Pmiss | PER | delta
4us | -5.4 dB | -5.2 dB | 0.2 dB | -2.7 dB | 2.4 dB | 5.1 dB
2us | -5.6 dB | -5.3 dB | 0.3 dB | -3.4 dB | 0.8 dB | 2.6 dB
 | 62.5kbps |  |  | 250kbps |  | 
 | Pmiss | PER | delta | Pmiss | PER | delta
4us | -0.6 dB | -0.3 dB | 0.3 dB | 2.5 dB | 6.2 dB | 3.7 dB
2us | -1.4 dB | -1.0 dB | 0.4 dB | 1.5 dB | 5.0 dB | 3.5 dB
 | UMi-Nlos |  |  |  |  | 
 | 62.5kbps |  |  | 250kbps |  | 
 | Pmiss | PER | delta | Pmiss | PER | delta
4us | -1.7 dB | -1.6 dB | 0.1 dB | 1.8 dB | x | x
2us | -1.6 dB | -1.3 dB | 0.3 dB | 1.4 dB | x | x

## Slide 10: Discussion
SYNC bit duration of 2us shows some performance advantage over 4us SYNC
  The SNR gain of SYNC bit duration of 2us will depend on multiple receiver design parameters: receiver analog design (low-pass filter, AGC, and etc.), receiver sampling rate, SYNC detection threshold setting, DATA OOK detection algorithm and etc.
  SYNC bit duration of 2us enables the possibility for receiver to achieve better sensitivity
The sensitivity gain is accompanied by additional power consumption at low SNR. For example,
  SNR<-5dB, the high-rate PER is close to 1, better CS detection (smaller Pmiss) of 2us design will induce more receiver data decoding trials, resulting in slightly higher power consumption
  This wrong packet length detection can also cause CCA issues, if a different length design option is allowed on the MAC side

## Slide 11: Straw Poll 1
Do you agree that duration of each 11ba SYNC bit to be 2us and the base sequence S of length 32?
  Y:
  N:
  A:

## Slide 12: Reference
[1] IEEE 802.11-17/1781r1, “SYNC Structure Motions”
[2] IEEE 802.11-17/1618r1, “Dual SYNC Design and Performance.”
[3] IEEE 802.11-17/1343r0, “WUR preamble SYNC design and performance”