## Slide 1: Computation of TSF Update
Date: 2018-01-14
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Daniel F Bravo |  |  |  | 
Noam Ginsburg |  |  |  | 
Robert Stacey |  |  |  | 

## Slide 2: Abstract
We have agreed to put partial TSF in WUR Beacon [1], and there are two remaining TBDs
  Bit location of the partial TSF
  Computation of partial TSF when sending the WUR Beacon and computation of TSF when receiving the WUR Beacon
We discuss the second TBD in this presentation

## Slide 3: History of Carrying Partial TSF for 802.11
Carrying partial TSF in a Beacon frame is not new, and 11ah has already adopted similar ideas, where 4 bytes LSBs are carried in the SIG Beacon
Spec texts for the transmitter of S1G Beacon:
  The Timestamp field contains the 4 least significant octets of the transmitting STA’s TSF timer at the time that the start of the data symbol, containing the first bit of the Timestamp, is transmitted by the PHY plus the transmitting STA’s delays through its local PHY from the MAC-PHY interface to its interface with the WM.
Spec texts for the receiver of S1G Beacon:
  An S1G STA that receives an S1G Beacon frame shall update its TSF timer according to the algorithm described in 11.1.3.10.3.

## Slide 4: History of Carrying Partial TSF for 802.11
Spec texts of 11.1.3.10.3:
  The received Timestamp value shall be adjusted by adding an amount equal to the receiving STA’s delay through its local PHY components plus the time since the first bit of the Timestamp field was received at the MAC/PHY interface.
  If the received S1G Beacon frame does not include an S1G Beacon Compatibility element:
    If the most significant bit (MSB) of the adjusted value of the received Timestamp is not equal to the MSB of the 4 least significant octets of the local TSF timer then the value of the 4 most significant octets of the TSF timer shall be adjusted to account for roll over as follows: — The value shall be increased by one unit (modulo 2^32) if LT > AT and LT > AT + 2^31 — The value shall be decreased by one unit (modulo 2^32) if LT < AT and LT < AT – 2^31 where AT is the adjusted value of the received Timestamp and LT is the value of the 4 least significant octets of the local TSF timer
    The 4 least significant octets of the STA’s local TSF timer shall be set to the adjusted value of the Timestamp.
  If the received S1G Beacon frame includes an S1G Beacon Compatibility element:
    The 4 least significant octets of the STA’s TSF timer shall then be set to the adjusted value of the Timestamp.
    If the most significant bit of the adjusted value of the Timestamp is 0 and the value of the TSF Rollover Flag field in the S1G Beacon Compatibility element is 1, then the 4 most significant octets of the TSF timer shall be adjusted to account for roll over (i.e., the value obtained from the TSF Completion field shall be increased by one unit (modulo 2^32). Otherwise, the 4 most significant octets of the TSF timer shall be set to the value of the TSF Completion field in the S1G Beacon Compatibility element.
WUR Beacon does not have space for Beacon Compatibility element. Hence, we only consider the second bullet

## Slide 5: Proposed Texts for 11ba
Transmitter of WUR Beacon:
  The Partial TSF field contains the bits X to X+11 of the transmitting STA’s TSF timer at the time that the start of the data symbol, containing the first bit of the Partial TSF field, is transmitted by the PHY plus the transmitting STA’s delays through its local PHY from the MAC-PHY interface to its interface with the WM.

## Slide 6: Proposed Texts for 11ba
For a WUR non-AP STA that receives a WUR Beacon carrying partial TSF with bit position X to X+11 of the TSF, the algorithm to adjust local TSF is:
  The received partial TSF value shall be adjusted by the following
    Create temporal timestamp by concatenating received partial TSF with X bits containing an implementation specific value that represents the assumed value of bit position 0 to X-1 of the temporal timestamp
    Add an amount equal to the receiving STA’s delay through its local PHY components plus the time since the first bit of the Partial TSF field was received at the MAC/PHY interface to the temporal timestamp
    The adjusted value of the received partial TSF is set as the value of bit position X to X+11 of the temporal timestamp
  If the most significant bit (MSB) of the adjusted value of the received partial TSF is not equal to the bit Y of the local TSF timer then the value of bits X+12 to 63 of the local TSF timer shall be adjusted to account for roll over as follows:
    The value shall be increased by one unit (modulo 2^(52-X)) if LT[X:X+11] > AT and LT[X:X+11] > AT + 2^(11)
    The value shall be decreased by one unit (modulo 2^(52-X)) if LT[X:X+11] < AT and LT[X:X+11] < AT – 2^(11)
where AT is the adjusted value of the received partial TSF and LT[X:X+11] is the value of bits X to X+11 of the local TSF timer
  The bits X to X+11 of the STA’s local TSF timer shall be set to the adjusted value of the received partial TSF.

## Slide 7: Conclusion
We suggest the text to compute the partial TSF carried in the WUR Beacon and to update the local TSF when
  For the transmitter of WUR Beacon
  For the receiver of WUR Beacon

## Slide 8: Straw Poll #1
Do you support the following?
For the transmitter of WUR Beacon:
  The Partial TSF field contains the bits X to X+11 of the transmitting STA’s TSF timer at the time that the start of the data symbol, containing the first bit of Partial TSF field, is transmitted by the PHY plus the transmitting STA’s delays through its local PHY from the MAC-PHY interface to its interface with the WM.
Note that X is TBD

## Slide 9: Straw Poll #2
Do you support the following?
For a WUR non-AP STA that receives a WUR Beacon carrying partial TSF with bit position X to X+11 of the TSF, the received partial TSF is adjusted to consider STA’s delay as shown below
  Create temporal timestamp by concatenating received partial TSF with X bits containing an implementation specific value that represents the assumed value of bit position 0 to X-1 of temporal timestamp
  Add an amount equal to the receiving STA’s delay through its local PHY components plus the time since the first bit of the Partial TSF field was received at the MAC/PHY interface to the temporal timer
  The adjusted value of the received partial TSF is set as the value of bit position X to X+11 of the temporal timestamp
Note that X is TBD

## Slide 10: Straw Poll #3
Do you support the following?
For a WUR non-AP STA that receives a WUR Beacon carrying partial TSF with bit position X to X+11 of the TSF,
  If the most significant bit (MSB) of the adjusted value of the received partial TSF is not equal to the bit Y of the local TSF timer then the value of bits X+12 to 63 of the local TSF timer shall be adjusted to account for roll over as follows:
    The value shall be increased by one unit (modulo 2^(52-X)) if LT[X:X+11] > AT and LT[X:X+11] > AT + 2^(11)
    The value shall be decreased by one unit (modulo 2^(52-X)) if LT[X:X+11] < AT and LT[X:X+11] < AT – 2^(11)
where AT is the adjusted value of the received partial TSF and LT[X:X+11] is the value of bits X to X+11 of the local TSF timer
  The bits X to X+11 of the STA’s local TSF timer shall be set to the adjusted value of the received partial TSF.
Note that X is TBD

## Slide 11: Reference
[1] 11-17-0575-08 Spec Framework