## Slide 1: Fixing TBDs in WUR frames
Date: 2018-01-08
Authors:

## Slide 2: Introduction
The general WUR frame format was defined in [1-6]:
With good progress on many of the structure/functionality details:
  Length of the MAC Header is fixed,
  Frame Control field contains a Type subfield, etc.
In this presentation we follow up on some of the TBDs
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | 8 | 12 | 12

## Slide 3: Frame Control
The Frame Control field has Type (size TBD) and Length/Misc field (size TBD)
We focus in determining the size of Length field and its unit for VL WUR frames
  Currently, the length is in units of TBD octets, and is up to 8 or 16 (TBD) octets
Size of Frame Body field will determine the maximum length of the WUR frame
  If Frame Body is 8 bytes then max WUR frame is 14 Bytes* (~1.9ms airtime@62.5kbps)
  If Frame Body is 16 Bytes then max WUR frame is 22 Bytes* (~3ms airtime@62.5kbps)
    Airtime is ~4 times less if 250 kbps is used for the transmissions
Proposal: Maximum length of Frame Body is 16 octets
    And the unit of the length to be 2 octets in order to reduce the size of the Length field
* Assuming the FCS field is 2 Bytes
 | Type | Length/Misc. | Reserved
Bits | 3-4 | 3-4 | rest

## Slide 4: FCS
Motioned: The FCS carries the CRC of the frame
  Length and computation of the FCS is TBD
  FCS additionally embeds BSSID information
    Not applicable for pre-association WUR frames)
    How to embed the BSSID information in the FCS is TBD
Items for discussion in the following slides:
  Computation of the CRC
  Embedding BSSID information in the FCS
MAC Header | Frame Body | FCS

## Slide 5: Embed BSSID information
Embedding BSSID info. requires AP and WUR STA to share this information in advance
  AP selects which portion of BSSID (or any other sequence?) is embedded in FCS and indicates it during association
    E.g., Embedded BSSID field contained in the WUR element could provide such information
      If WUR element is sent in PMF frame then transmission of WUR frames would provide some privacy as well
    Or assume whole BSSID is embedded but would require WUR STA to store all 6 bytes and could be known by all
  All WUR frames generated by AP post-association contain this embedded BSSID information
Embedding BSSID info. in the WUR frame can be done in two simple ways:
  Compute the CRC assuming that Embedded BSSID field is present
    Embedded BSSID field is not present in the transmitted WUR frame
  Compute the CRC and then XOR the Embedded BSSID with the CRC
    This option would allow XORing to extend beyond CRC (benefiting to privacy)
Frame Control | Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame
Frame Control | Address | TD Control | Frame Body | CRC
Embedded BSSID
X
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame
Compute CRC

## Slide 6: Computation of the CRC
WUR is expected to be a companion of MR radio
  Preference is to use an existing CRC engine available for the MR
    Aim at: minimizing complexity, memory, and FCS length
      Without significant degradation in terms of false alarms
MR (802.11) supports the three CRC engines listed below:
  32-bit CRC (e.g., MPDU protection (9.2.4.8 (FCS field)
    G(x) = x32 + x26 + x23 + x22 + x16 + x12 + x11 + x10 + x8 + x7 + x5 + x4 + x2 + x + 1
  16-bit CRC (e.g., SIG field protection of DSS PHY (15.3.3.7 (PHY CRC field)
    G(x) = x16 + x12 + x5 + 1
  8-bit CRC (e.g., A-MPDU delimiter protection (9.7.2 (MPDU delimiter CRC field)
    G(x) = x8 + x2 + x + 1
Proposal: Use one of these engines for obtaining the CRC
  Note: We could use a higher order generator polynomial even if the FCS field length is smaller
    E.g., if we decide FCS-8 and CRC-16 then send in FCS the 8 MSBs of calculated CRC etc.

## Slide 7: Length of FCS field (1)
FCS field length has been and continues to be debated
  Several options are candidates (8, 16, 24 bits)
    Longer FCS provides better protection but higher overhead
    Shorter FCS provides lesser protection but lower overhead
  A trade-off between the two properties need to be found
    Ensuring acceptable protection and low overhead for WUR frames
To make a decision we might need to consider that we have:
  Constant length (CL) WUR frames (only 4 bytes)
  Variable length (VL) WUR frames (up to 20 bytes)
And that the FCS could carry the MIC as well [1]
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | 8 | 12 | 12
CRC
TBD

## Slide 8: Length of FCS field (2)
Overhead (FCS length/MPDU length)
  The lower the overhead the better. Generally > 25% overhead is not desirable
False positive rate (worst case)
  The lower the false positive rate the better.
  The actual false positive will be lower since Address field has to check as well
Collision probability expected to be minimal due to
  At least 12 bits of Address field present in every WUR frame
  BSSID information will be hidden in the FCS of WUR frames sent after association
  WUR frames transmitted at scheduled times can reduce overlap with OBSS activities
Overhead [%] | 8-bit FCS | 16-bit FCS | 24-bit FCS
CL WUR frame (4B) | ~20% | ~33% | ~43%
Min VL WUR frame (6B) | ~14% | ~25% | ~33%
Max VL WUR frame(20B) | ~5% | ~9% | ~13%
NOTE-Every octet costs ~0.13ms of airtime@62.5kbps, and ~0.03ms of airtime@250kbps. |  |  | 
FPR [%] | 8-bit FCS | 16-bit FCS | 24-bit FCS
1/2n | ~4*10-3 | ~1.5*10-5 | ~6*10-8

## Slide 9: Further considerations
Since the impact of the FCS length may vary for different frames
  We might want to consider an FCS that is:
    Shorter for the CL WUR frames (4 Bytes payload)
    Longer for the VL WUR frames (20 Bytes payload)
For example we could use a 16-bit CRC polynomial
  8 bit CRC included in the FCS (e.g., 8 MSBs of the 16-bit CRC)
    Common for all WUR frames
  Additional 8 bit CRC included in the Frame Body of VL WUR frames
    Suppressed in transmission for CL WUR frames
These considerations are noteworthy if a unified FCS design for all WUR frames is not acceptable
  E.g., all WUR frames contain a TBD-bit FCS field
    Where TBD could be for example 8, 16, …

## Slide 10: Straw Poll 1
Do you support to amend the following text in the TGba SFD:
  “The length of the Frame Body field is in units of TBD 2 octets, and is up to 8 or 16 (TBD) octets.”

## Slide 11: Straw Poll 2
Do you support using one of the following CRC engines from IEEE 802.11 to compute the CRC?
  32-bit CRC, 16-bit CRC, 8-bit CRC

## Slide 12: Straw Poll 3
Which option do you prefer for embedding BSSID info. in the FCS?
  Option 1: Compute the CRC assuming that Embedded BSSID field is present
    Embedded BSSID field is not present in the transmitted WUR frame
  Option 2: Compute the CRC and then XOR the Embedded BSSID with the CRC
Frame Control | Address | Embedded BSSID | TD Control | Frame Body
Compute CRC
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame
Frame Control | Address | TD Control | Frame Body | CRC
Embedded BSSID
X
Frame Control | Address | TD Control | Frame Body | FCS (CRC)
Transmit WUR frame
Compute CRC

## Slide 13: References
[1] 11-17/1004r4 Considerations on WUR frame format (A. Asterjadhi, et. al.)
[2] 11-17/1115r5 11ba wakeup frame format (L. Chu, et. al.)
[3] 11-17/977r4 Address structure in unicast wake-up frame (J. Kim, et. al.)
[4] 11-17/1008r0 Vendor Specific WUR Frame Follow up (P. Huang, et. al.)
[5] 11-17/1608r0 WUR Discovery Frame for Smart Scanning (G. Li, et. al.)
[6] 11-17/1645r3 WUR frame format follow up (A. Asterjadhi, et. al.)