## Slide 1: WUR Preamble Sequence Performance Evaluation
Date: 2018-01-12
Authors:
Name | Affiliation | Address | Phone | Email
Justin Jia Jia | Huawei |  |  | justin.jia@huawei.com
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction
Current SFD[1] defines the WUR preamble structure where
  For high data rate: , where is the complementary sequence of the basic preamble sequence S
  For low data rate:
  To simplify the WUR detector implementation,
  A short local reference sequence for WUR signal detection (Correlation) is selected
  only one correlator is required at the WURx side

## Slide 3: Metrics
The correlations performed at WUR for high and low data preambles are:
The metrics for the optimum S are defined as follows
  Maximize the sum of negative high rate ACMetric and positive low rate ACMetric(sum of absolute values)
  Maximize the absolute ACMetric for both high rate and low rate
    Give the priority to the ACMetric of low rate under the same sum of absolute ACMetrics
    where indicates the absolute value

## Slide 4: Metrics Analysis
  Multiple Auto/Cross-Correlation Metrics may be not necessary
  It is impossible to have two sets of local reference sequence Refs at the correlator of the receiver
  Data rates can be identified by the sign of output of correlator at the receiver side
    It could be further enhanced by the number of peaks
  Auto Correlation Metric can ensure the timing performance
  The output sign of correlator in the numberator can be used to distinguish the two data rates
  The absolute value of second largest peak in denominator is used for our metrics to avoid the timing error and false rate detection
    A huge second largest peak with the same sign as the largest peak may cause timing error
    A huge second largest peak with the opposite sign as the largest peak may cause false rate detection
  In this contribution, we pick up three candidates of 32-bit-based basic sequence S1[3], S2[4], and S3 and evaluate their performance
  S1 = [1 0 1 0 0 0 1 1 0 1 1 0 1 1 1 1 0 0 0 0 1 0 0 1 1 1 0 0 0 1 0 1];
  S2 = [0 1 1 1 0 1 0 1 0 0 1 0 1 0 0 1 0 1 1 0 0 1 1 0 1 1 0 0 0 1 1 0];
  S3 = [1 0 1 0 0 1 0 0 1 0 1 1 1 0 1 1 0 0 0 1 0 1 1 1 0 0 1 1 1 0 0 0];
Equal number of Ones and Zeros
Recommended
Sequence

## Slide 5: Correlation Property of S1
Correlations at the receiver for S1:
ACMetric <HighR> | -8
ACMetric <LowR> | 4
Better performance for the high rate

## Slide 6: Correlation Property of S2
Correlations at the receiver for S2:
ACMetric <HighR> | -3.2
ACMetric <LowR> | 4

## Slide 7: Correlation Property of S3
Correlations at the receiver for S3:
ACMetric <HighR> | -5.3
ACMetric <LowR> | 8
Better performance for the low rate

## Slide 8: Metrics for preamble sequence
Summary on Metrics comparison
  S3 has the best performance for data rate, however, S1 performs best on high data rate
 | S1 | S2 | S3
ACMetric <HighR> | -8 | -3.2 | -5.3
ACMetric <LowR> | 4 | 4 | 8

## Slide 9: Simulation Settings[2]
Symbol Form:
  Preamble: 4us Conventional OOK, based on 32-bit S sequence
  Data Payload(Manchester):
    High Rate: 2us ON+2us OFF, vice versa
    Low Rate: 4us ON+4us OFF+4us ON+4us OFF, vice versa
Baseband Sampling: 5MHz—20 samples per OOK symbol(16-IFFT)
Channel Upsampling Rate.: 20x—@100MHz;
Channels: TGn Ch.D NLOS; CFO: +/-200ppm
Tx/Rx Filter: 5th-order Butterworth @ 2.5MHz Fc and 50MHz Fs
SNR Measurement: @20MHz by upsampling the baseband 5MHz(SNR is calculated with the inserted zeroes)
Front Silent Period: 2ms
False alarm rate is slightly less than 1% @all SNR
Data payload: 100bits
Sync Error Event Definition:
  Max(abs(Correlation Result))< Threshold
  S is detected as , vice versa
  Time acquisition error @5MHz fs samplings>2
Packet Error Event Definition:
  Max(abs(Correlation Result))< Threshold
  S is detected as , vice versa
  Bit error >0

## Slide 10: High Rate Sync Performance

## Slide 11: High Rate PER Performance

## Slide 12: Low Rate Sync Performance

## Slide 13: Low Rate PER Performance

## Slide 14: Summary
  Through the simulation results and metrics analysis, we obtain
  Low rate case: S3 outperforms S1 and S2 by about 0.3dB gain @1% PER, where S1 and S2 have similar overall PER performance
  High rate case: S1 and S3 outperforms S2 by 0.53dB gain and 0.23 dB gain @1% PER, respectively
It is recommended to choose S3 since the performance in low data rate environment is more concerned.
 | Low Rate |  | High Rate |  | Maximum off duration
 | 1% PER | 10% PER | 1% PER | 10% PER | 
 | SNR | SNR | SNR | SNR | 
S1 | 6.03dB | 0.62dB | 8.87dB | 4.09dB | 8 us
S2 | 6.00dB | 0.63dB | 9.40dB | 4.13dB | 6 us
S3 | 5.70dB | 0.61dB | 9.17dB | 4.19dB | 6 us

## Slide 15: Reference
[1] IEEE 802.11-17/0575r6,“Specification Framework for TGba”, Nov. 2017
[2] IEEE 802.11-17/0188r9, “Simulation Scenario and Evaluation Methodology”, Jul. 2017
[3]17/1636 r0 A Simple WUR Preamble Design
[4] 18/0123r0 Options for 32-bit S in Sync Field

## Slide 16: Straw Poll
Do you support S3 to use to construct the short preamble sequence and the long preamble sequence ?
  S3 = [1 0 1 0 0 1 0 0 1 0 1 1 1 0 1 1 0 0 0 1 0 1 1 1 0 0 1 1 1 0 0 0];
  where the bit duration is 2 us.
  Results: 11/0/21