## Slide 1: Discussion on TSF
Date: 2018-01-10
Authors:

## Slide 2: Introduction
TSF timer is proposed to be included in WUR beacon [1-3]
  It helps the WURx synchronize to the AP’s timer
  Current spec. states that the accuracy of the TSF timer shall be no worse than ±100 ppm
In this contribution, we focus on
  The TSF timer accuracy requirement

## Slide 3: TSF timer accuracy
To keep high transmit center frequency and symbol clock, a high-precision reference oscillator is required for every 802.11 PHY
  The worse accuracy shall be less than 20 ppm~25 ppm
  Typical reference clock frequencies are 22 or 44 MHz (802.11b), and 20, 40 or 80 MHz (802.11a or 802.11g)
At the beginning, 1588 in the upper layer was proposed to maintain timer in the MAC layer
To further reduce power and cost, the MAC-layer TSF timer is derived from a separate reference oscillator
  Generally speaking, the TSF is based on a 1-MHz clock and "ticks" in microseconds.
  Each STA maintains a TSF timer with modulus 264 counting in increments of microseconds
  non-DMG STA’s TSF timer shall be accurate to within ±100 ppm

## Slide 4: TSF timer accuracy
Extreme low power oscillator (LPO)
  The 32.768 kHz LPO clock is used when the STA stays in doze state where the radio, analog domains, and most of the linear regulators are powered down.
  It allows the power management sequencer to wake-up the chip and transition to Active mode.
  A maximum drive level is of a mere 1 uW [6]
  However, LPO still can keep the frequency stability less than 100 ppm based on the existing commercial oscillator datasheets [5]
  Some LPO accuracy even goes down to 10 ppm
  100 KHz oscillator keeps frequency stability within about 30 ppm
  Hence, it is not reasonable to assume the TSF timer accuracy for WUR is ±500ppm as [4]
  Hence, it is nature to keep the TSF timer accuracy within ± 100 ppm as today’s WiFi devices
  Otherwise, it brings serious time drift issue and requires frequent synchronization actions

## Slide 5: SP
Do you agree to maintain the TSF timer accuracy in the MAC layer for WUR STA within ±100 ppm?

## Slide 6: Reference
[1] 17/1004r4 Consideration on WUR frame format
[2] 17/1645r3 WUR frame format – Follow up
[3] 20170221 Intel WUR Beacon Follow up
[4] 17/1384r0 WUR Synchronization
[5] https://www.mouser.com/Passive-Components/Frequency-Control-Timing-Devices/Oscillators/Standard-Clock-Oscillators/_/N-7jdva?P=1yzmo0z&FS=True
[6] Clock solutions for WiFi (IEEE 802.11) http://application-notes.digchip.com/031/31-20310.pdf