## Slide 1: Further considerations on WUR frame format
Date: 2018-01-10
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
Some SFD texts for WUR frame format[1]
  The Frame Control field is 8 bits and contains:
    A Type subfield that identifies the type and, together with the Length field differentiates between constant length (CL) and variable length (VL) WUR frames
  TBD bits Type field is included in the Frame control field of MAC header with the following mapping of the Type field: 0 assigned to WUR Beacon, 1 assigned to Wake-Up frame, 2 assigned to Vendor specific frame
  The Address field is 12 bits, and the TD Control field is 12 bits
  Address field of Wake-Up frame contains WID for unicast frame, Group ID for multicast frame, and TXID for broadcast frame
  The WUR Action frame sent by an AP through the PCR includes a WUR identifier (WID):
    The WID uniquely identifies a WUR STA within the BSS of the AP.
    The WID is included in a unicast wake-up frame to identify the intended immediate recipient WUR STA within the BSS of the AP.
  A wake-up frame with variable length may contain the information for the multiple STAs in the Frame Body
  The FCS additionally embeds BSSID information:
  AP may negotiate one or more Group IDs to a STA through PCR
    The assigned Group ID is used in a wake-up frame
    The details for group ID (e.g., ID allocation procedure (e.g., WUR Action frame or others similar to 11ac procedure), ID structure, etc.) are TBD
This contribution provides more details of WUR frame format

## Slide 3: WUR Identifier (WID)
According to SFD text[1], a WID is included in a wake-up frame
  Some of WIDs are individual WID(I-WID)s used in unicast wake-up frame
  A value of WIDs (e.g., TXID, 0 or 4096) is broadcast WID (B-WID) used in broadcast wake-up frame
  Others of WIDs are group WID(G-WID)s used in multicast wake-up frame
Update the SFD texts for clarification
  R.2.4.E: The WUR Action frame sent by an AP through the PCR includes an individual WUR identifier (WID):
    The individual WID(I-WID) uniquely identifies a WUR STA within the BSS of the AP.
    The individual WID is included in a unicast wake-up frame to identify the intended immediate recipient WUR STA within the BSS of the AP.
    The size of the individual WID is TBD, and how it is computed is TBD.
  R.2.4.F: AP may negotiate one or more Group WIDs to a STA through PCR
    The assigned Group WID(G-WID) is used in a wake-up frame
    The details for Group WID (e.g., ID allocation procedure (e.g., WUR Action frame or others similar to 11ac procedure), ID structure, etc.) are TBD
  ….

## Slide 4: Group ID (1/3)
A GID is used in multicast wake-up and one or more GIDs can be assigned to a STA
GID assignment procedure
  Option 1: WUR Parameter Negotiation (e.g., Enter WUR Mode RSP/Mode Suspend RSP)
  Option 2: New frame for WUR Group ID assignment (e.g., WUR GID management)
AP
STA
Association
procedure
WUR Mode Request
WUR Mode Response (GIDs)
AP
STA
Association
procedure
WUR Mode Suspend Request
WUR Mode Suspend Response
WUR GID management (GIDs)
We prefer option 1 because option 1 is simple and doesn’t make an additional procedure and new frame for Group ID assignment
WUR Mode Request
WUR Mode Response

## Slide 5: Group ID (2/3)
Multicast wake-up packet can be used for PCR MU PPDU TX (i.e., unicast data) as well as multicast-group addressed frames TX
  Note that group address is divided into broadcast address and multicast-group address in [2]
  Broadcast wake-up frame can be used for indicating broadcast addressed frame
For multicast wake-up for PCR MU PPDU TX, intended STA needs to send WUR response frame to a AP through PCR
Generally, AP will not require intended STA to send WUR response frame through PCR in response to multicast wake-up frame for multicast-group addressed frames
  But AP may require intended STA to send WUR response frame in response to multicast wake-up frame for some multicast-group group addressed frame
    E.g., STAs requiring GCR Block Ack or when the number of STAs belonging to a group is small

## Slide 6: Group ID (3/3)
Need a mechanism to indicate whether or not the intended STA should send WUR response frame in response to multicast wake-up frame
Option 1: adding 1 bit indicator in TD Control field of MU WUR frame
  When the MU WUR frame is sent, AP decides if the MU WUR frame requires STA to send WUR response frame or not  Providing the flexible scheduling and adopting this to all GIDs but need to add 1 bit in TDC
Option 2: Two types of Group ID
  During GID assignment, AP indicates if the GID requires intended STA to send WUR response frame  Not providing full flexible scheduling but not require additional bit in WUR frame
  A part of Group IDs requires STA to send WUR response frame for multicast wake-up
  The other GIDs does not require STA to send WUR response frame for multicast wake-up

## Slide 7: Multiple STA information in wake-up frame (1/4)
In SFD[1]: A wake-up frame with variable length may contain the information for the multiple STAs in the Frame Body
  The detailed information of multiple STAs (e.g., bitmap, ID list) is TBD
  Unicast wake-up frame does not carry the information of multiple STAs
This is extended format of multicast wake-up
If Address field contains Group ID and Length = 0, Frame Body is not present and all of the STAs belonging to the group turns on their PCR
If Address field contains Group ID and Length > 0, the WID/User bitmap is included in the Frame Body and only STAs corresponding to the bits set to 1 in the bitmap will turn on their PCR
MAC header
Frame Body
FCS
Type=1, Length=2 byte, Address=GID
2 bytes WID/User Bitmap

## Slide 8: Multiple STA information in wake-up frame (2/4)
Option 1: WID Bitmap
  STA’s position in the Bitmap is Bit N where N is value of (STA’s WID mod the bit size of Bitmap)
    E.g.,) If STA X/Y’s WID = 3/32 & Size of Bitmap = 16 bits, then Bit 3/0(=3/32 mode 16) for STA X/Y
  The received Group ID also should be equal to one of the assigned Group IDs (i.e., if group ID is not equal, the frame is ignored)
  Some STAs may be located at the same position (Bit N) of the bitmap (i.e., not unique position)
  This can be solved by AP’s implementation
    Ex 1) AP can assign those STAs to different groups (e.g., Group 1 for WID = 16, Group 2 for WID = 32)
    Ex 2) AP can assign those STAs to different On durations (e.g., Group 1 and 1st On duration for WID = 8, Group 1 and 2nd On duration for WID=16)
    Ex 3) AP can use WID Bitmap considering only STAs which have the capability of variable frame length
  When AP assigns WUR GIDs to a STA, the AP doesn’t need to notify the STA of the User position in the group  No overhead of User Position information in the assignment frame
  ….
B0
B1
B2
B3
B4
B5
B6
B15
STA X
STA Y
…

## Slide 9: Multiple STA information in wake-up frame (3/4)
Option 2: User Bitmap
  When AP assigns Group IDs to a STA, the AP informs the STA of the User Position in the group (similar to 11ac GID management procedure [2]). That is, Need to add the User Position information into the frame for GID assignment  additional frame overhead
  The size of User position information depends on the maximum size of User Bitmap
    E.g.,) if the maximum size of the User Bitmap is 2 bytes (16 bits)
    E.g.,) if the maximum size of the User Bitmap is 4 bytes (32 bits)
User Position in 1st GID
User Position in 2nd GID
User Position in N-th GID
…
4 bits
4 bits
4 bits
User Position Array field
User Position in 1st GID
User Position in 2nd GID
User Position in N-th GID
…
5 bits
5 bits
5 bits
User Position Array field
4 x N (bits)
5 x N (bits)

## Slide 10: Multiple STA information in wake-up frame (4/4)
A special value of GID (e.g., 0) indicates the individual WID list presence
  Option 1: 12 bits length WIDs are included in Frame body
  Option 2: Partial WID (8 least significant bits of WID)s are included in Frame body
MAC header
Frame Body
FCS
Type=1, Length = 6 byte, GID = 0
4 WIDs
MAC header
Frame Body
FCS
Type=1, Length = 4 byte, GID = 0
6 WIDs

## Slide 11: Broadcast wake-up (1/2)
SFD text[1]
  TXID is used in broadcast wake-up and GID is used in multicast wake-up
  A non-individually addressed wake-up frame may include the information for indicating the group addressed frame transmission through PCR
    The details of indicating the group addressed frame transmission (e.g., using Group ID or additional bit) is TBD
In legacy spec[2], there are two kinds of group addresses
  One is multicast-group address and the other is broadcast address (section 9.2.4.3.3)
Broadcast wake-up is used for broadcast addressed frame as well as BSS parameter update while multicast wake-up is used for indicating multicast-group addressed frame
  Need to distinguish if the broadcast wake-up is for broadcast addressed frame TX or not for more power saving of the STA (See next slide)
Broadcast addressed frame indication
  Option 1: Broadcast addressed frame presence field set to 1 indicates the broadcast wake-up with broadcast addressed frame indication. The field can be included in TD control field of broadcast Wake Up frame
  Option 2: A value of WID (e.g., 0 or TXID) is for broadcast wake-up without broadcast addressed frame indication. Another ID (e.g., 1 or TXID+1) is for broadcast wake-up with broadcast addressed frame indication
  AP shall not assign WIDs used for broadcast wake-up as individual WID or group WID

## Slide 12: Broadcast wake-up (2/2)
STA operation
  For broadcast wake-up without broadcast addressed frame indication,
    If the stored counter for BSS parameter doesn’t equal to the received counter, STA attempts to update BSS parameters (e.g., The STA receives the PCR beacon after waking up at the TBTT or the STA sends the Probe Request to AP). In this case, the STA may enter the doze state until next TBTT
    After updating the BSS parameter, the STA can enter the doze state of PCR
  For broadcast wake-up with broadcast addressed frame indication,
    STA may attempt to receive broadcast frame as well as the BSS parameter update
    After updating the BSS parameters in case that the BSS parameter update is required, the STA waits for broadcast frame. In this case, the STA can enter the doze state at the broadcast frame TX start time (e.g., Target DTIM transmission time)
    After receiving broadcast frame as well as updating the BSS parameter, the STA can enter the doze state

## Slide 13: Reference
[1] 11-17-0575-06-00ba-spec-framework
[2] 802.11-2016

## Slide 14: Straw Poll 1
Do you agree to modify the SFD text related to WID and Group ID as follows?
  R.2.4.E: The WUR Action frame sent by an AP through the PCR includes an individual WUR identifier (WID):
    The individual WID(I-WID) uniquely identifies a WUR STA within the BSS of the AP.
    The individual WID is included in a unicast wake-up frame to identify the intended immediate recipient WUR STA within the BSS of the AP.
    The size of the individual WID is TBD, and how it is computed is TBD.
  R.2.4.F: AP may negotiate one or more Group WIDs to a STA through PCR
    The assigned Group WID(G-WID) is used in a wake-up frame
    The details for Group WID (e.g., ID allocation procedure (e.g., WUR Action frame or others similar to 11ac procedure), ID structure, etc.) are TBD

## Slide 15: Straw Poll 2
Which option do you prefer as the Group ID assignment procedure?
  Option 1: Using WUR parameter negotiation procedure
    e.g., WUR Mode Response frame or WUR Mode Suspend Response frame
  Option 2: Using new WUR GID management procedure
    e.g., Define new WUR GID management Action frame

## Slide 16: Straw Poll 3
Do you agree the following?
  TGba shall define the mechanism to indicate whether or not the intended STA should send WUR response frame in response to multicast wake-up frame

## Slide 17: Straw Poll 4
Which option do you prefer as the mechanism to indicate whether or not the intended STA should send WUR response frame in response to multicast wake-up frame?
  Option 1: adding 1 bit in TD Control field for the purpose
    0: Indicate that the intended STAs should not send WUR response frame via PCR in response to multicast wake-up frame
    1: Indicate that the intended STA should send WUR response frame via PCR in response to multicast wake-up frame
  Option 2: Define two types of Group ID
    One type: Indicate that the intended STAs should not send WUR response frame via PCR in response to multicast wake-up frame
    The other type: Indicate that the intended STA should send WUR response frame via PCR in response to multicast wake-up frame

## Slide 18: Straw Poll 5
Do you agree the following?
  When the Address field is Group ID and the Length field is not 0 in Wake Up frame, the bitmap indicating the multiple STAs is present in Frame Body of the frame
    The size of the Bitmap is decided by the value of Length field

## Slide 19: Straw Poll 6
Which option do you prefer as the bitmap to indicate multiple STAs in multicast Wake Up frame?
  Option 1: WID Bitmap described in slide 8
  Option 2: User Bitmap described in slide 9

## Slide 20: Straw Poll 7
Do you agree the following?
  When the Address field of Wake Up frame contains a special value of Group ID (e.g., 0), the Frame Body of the Wake Up frame contains the list of individual WIDs
    The size of a individual WID included in the Frame Body is TBD

## Slide 21: Straw Poll 8
Which option do you prefer as the size of the individual WIDs included in the Frame Body?
  Option 1: The same size as the assigned individual WID (e.g., 12 bits)
  Option 2: Partial individual WID (e.g., 8 least significant bits WID)

## Slide 22: Straw Poll 9
Do you agree the following?
  The broadcast addressed Wake Up frame contains the information to indicate that the broadcast addressed frame(s) will be transmitted through PCR

## Slide 23: Straw Poll 10
Which option do you prefer as a mechanism to inform WUR STA that the broadcast frame will be sent through PCR?
  Option 1: Adding one bit indicator field in TD Control field of broadcast Wake Up frame
    The indicator set 1 indicates that the broadcast frame will be sent through PCR
  Option 2: Define two broadcast WIDs for broadcast wake-up
    One (e.g., 0 or TXID) is broadcast wake-up without broadcast frame in PCR
    The other (e.g., 1 or TXID + 1) is broadcast wake-up with broadcast frame in PCR
    Two broadcast WIDs are not assigned as Individual/group WID