## Slide 1: Further considerations on WUR frame format
Date: 2018-01-10
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
Some SFD texts for WUR frame format[1]
  The Frame Control field is 8 bits and contains:
    A Type subfield that identifies the type and, together with the Length field differentiates between constant length (CL) and variable length (VL) WUR frames
  TBD bits Type field is included in the Frame control field of MAC header with the following mapping of the Type field: 0 assigned to WUR Beacon, 1 assigned to Wake-Up frame, 2 assigned to Vendor specific frame
  The Address field is 12 bits, and the TD Control field is 12 bits
  Address field of Wake-Up frame contains WID for unicast frame, Group ID for multicast frame, and TXID for broadcast frame
  The WUR Action frame sent by an AP through the PCR includes a WUR identifier (WID):
    The WID uniquely identifies a WUR STA within the BSS of the AP.
    The WID is included in a unicast wake-up frame to identify the intended immediate recipient WUR STA within the BSS of the AP.
  A wake-up frame with variable length may contain the information for the multiple STAs in the Frame Body
  The FCS additionally embeds BSSID information:
  AP may negotiate one or more Group IDs to a STA through PCR
    The assigned Group ID is used in a wake-up frame
    The details for group ID (e.g., ID allocation procedure (e.g., WUR Action frame or others similar to 11ac procedure), ID structure, etc.) are TBD
This contribution provides more details of WUR frame format

## Slide 3: WUR Identifier (WID)
STA can know if the received Wake Up frame is sent by the unicast, multicast, or broadcast by address field of MAC address of the frame
  If the WID is included in Address field, unicast wake-up frame
  If the Group ID is included in Address field, multicast-group wake-up frame
  If the Broadcast ID (e.g., TXID) is included in Addressed field, broadcast-group wake-up frame
Therefore, AP should not assign WID to a STA with the same value as one among the Group IDs or TXID
And, AP should not assign Group ID to a STA with the same value as one among the WIDs or TXID

## Slide 4: Broadcast wake-up (1/2)
SFD text[1]
  TXID is used in broadcast wake-up and GID is used in multicast wake-up
In baseline spec[2], there are two kinds of group addresses
  One is multicast-group address and the other is broadcast address (section 9.2.4.3.3)
Broadcast wake-up is used for broadcast addressed frame as well as BSS parameter update while multicast wake-up is used for indicating multicast-group addressed frame
Need to distinguish if the broadcast wake-up is for broadcast addressed frame TX or not for more power saving of the STA (See next slide)
Broadcast addressed frame indication
  Option 1: Broadcast addressed frame presence field set to 1 indicates the broadcast wake-up with broadcast addressed frame indication. The field can be included in TD control field of broadcast Wake Up frame
  Option 2: A value of WID (e.g., 0 or TXID) is for broadcast wake-up without broadcast addressed frame indication. Another ID (e.g., 1 or TXID+1) is for broadcast wake-up with broadcast addressed frame indication
  AP shall not assign WID or group ID to a STA with WIDs used for broadcast wake-up

## Slide 5: Broadcast wake-up (2/2)
STA operation
  For broadcast wake-up without broadcast addressed frame indication,
    If the stored counter for BSS parameter doesn’t equal to the received counter, STA attempts to update BSS parameters (e.g., The STA receives the PCR beacon after waking up at the TBTT or the STA sends the Probe Request to AP). In this case, the STA may enter the doze state until next TBTT
    After updating the BSS parameter, the STA can enter the doze state of PCR
  For broadcast wake-up with broadcast addressed frame indication,
    STA may attempt to receive broadcast frame as well as the BSS parameter update
    After updating the BSS parameters in case that the BSS parameter update is required, the STA waits for broadcast frame. In this case, the STA can enter the doze state at the broadcast frame TX start time (e.g., Target DTIM transmission time)
    After receiving broadcast frame as well as updating the BSS parameter, the STA can enter the doze state

## Slide 6: Group ID (1/3)
A GID is used in multicast wake-up frame and one or more GIDs can be assigned to a STA
GID assignment procedure
  Option 1: WUR Parameter Negotiation (e.g., Enter WUR Mode RSP/Mode Suspend RSP)
  Option 2: New frame for WUR Group ID assignment (e.g., WUR GID management)
AP
STA
Association
procedure
WUR Mode Request
WUR Mode Response (GIDs)
AP
STA
Association
procedure
WUR Mode Suspend Request
WUR Mode Suspend Response
WUR GID management (GIDs)
We prefer option 1 because option 1 is simple and doesn’t make an additional procedure and new frame for Group ID assignment
WUR Mode Request
WUR Mode Response

## Slide 7: Group ID (2/3)
In SFD[1], WUR STA should send WUR response frame via PCR in response to unicast wake-up frame
Then, multicast wake-up frame?
WUR STA doesn’t have to send any WUR response frame in response to multicast wake-up frame if the multicast wake-up frame is sent for indicating multicast-group addressed BU
But, AP may require WUR STA to send WUR response frame via PCR in response to Multicast wake-up frame in following cases
  When the multicast wake-up frame is sent for PCR DL MU PPDU Tx containing unicast data
  When the number of STAs belonging to a group is small

## Slide 8: Group ID (3/3)
Possible options
  Option 1: adding 1 bit indicator in multicast wake-up frame
    When the multicast wake-up frame is sent, AP decides if the MU WUR frame requires STA to send WUR response frame or not
    Pros & Cons: Providing the flexible scheduling and adopting this to all GIDs but need to add 1 bit in TDC
  Option 2: Two types of Group ID
    During GID assignment, AP indicates if the GID requires intended STAs to send WUR response frame
    A part of Group IDs requires STA to send WUR response frame for multicast wake-up
    The other GIDs does not require STA to send WUR response frame for multicast wake-up
    Pros & Cons: Not providing full flexible scheduling but not require additional bit in WUR frame

## Slide 9: Multiple STA information in wake-up frame (1/4)
In SFD[1]: A wake-up frame with variable length may contain the information for the multiple STAs in the Frame Body
  The detailed information of multiple STAs (e.g., bitmap, ID list) is TBD
  Unicast wake-up frame does not carry the information of multiple STAs
If Address field contains Group ID and Length = 0, Frame Body is not present and all of the STAs belonging to the group turns on their PCR
If Address field contains Group ID and Length > 0, the WID/User bitmap is included in the Frame Body and only STAs corresponding to the bits set to 1 in the bitmap will turn on their PCR
MAC header
Frame Body
FCS
Type=1, Length=2 byte, Address=GID
2 bytes WID/User Bitmap

## Slide 10: Multiple STA information in wake-up frame (2/3)
Option 1: WID Bitmap
  STA’s position in the Bitmap is Bit N where N is value of (STA’s WID mod the bit size of Bitmap)
    E.g.,) If STA X/Y’s WID = 3/32 & Size of Bitmap = 16 bits, then Bit 3/0(=3/32 mode 16) for STA X/Y
  The received Group ID also should be equal to one of the assigned Group IDs (i.e., if group ID is not equal, the frame is ignored)
  Some STAs may be located at the same position (Bit N) of the bitmap (i.e., not unique position)
  This can be solved by AP’s implementation
    Ex 1) AP can assign those STAs to different groups (e.g., Group 1 for WID = 16, Group 2 for WID = 32)
    Ex 2) AP can assign those STAs to different On durations (e.g., Group 1 and 1st On duration for WID = 8, Group 1 and 2nd On duration for WID=16)
    Ex 3) AP can use WID Bitmap considering only STAs which have the capability of variable frame length
  When AP assigns WUR GIDs to a STA, the AP doesn’t need to notify the STA of the User position in the group  No overhead of User Position information in the assignment frame
  ….
B0
B1
B2
B3
B4
B5
B6
B15
STA X
STA Y
…

## Slide 11: Multiple STA information in wake-up frame (3/3)
Option 2: User Bitmap
  When AP assigns Group IDs to a STA, the AP informs the STA of the User Position in the group (similar to 11ac GID management procedure [2]). That is, Need to add the User Position information into the frame for GID assignment  additional frame overhead
  The size of User position information depends on the maximum size of User Bitmap
    E.g.,) if the maximum size of the User Bitmap is 2 bytes (16 bits)
    E.g.,) if the maximum size of the User Bitmap is 4 bytes (32 bits)
User Position in 1st GID
User Position in 2nd GID
User Position in N-th GID
…
4 bits
4 bits
4 bits
User Position Array field
User Position in 1st GID
User Position in 2nd GID
User Position in N-th GID
…
5 bits
5 bits
5 bits
User Position Array field
4 x N (bits)
5 x N (bits)

## Slide 12: Reference
[1] 11-17-0575-06-00ba-spec-framework
[2] 802.11-2016

## Slide 13: Straw Poll 1
Do you agree to modify the SFD as following?
  R.4.7.3.A: A non-individually addressed wake-up frame that has the Address field set to a value of TBD indicates that the AP intends to transmit group addressed frames may include the information for indicating the group addressed frame transmission through PCR
    The details of indicating the group addressed frame transmission (e.g., using Group ID or additional bit) is TBD
    Y:18, N: 8, A:11

## Slide 14: Straw Poll 2
Do you agree to modify the SFD as following?
  AP may negotiate one or more Group IDs to with a STA through PCR using WUR Action frame during WUR negotiation and WUR mode signaling procedure
    The assigned Group ID is used in a wake-up frame
    The details for group ID (e.g., ID allocation procedure (e.g., WUR Action frame or others similar to 11ac procedure), ID structure, etc.) are TBD
Y:27, N:0, A:3

## Slide 15: Straw Poll 3
Do you agree the following?
  If the Frame Body is present in the WUR Wake Up frame and the Address field is set to 0, the Frame Body contains multiple WIDs.
Y:15, N:1, A: 13

## Slide 16: Motion 1
Move to modify the following TGba SFD text as following
  AP may negotiate one or more Group IDs to with a STA through PCR using WUR Action frame during WUR negotiation and WUR mode signaling procedure
    The assigned Group ID is used in a wake-up frame
    The details for group ID (e.g., ID allocation procedure (e.g., WUR Action frame or others similar to 11ac procedure), ID structure, etc.) are TBD
Y:, N:, A:

## Slide 17: Motion 2
Move to add the following into TGba
  If the Frame Body is present in the WUR Wake Up frame and the Address field is set to 0, the Frame Body contains multiple WIDs.
Y:, N:, A: