## Slide 1: Clarification for Variable-length WUR frame
Date: 2018-01-10
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
There is ambiguity for SFD texts on variable-length WUR frame
  R.4.9.1.B: The Frame Control field is 8 bits and contains:
    A Type subfield that identifies the type and, together with the Length field differentiates between constant length (CL) and variable length (VL) WUR frames
    A Length/Misc field which contains:
      The length of the Frame Body field for a VL WUR frame
      Bits that are expected to be used for other purposes for a CL WUR frames
        No Length field is present in CL WUR frames
  R.4.9.1.A: TBD bits Type field is included in the Frame control field of MAC header with the following mapping of the Type field:
    0 assigned to WUR Beacon
    1 assigned to Wake-Up frame
    2 assigned to Vendor specific frame
  R.4.9.3.C: A wake-up frame with variable length may contain the information for the multiple STAs in the Frame Body
Need to clarify the SFD text w/o any ambiguity

## Slide 3: Possible options
Option 1: Add 1 bit CL/VL indicator in FC field (8 bits) of Wake Up frame
  If the indicator is VL, the frame is VL and the Length is included in FC field.
  Otherwise, the frame is CL and Misc. is included in FC field instead of Length
Option 2: Length field is always present when Type field is 1 (Wake Up frame)
  If the Length is 0, CL Wake Up frame. Otherwise, VL Wake Up frame
FC (8 bits)
Address (12 bits)
TD Control (12 bits)
Type (3bits)
CL/VL indicator (1 bit)
Length/Misc. (4 or 3 bits)
FC (8 bits)
Address (12 bits)
TD Control (12 bits)
Type (3bits)
Length (3or 4 bit)
Reserved (2 or 1 bits)
Reserved (0 or 1 bit)
MAC header of Wake Up frame
MAC header of Wake Up frame

## Slide 4: Straw Poll
Which option do you prefer as a method for distinguish CL and VL WUR Wake Up frame?
  Option 1: 1 bit CL/VL indicator is present in FC field of Wake Up frame
    If the indicator is CL, the Misc. is included in FC field. Otherwise, the Length is included in FC field
  Option 2: Length field is always present when Type field is 1 (Wake Up frame)
    If the Length is 0, the frame is CL. Otherwise, the frame is VL
Option 1: 18, Option 2: 11

## Slide 5: Motion 1
Move to add the following into TGba
  1 bit CL/VL indicator is present in the FC field of the Wake Up frame
    If the indicator is CL, the Misc field is included in the FC field. Otherwise, the Length field is included in the FC field
FC (8 bits)
Address (12 bits)
TD Control (12 bits)
Type (3bits)
CL/VL indicator (1 bit)
Length/Misc. (TBD bits)
Reserved (TBD bit)
MAC header of WUR Wake Up frame

## Slide 6: Motion 2
Move to add the following into TGba
  The Length field is always present when the Type field is set to 1 (Wake Up frame)
    If the Length is set to 0, the frame is a constant length (CL) WUR Wake Up frame. Otherwise, the frame is a variable length (VL) WUR Wake Up frame
FC (8 bits)
Address (12 bits)
TD Control (12 bits)
Type (3bits)
Length (TBD bits)
Reserved (TBD bits)
MAC header of WUR Wake Up frame