## Slide 1: WUR Beacon transmission
Date: 2018-01-05
Authors:
Name | Affiliation | Address | Email
Li Nan | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | li.nan25@zte.com.cn
Lv Kaiying |  |  | lv.kaiying@zte.com.cn
Sun Bo |  |  | sun.bo1@zte.com.cn
Wei Ning |  |  | wei.ning@zte.com.cn

## Slide 2: Abstract
WUR Beacon is transmitted periodically by an AP for the synchronization of STAs in WUR mode.
Motion about WUR channel has passed [1]:
  R.4.2.G:AP decides the WUR operating channel in the band(s) supported by the associated non-AP STA operating in WUR Mode.
AP may define own one or more WUR channels,which means associated STAs in the BSS may monitor different WUR channels for WUR frames. And the AP can utilze multi-user transmission for WUR frames. [2][3]
WUR Beacon transmission on multiple WUR channels is discussed in this presentation.

## Slide 3: WUR channel
WUR Channel is the channel on which a STA monitors WUR frames with broadcast RA(WUR Beacon, Discovery frame) or multicast/unicast RA (Wake-up frames).
The allocation of WUR channels within AP’s operation bandwidth could be one of the following cases:
  Within Primary channel and/or Secondary channels
  WUR channels in 2.4GHz and PCR channels in 5GHz
For the cases above,three approachs for sending WUR Beacon are discussed in the next slides.

## Slide 4: WUR Beacon Transmission
Approach 1: AP sends WUR Beacon on each WUR channel and each WUR Beacon's interval is based on the timing accuracy of the STA operating on the corresponding WUR channel.
  The STA’s WUR channel is allocated considering the TSF timing accuracy requirement of the STA so that STAs operating on the same WUR channel have the same or similar timing accuracy
  WUR Beacons sent on different WUR channels may have different WUR Bl,which could be notified to the STAs monitoring that WUR channel through WUR negociation.
  WUR Beacons will be sent on every WUR channels

## Slide 5: WUR Beacon Transmission
Approach 2:WUR Beacon is sent on one WUR channel in the corresponding 20MHz channel.
  Choosing one of the WUR channels in each 20MHz as the WUR Beacon channel to send WUR Beacon.
  STAs monitor wake-up frames on its WUR channel and receive WUR beacon on WUR Beacon channel within the same 20MHz.
    Pros: Less WUR Beacon sent than Approach 1
    Cons:
      STAs have to perform channel switch to receive WUR Beacon if its WUR channel is different from the WUR Beacon.

## Slide 6: Conclusion
We discussed two approaches to send WUR beacon on multiple WUR channels
Both overhead and simplicity of the operation should be considered.
The transmission of WUR Beacon could be further optimized.

## Slide 7: Straw Poll 1
Which approach for sending WUR Beacon is preferred if multiple WUR channels are defined by an AP?
  Approach1:Y N A
  Approach2:Y N A

## Slide 8: Straw Poll 2
Do you agree to add the proposed Text to SFD?
  R.4.2.G:[Assigned D0.1] AP decides the WUR operating channel in the band(s) supported by the associated non-AP STA operating in WUR Mode.
    –AP may send WUR beacon on multiple WUR operating channel(s).The WUR beacon interval could be different based on the timing accuracy of the STA operating on the corresponding WUR operating channel.
  Y :
  N :
  A :

## Slide 9: Proposed text in Draft
TGba Editor: Instruction: Add text in 31.3.1 as follows:
31.3 Maintaining synchronization
31.3.1 General
...
  For the purpose of maintaing synchronization for the associated STAs, AP sends WUR beacon on multiple WUR operating channel(s).The WUR beacon period on different WUR operating channels could be different based on the timing accuracy of the STA operating on the corresponding WUR operating channel.In this case,a STA with WURx shall adopt the WUR beacon period of its WUR operating channel during WUR negociation.

## Slide 10: References
[1]11-17-0575-08-00ba-spec-framework
[2]11-17-1333-01-00ba-wur-operating-channel
[3]11-17-0028-00-00ba-on-waking-up-of-multiple-wur-stations