## Slide 1: How to describe WUR PPDU Waveform Generation
Date: 2018-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Justin Jia Jia |  |  |  | 
Ming Gan |  |  |  | 
Ross Jian Yu |  |  |  | 

## Slide 2: Background
The single band WUR PPDU waveform is supposed to be generated by using contiguous 13 subcarriers with subcarrier spacing of 312.5 KHz and with the center subcarrier nulled [1].
However, it is implementation-specific how to actually generate the time-domain waveform according to [1].
There was a proposal to mandate a sequence occupying the contiguous 13 subcarriers during the discussion in the last Nov. F2F meeting [2], but majority seemed to support describing how to generate the waveform in detail only as an example in the Spec text.
There are three different WUR PPDU waveform generation methods discussed in the TGba [3-5].

## Slide 3: 3 different WUR PPDU waveform generation
Method 1: Time-domain Masking based (for high data rate) [3]
  The contiguous middle 13 subcarriers out of 20 MHz 64 subcarriers are occupied with a certain sequence
  The 64 point IFFT is taken for the 20 MHz 64 subcarriers, and then the last 16 samples of the 64 samples are pre-pended to the 64 samples in order to create a 4 usec long time domain waveform
  Masking is applied in the time-domain to generate the “2 usec ON (OFF) – 2 usec OFF (ON)” Manchester coded pulse
  The time domain waveform generated above can be stored in a memory space and retrieved every time 250 Kbps high data rate WUR PPDU waveform is transmitted.
Method 2: FFT based (for high data rate) [4]
  The contiguous middle 13 subcarriers out of 20 MHz subcarriers are occupied with a certain sequence
  The 32 point IFFT is taken for the 20 MHz subcarriers, and then the last 8 samples of the 32 samples are pre-pended to the 32 samples in order to create a 2 usec long time domain waveform.
  The time domain waveform generated above can be stored in a memory space and retrieved every time 250 Kbps high data rate WUR PPDU waveform is transmitted.
  The 2 usec long time domain waveform generated above constitutes the ON portion of a Manchester coded pulse for 250 Kbps WUR PPDU waveform

## Slide 4
Method 3: Sequence based [5]
  A certain sequence occupies the different subcarriers out of 256 20 MHz subcarriers depending on the data and the symbol position.
  Three WUR pulses are generated at a time.
  Base sequence is taken with 64 DFT to generate 312.5 KHz spaced 64 subcarriers, before 256 IFFT is taken

## Slide 5: Summary
The WUR PPDU waveform generation is fundamental in the TGba PHY/MAC schemes and technologies. However, it is missing in the SFD without detail descriptions.
It is observed that we may have the following three options to fill-in the missing part in the SFD and D0.1.
  Option 1: All the WUR waveform generation procedures need to be specified in detail including the FFT size, the value of all the coefficients, and how the multicarrier waveform is modulated by the OOK signal
  Option 2: All the WUR waveform generation procedures need to be specified, including the FFT size, the list of which coefficients are non-zero, and how the multicarrier waveform is modulated by the OOK signal, except for the values of the coefficients. The standard would include on example set of coefficients, but other coefficient values would be allowed by the standard.
  Option 3: Any of the WUR waveform generation procedure does not have to be specified except for the following which is already decided
    When a single band is used for transmission of WUR PPDU, the OOK waveform of WUR PPDU is generated by using contiguous 13 subcarriers with the subcarrier spacing of 312.5 kHz
    In this case, it is strongly recommended to describe a detail generation procedure including the coefficients as an example

## Slide 6: Reference
[1] P. Huang “17/0575r7 Spec Framework, R.3.3.C”, IEEE 802.11 TGba, Nov 2017, Orlando, FL USA
[2] E. Park, et. al. “17/1613r2 13-Length Sequence for OOK Waveform Generation”, IEEE 802.11 TGba, Nov 2017, Orlando, FL USA
[3] J. Suh, et. al. “17/376r0 Waveform Generation for Waveform coding”, IEEE 802.11 TGba, Mar 2017, Vancouver, BC Canada
[4] V. Kristem, et. al. “17/1615r0 Discussion on OOK Pulse Design for Higher Rate”, IEEE 802.11 TGba, Nov 2017, Orlando, FL USA
[5] R. Yang, et. al. “17/1037r2 Performance Evaluation of OOK Waveform Coding Schemes with Impairments”, IEEE 802.11 TGba, July 2017, Berlin, Germany

## Slide 7: Straw Poll
How do you want to describe the WUR waveform generation procedures in the SFD and D0.1?
  Option 1
  Option 2
  Option 3