## Slide 1: BRP frame exchange in TDD SP
Authors:
Name | Company | Address | Phone | Email
Lochan Verma | Qualcomm |  |  | lverma@qti.qualcomm.com
George Cherian |  |  |  | gcherian@qti.qualcomm.com
Solomon Trainin |  |  |  | strainin@qti.qualcomm.com
Assaf Kasher |  |  |  | akasher@qti.qualcomm.com
Djordje Tujkovic | Facebook |  |  | djordjet@fb.com
Payam Torab |  |  |  | ptorab@fb.com
Carlos Cordeiro | Intel |  |  | Carlos.cordeiro@intel.com

## Slide 2: Outline
BRP (Beam Refinement Protocol) is a request and response process
  The response frame to a BRP request frame is a BRP response frame (carrying either feedback or a TRN field)
  Response shall be transmitted > SIFS (3 us) and <BRPIFS (40 us)
  Response frame may also contain a request for BRP request frame
The BRP frame exchange needs to be adapted to suite the TDD SP operation where bidirectional traffic is prohibited in a TDD Slot
  Sample draft text is provided

## Slide 3: Example Draft Text for non-AP and non-PCP STA
A non-AP and non-PCP STA operating in an SP with TDD channel access (see 10.36.6.2.2 (SP with TDD Channel Access)) on receiving beam refinement request shall transmit a beam refinement response, starting at the earliest occurring TDD slot the non-AP and non-PCP STA is assigned to, with access permission of the TDD slot set to simplex RX TDD slot, and with slot category of the TDD slot set to Basic TDD slot, as indicated in the TDD Slot Schedule element (see 9.4.2.268).

## Slide 4: Example Draft Text for DMG AP and PCP
A DMG AP or PCP operating in an SP with TDD channel access (see 10.36.6.2.2 (SP with TDD Channel Access)) that receives from a non-AP and non-PCP STA, a beam refinement request shall transmit a beam refinement response, starting at the earliest occurring TDD slot the non-AP and non-PCP STA is assigned to, with access permission of the TDD slot set to simplex TX TDD slot, and with slot category of the TDD slot set to Basic TDD slot, as indicated in the TDD Slot Schedule element (see 9.4.2.268).

## Slide 5: SP #1
Do you agree that in TDD SP operation the beam refinement response to a beam refinement request shall be transmitted at the start of the earliest occurring TDD Slot that allows for its transmission
  NOTE: This is introduced to prohibit bi-directional exchange of BRP request and BRP response frames in a Basic TDD Slot
Y : N : A