## Slide 1: Starting Time Indication of WUR Beacon
Date: 2018-01-14
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Daniel F Bravo |  |  |  | 
Noam Ginsburg |  |  |  | 
Robert Stacey |  |  |  | 

## Slide 2: Abstract
We have agreed to indicate WUR Beacon in WUR Mode element from AP [1]
For WUR non-AP STA to know the Target Wake-up Beacon Transmission Time (TWBTT), we discuss how to indicate one TWBTT.

## Slide 3: Method used by the PCR Beacon
For PCR Beacon, TSF 0 is one TBTT
For STBC Beacon, the TBTT is offset by half of the beacon interval
The beacon interval of PCR Beacon and STBC Beacon is the same.

## Slide 4: Consideration for WUR Beacon
WUR Beacon interval is likely to be much longer than PCR Beacon interval
  Except a maximum indicated value, there is no restriction on the WUR Beacon interval announced by the AP
If TSF 0 is one TWBTT, then AP may schedule WUR Beacon and Beacon at the same time
  This can be argued to be acceptable or not acceptable
To separate TBTT, STBC TBTT, and TWBTT, some additional restriction is required
  Ex the relation of Beacon interval on PCR and WUR, the fixed offset of TWBTT
We think we should leave the scheduling problem to the AP and should not mandate more and more rules, which may create problems in the future

## Slide 5: Proposal
We propose that AP indicates the offset of Target Wake-up radio Beacon Transmission Time (TWBTT) in WUR Mode element, which is the TSF time of the first TWBTT
  AP has full flexibility to decide TWBTT based on whatever criteria that exists now or may come in the future
  No additional rule on setting WUR Beacon interval

## Slide 6: Conclusion
We propose to let AP indicate the starting time of TWBTT

## Slide 7: Straw Poll
Do you support that AP indicates the offset of Target Wake-up radio Beacon Transmission Time (TWBTT) in WUR Mode element, which is the TSF time of the first TWBTT?

## Slide 8: Reference
[1] 11-17-0575-08 Spec Framework