## Slide 1: 60GHz Propagation Analysis For Micro Hotspot Services in Stadium
Authors:
Date: 2018-01-17

## Slide 2: Abstract
This contribution proposes a channel model for Micro Hotspot Access scenario in the stadium considering the reflected paths from surrounding spectators

## Slide 3: Introduction
Improvement of communication performance under dense user environment such as stadium
This contribution
  Provide information propagation characteristics for Hotspot access in stadium
  Multipath analysis caused by surrounding spectators

## Slide 4: MMW hotspot scenario in stadium
High gain antennas create a very small hotspot in MMW

## Slide 5: Multipath probability caused by spectators
If a spot includes plural seats within the service area, multipath reflection may be caused by the spectators.
->To identify the strength of reflection also measured and analyzed.
Y. Ohashi, et al, “Basic Analysis of Multipath Characteristics for Millimeterwave Wireless Communication in Dence User Environment”, IEICE Tech. Report, Electronics Simulations Technology(EST), Vol.115, No.434, EST2015-114, pp.147-152 (In Japanese)

## Slide 6
Propagation Measurement

## Slide 7: MMW Propagation Measurement System
Frequency: 57.01-65.99GHz
Power: 10 dBm
Tx/Rx antennas are extended by RoF
Dynamic Range: >100dB@100Hz IF BW
Range Resolution: 3.3 cm
One path two port Measurement: S11 & S21

## Slide 8: System Installation in Suita Stadium

## Slide 9: Distance Calculation for propagation
S21 measurements provide frequency response between Tx and Rx antennas.
S21 responses are transformed from frequency to time domain response.
The distance of propagation path is calculated by multiplying the speed of light to time response.
IFFT x c

## Slide 10: Distribution of propagation distance and received power
Distance to the Seats
Received Power

## Slide 11
Path Loss Analysis

## Slide 12: Path loss calculation
All of the data shows the strong received power of direct path.
Peak values of received power are compensated by the directivity of antenna and attenuation for calibration
Measured results are plotted according to the position of the seats
Theoretical propagation losses are also calculated to compare to the measured results.

## Slide 13: Measured antenna directivity and gain
Tx Antenna Gain
Rx Antenna Gain

## Slide 14: Path loss calculation results
Measured results show slightly higher path loss than theoretical values.
-> We can assume the free space propagation
Path loss at the seats

## Slide 15
Multipath Analysis

## Slide 16: Influence of spectators
Measurement without Spectators
Measurement with Spectators
(Standing or Sitting)

## Slide 17: Multipath measured by received power beneath transmitter (Seat #A12-18-7)
Direct Path
Reflection from Receiver Box
Reflection from the Cart

## Slide 18: Multipath measured by received power at the edge of the block (Seat #A12-18-1)
Direct Path
Reflection from Receiver Box
Reflection from Spectators

## Slide 19: Summary
MMW propagation characteristics in the stadium were investigated.
MMW propagation measurement system with RoF was developed.
Field test results predict:
  The propagation condition in the stadium between ceiling and seats is complete LOS.
  Surrounding spectators won’t affect the propagation between the ceiling and seats.
The micro hotspot in the stadium is established without any influence of the surrounding spectators

## Slide 20: Strawpoll 1
Do you think that a micro hotspot service would be prospective market of TGay?
Yes 32
No 0
Abstain 4

## Slide 21: Strawpoll 2
Do you support to incorporate an article of this stadium propagation measurement to TGay channel model document?
Yes 21
No 0
Abstain 15

## Slide 22: References
[1] Y. Ohashi, et al, “Basic Analysis of Multipath Characteristics for Millimeterwave Wireless Communication in Dence User Environment”, IEICE Tech. Report, Electronics Simulations Technology(EST), Vol.115, No.434, EST2015-114, pp.147-152 (In Japanese)
[2] Naruto Yonemoto, et al., “MMW Remote Antenna System of Vector Network Analyzer for Propagation Measurement in Stadium”, Proceedings on 2017 IEEE Conference on Antenna Measurements & Applications, TB3.3