## Slide 1: WUR Discovery Frame
Date: 2018-01-10
Authors:

## Slide 2: Abstract
Many contributions have discussed the content of the WUR Discovery frame as summarized in [1].
We attempt to provide a flexible structure for the WUR Discovery frame that accommodates various deployment scenarios.

## Slide 3: WUR Discovery frame content (1/3)
Candidate Contents of WUR Discovery frame:
Transmitter ID [1] / APID [4]
  Identifier of the AP transmitting the WUR Discovery frame
PCR Channel Information [1], [4], [5], [6]
  Identifies the Primary 20 MHz channel used by the AP for PCR.
(Short/Compressed) SSID [4], [5], [6]
  Identifies the SSID represented by the AP.
(Partial) BSSID [6]
  Identifies the AP’s BSS.
(Partial) HESSID [4]
  Identifies the Homogenous ESS that the AP belongs to.
BSS Capability/BSS Load information [6]
  AP’s Capability/Current BSS Load.
Others
  TBD.

## Slide 4: WUR Discovery frame content (2/3)
Transmitter ID/APID and (Partial) BSSID helps to identify the AP and we think at least one should always be present in the WUR Discovery frame.
  If the Transmitter ID is based on the AP’s (Partial BSSID), a separate (Partial) BSSID field is not necessary.

## Slide 5: WUR Discovery frame content (3/3)
The rest [2, 3, 5, 6] help in selecting candidate AP for roaming/association and their respective usefulness to STAs may depend on the deployment scenarios:
  In controlled deployments such as an enterprise network, a STA may already have access to comprehensive information about neighboring APs/networks (e.g. through 802.11ai Reduced Neighbor Report [3] or through Neighbor Report [4]):
    BSSID, PCR Channel Information, HESSID, SSID
    - In such deployments, WUR Discovery frame may carry minimal information.
  However in other deployments such as hotspots in a mall, a STA may not have access to information about neighboring APs/networks.
    In such deployments, WUR Discovery frame may have to carry more information.
  In deployments that are purely for ultra-low power scan, AP’s transmitter ID may be enough.
Summary: the content of the WUR Discovery frame depends on the deployment scenarios; we think that AP should have flexibility to decide the content.

## Slide 6: Proposal
AP decides the content of the WUR Discovery frame based on deployment scenario.
Bitmap Indicates the presence of sub-fields in the Frame Body field
Carries the AP’s Transmit ID
AP’s Transmit ID is always included in the Address field.
Content of the Frame Body field is flexible and presence of sub-fields is indicated by a bitmap in the TD Control field.
Example content of Frame Body field when all bits in the bitmap are set to 1.

## Slide 7: Summary
In this presentation we proposed:
A flexible structure for the WUR Discovery frame that accommodates various deployment scenarios.
AP decides the sub-fields to be included in the Frame body field of WUR Discovery frames.
The Address field of WUR Discovery frames carry the AP’s Transmit ID.

## Slide 8: Straw Poll 1
Do you agree that the content of the Frame Body field of WUR Discovery frame should be flexible and AP decides the sub-fields to be included in the Frame body field of WUR Discovery frames?
Y/N/A

## Slide 9: Straw Poll 2
Do you agree that a bitmap in the TD Control field of WUR Discovery frame indicates the presence of sub-fields of the Frame Body field?
Y/N/A

## Slide 10: Straw Poll 3
Do you agree that the Address field of WUR Discovery frame carries the AP’s Transmit ID?
Y/N/A

## Slide 11: References
[1] IEEE 802.11-17/1608r6 - Update on WUR discovery frame for smart scanning
[2] IEEE 802.11-17/0575r08 - 802.11ba specification framework
[3] IEEE 802.11-17/ 1644r1 - Further consideration on smart scanning usage model
[4] IEEE 802.11-17/1681r0 - BSS scanning through low power radio
[5] IEEE 802.11-17/1619r1 - Consideration on WUR frame for fast scanning
[6] IEEE 802.11-17/1641r0 - WUR frame format for smart scanning