## Slide 1: 60GHz Direction Measurement SFD text
Date: 2018-01-10
Authors:

## Slide 2: Abstract
[place presentation abstract text here]

## Slide 3: Introduction
This presentation proposes the changes required to the SFD to enable angle of arrival and angle of departure measurement for location in 60GHz.

## Slide 4: What are the changes need in the draft
To enable 60GHz AOA and AOD measurement we need the following changes:
  Capability exchange
    AOA, AOD capabilities as transmitter and receiver.
    Measuring FTM at the end of the packet (both transmitter and receiver)
    AOD feedback types
  Parameters exchange
    Length of training fields
      For FTM
      For AOA
      For AOD
    AOA or AOD in each direction
    Density of direction measurement in a burst
  Packet format modification
    Addition Of training field to FTM frames (Standard 11ad/11ay feature)
  Feedback
    AOA and Accuracy results
    Feedback need for AOD calculations (similar to feedback used today for BRP packets)

## Slide 5: Capability Exchange
We need capability exchange for the following:
  AOA measurement – as transmitter and receiver
  AOD measurement – as transmitter and receiver
  AOD feedback capabilities
    Best TRN subfield
    Channel measurement feedback
We propose to add these set of capabilities as an extended capability to the EDMG extended capabilities element

## Slide 6: Capabilities Element
This can be a separate capability element or a sub-element of an existing capabilities set.
  AOA TX capability indicates support for AOA TX – ability to add RX TRN field
  AOA RX capability indicates support for AOA RX – ability to measure RX TRN field and estimate AOA
  AOD TX capability indicates support for AOA TX – ability to transmit TX TRN field for AOA estimation
  AOD RX capability indicates support for AOA RX – ability to measure TX TRN field for AOD estimation
  AOD Channel Measurement Feedback – ability to measure and send channel feedback information as in DMG channel measurement feedback element.

## Slide 7: Protocol
Parameters are exchanged in the initial FTM request
Remain constant until changed.
AOD may be sent not in the immediately following FTM measurement

## Slide 8: Parameters Exchange
Initiator Request may ask for
  AOA on FTM
  AOD on FTM
  AOA on ACK
  AOD on ACK
Parameters:
  Number of TRN subfields
  AOA measurement density
Assumption:
  The request of the initiator must be obeyed by the responder if it has published these capability
  The responder requests for TRN subfields and for AOA measurement density (assuming it is the AP)

## Slide 9: Direction Measurement Parameters Element
To be added to iFTM request and iFTM measurement frames
Fields:
  UL AOA request, DL AOA request, UL AOD request, DL AOD request: request for Angel of Arrival, Angle of Departure in uplink (ACK) and downlink (FTM).
  L-RX, TRN-M, TRN-P are the number of TRN-Units (DMG) and TRN-Units construction (EDMG). These parameters are requests from the other device for AOA training.
  Direction measurement Density: in next slide

## Slide 10: Direction Measurement Parameters element
The AOA Density is determined by the AP (responder),
  This parameter in the responder (AP) overrides the same parameter in initiator
  It can take the values:
    Only first exchange in burst
    Every 1, 2, 4, 8 measurement in burst.
  This parameter is needed because of the additional length needed for angle measurement
    Under default parameter, every 6 AWV measurements require 3.5usec, while transferring 100bytes require 4usec.
    Calculation of AOA may be expensive (compared to FTM).

## Slide 11: AOA results
AOA (in earth coordinates), Degrees
  Includes azimuth and elevation
  Other formats possible
AOA accuracy (estimate)
AOD response
  Best sector
  Channel measurement feedback
An element added to the FTM response
Channel Measurement feedback as a different element.

## Slide 12: AOA results element
The AOA results are in deg/4 accuracy (0-360°)
Accuracy results are in deg/4 accuracy

## Slide 13: Strawpoll
Do you agree to add to the SFD:
  The capabilities element as defined in slide 6
  The measurement parameters as defined in slide 9
  The AOA results element as defined in slide 12

## Slide 15: References