## Slide 1: Data transmission detail in WUR mode
Date: 2018-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have addressed data transmission method in WUR mode[1][2][3]
  Basic operation is defined in our current SFD, however, we may need more detail about it
We will focus on data transmission detail when we apply existing power saving features

## Slide 3: WUR Mode
Once a WUR STA finished WUR mode signaling to entering WUR mode, the WUR STA enters to WUR mode
  If PCR is OFF and WUR is ON in WUR mode, we will call it “WUR-PM Mode”
    A WUR STA waits for WUP
  If PCR is ON and WUR is OF in WUR mode, we will call it “WUR-Active Mode”
    After reception of WUP, a WUR STA will receive DL data from an AP
    A WUR STA will return to WUR-PM mode after finishing data reception

## Slide 4: Power Save Poll
When PSP is applied, the WUR STA has to transmit PS-Poll frame to solicit DL Data after WUP reception
  If the WUR STA receives the DL data frame with More Data set to 0, it will return to WUR-PM mode without any signaling

## Slide 5: PSP
If the WUR STA receives the DL data frame with More Data set to 1, there are unclearness in WUR STA’s next operation
  We may have two options in this case
Option 1
  WUR STA will return to WUR-PM mode and wait for WUP from the AP for next DL Data

## Slide 6: PSP
Option 2
  WUR STA will not return to WUR-PM mode and transmits PS-Poll frame for next DL Data
  WUR STA can return to WUR-PM mode only after finishing all DL data reception
We prefer option 2 because of transition latency and overhead

## Slide 7: Power Save Mode
When PSM is applied, the WUR STA has to transmit QoS Null frame with PM bit set to 0 to solicit DL Data
  If the WUR STA receives the DL data frame with MD set to 0, it will transmit QoS Null frame with PM bit set 1
  And then it will return to WUR-PM mode after receiving ACK frame

## Slide 8: PSM
If the WUR STA receives the DL data frame with MD set to 1, WUR STA’s next operation is clear in PSM case
  The AP will transmit DL data frames consecutively until receiving QoS Null frame with PM bit set to 1

## Slide 9: Unscheduled Automatic Power Save Delivery
When U-APSD is applied, the WUR STA has to transmit MPDU with specific access category to solicit corresponding DL Data
  If the WUR STA receives the DL data frame with MD set to 0 and End Of Service Period(EOSP) set to 1, it will return to WUR-PM mode after transmitting ACK frame

## Slide 10: U-APSD
If the WUR STA receives the DL data frame with MD set to 1 and EOSP set to 0, it just wait for receiving DL data frame with EOSP set to 1
  Only after receiving all remaining DL data, it can return to WUR-PM mode

## Slide 11: U-APSD
If the WUR STA receives the DL data frame with MD set to 1 and EOSP set to 1, it shall transmit MPDU with next AC to solicit remaining DL Data
  If the WUR STA receives the DL data frame with MD set to 0 and End Of Service Period(EOSP) set to 1, it will return to WUR-PM mode after transmitting ACK frame

## Slide 12: Target Wake Time
When TWT is applied, we have two options
  Option 1: WUP is transmitted in TWT service period
    WUR operation is relatively easier but TWT SP can be wasted
    If transition delay is very short and PER of WUP is very low, case 1 will be more preferable
  Option 2: WUP is transmitted before TWT SP
    We can utilize TWT SP more efficient but WUR operation can be complex
    If transition delay is long or PER of WUP is high, case 2 is preferable
  We prefer option 2

## Slide 13: TWT
Case 1: The WUR STA has to transmit QoS Null frame to solicit DL Data in TWT SP
  If the WUR STA receives the DL data frame with MD set to 0, it will return to WUR-PM mode after receiving ACK frame or TWT SP

## Slide 14: TWT
Case 2: If WUP is transmitted before TWT SP, we have two sub-options
  Sub-option 1: WUR STA responses by QoS Null frame in TWT SP
    WUR STA has to wait until TWT SP, but QoS Null frame is protected
    If the WUR STA missed WUP, TWT SP will be wasted
    Retransmission and response rule for WUP should be modified
  Sub-option 2: WUR STA responses by QoS Null frame before TWT SP
    WUR STA can response immediately
    Even though the WUR STA missed WUP, AP can retransmit WUP before TWT SP
    We don’t have to modify retransmission and response rule for WUP
  We prefer sub-option 2

## Slide 15: TWT
Sub-option 1
Sub-option 2

## Slide 16: TWT
If the WUR STA receives the DL data frame with MD set to 1 and remaining TWT SP is enough, WUR STA’s next operation is clear in TWT case
  The AP will transmit DL data frames consecutively
  WUR STA can return to WUR-PM mode only after finishing DL data reception

## Slide 17: TWT
If the WUR STA receives the DL data frame with MD set to 1 and remaining TWT SP is not enough, we have to decide WUR STA’s operation
Option 1
  WUR STA will return to WUR-PM mode after current TWT SP until next TWT SP

## Slide 18: TWT
Option 2
  WUR STA will not return to WUR-PM mode and wait for next TWT SP
  WUR STA can operate in PCR-doze state between TWT SPs
We prefer option 2 because of transition latency and mode mismatch problem

## Slide 19: Summary
We have analyzed detailed data transmission method when we applied existing power saving features
Through our analysis, we propose the followings
  When an AP transmitted data frame with More Data set to 1 to a WUR STA, it shall not transmit wake up frame to the WUR STA until the WUR STA receives data frame with More Data set to 0
  When a WUR STA received data frame with More Data set to 1, it shall not operate in PCR OFF and WUR ON, until the WUR STA receives data frame with More Data set to 0

## Slide 20: Reference
[1] 1657r7: MAC operation of WUR
[2] 630r0: SFD Proposal on Retransmission
[3] 379r4: SFD MAC proposal

## Slide 21: Straw poll
Do you agree to add following text in SFD?
  When an AP transmitted data frame with More Data set to 1 to a WUR STA, it shall not transmit wake up frame to the WUR STA until the WUR STA receives data frame with More Data set to 0
  When a WUR STA received data frame with More Data set to 1, it shall not operate in PCR OFF and WUR ON, until the WUR STA receives data frame with More Data set to 0