## Slide 1: Issues In Multicast Wake Up
Date: 2018-01-15
Authors:

## Slide 2
Abstract
In this contribution, we look at the issues of waking up STAs using a multicast wake up packet and propose to include a multicast counter in multicast wake up packets.

## Slide 3: Introduction
802.11ba agreed to use multicast wake up packets to wake up multiple STAs [1]
  “IEEE 802.11ba shall define a mechanism to wake up multiple WUR mode STAs (e.g., multiuser wake-up frame)”
  “GID is the GROUP ID provided by the AP and identifies one or more WUR STAs”
In order to wake up a group of STAs, a multicast packet may be sent addressing these STAs
  Possibly identified by a GID
  And/or possibly identified by a list of WIDs
In this contribution, we evaluate these addressing schemes for their benefit and cost

## Slide 4: Addressing Options in Multicast Wake Up Packet (1)
Three types of Wake Up Packets seem to be allowed in 802.11ba [1]
  Unicast: addressed by WID
  Broadcast: addressed by TXID
  Multicast: addressing seems to be a bit unclear
Multicast wake up packet can be addressed in several ways
  Option 1: Addressed by GID
  Option 2: Addressed by broadcast address and a list of individual WIDs
  Option 3: Addressed by GID and a list of individual WIDs
  Option 4: Addressed by GID in the initial multicast WUP; and addressed by GID and list of individual WIDs in retransmissions

## Slide 5: Addressing Options in Multicast Wake Up Packet (2)
Option 1: Addressed by GID
  Provides the shortest WUR packet format with predicable length
  Needs WUR configuration for GID using PCR
    Not expecting to be a big burden
  May wake up a STA multiple times
    E.g., when AP detects that some STAs associated with a GID that have not been woken up yet and retransmits the multicast WUP with GID
    Other identifiers may need to be added
Option 2: Addressed by Broadcast address (could be a special WID) and a list of individual WIDs
  May result into a long WUR packet given the low data rates
  Needs WUR configuration for WIDs using PCR
  Will not unnecessarily wake up any STAs

## Slide 6: Addressing Options in Multicast Wake Up Packet (3)
Option 3: Addressed by GID and a list of individual WIDs
  May result in a long WUR packet given the low data rates
  Needs WUR configuration for GIDs and WIDs using PCR
    not expecting to be a big burden
  Will not unnecessarily wake up any STAs
Option 4: Addressed by GID in the initial multicast WUP; and addressed by GID and list of individual WIDs in retransmission
  Hybrid approach
  Needs indicators to differentiate initial or retransmission of multicast WUP
  Length of multicast packet can vary significantly depending on the number of WIDs included
  Needs WUR configuration for GIDs and WIDs using PCR
  Will not unnecessarily wake up any STAs

## Slide 7: Addressing Options in Multicast Wake Up Packet (4)
Option 1 (multicast WUP addressed by GID) seems to minimize WUP medium time and provide predictable length of the WUP
  Needs to make sure that a multicast WUP doesn’t wake up a STA multiple times
Including a multicast counter field in a multicast WUP may solve the issue of waking up a STA multiple times
  Similar to broadcast WUP containing a sequence number [2] and BSS Parameter Update Counter [1]
  A WUR STA wakes up after receiving a multicast WUP addressed to a GID that it is associated with and if the multicast counter contains a value that is different
  A WUR STA ignores a multicast WUP if it is addressed to a GID that it is associated with and if the multicast counter contains the same value as that in a previous multicast WUP that has awaken it
  Additional overhead should be minimal

## Slide 8: Conclusion
We evaluated four different addressing options for multicast WUP
  Option 1: Addressed by GID
  Option 2: Addressed by broadcast address and a list of individual WIDs
  Option 3: Addressed by GID and a list of individual WIDs
  Option 4: Addressed by GID in the initial multicast WUP; and addressed by GID and list of individual WIDs in retransmissions
If Option 1 is chosen, then a multicast counter may be needed to prevent STAs from being woken up unnecessarily

## Slide 9
References
[1] 11-17/575r8, 802.11ba Specification Framework Document, Dec. 2017
[2] 11-17/1356r3, PS Operation for Duty Cycle STAs follow-up, Nov, 2017

## Slide 10: SP 1
Which addressing option do you prefer for a multicast WUP:
  Option 1: Addressed by GID
  Option 2: Addressed by broadcast address and a list of individual WIDs
  Option 3: Addressed by GID and a list of individual WIDs
  Option 4: Addressed by GID in the initial multicast WUP; and addressed by GID and list of individual WIDs in retransmissions

## Slide 11: SP 2
Do you agree that:
  A multicast counter field should be added to the multicast WUP if addressing Option 1 is chosen?