## Slide 1: Wake Up Frame to Indicate Group Addressed Frames Transmission
Date: 2018-01-16
Authors:

## Slide 2: Abstract
Currently, the wake-up frame can indicate that AP will transmit group addressed frames. Details, how the Wake Up frame indicates buffered group addressed frames are TBD.
This submission discusses on the wake up frame type selection and options to for wake-up frame to indicate buffered group addressed frames.

## Slide 3: Wake Up Receiver Challenges to Receive Group Addressed Frames
WLAN transmits all group addressed frames after a DTIM Beacon
  STAs in power save mode wake up to receive DTIM Beacons and group addressed frames
STAs in WUR Mode should also to receive group addressed frames after the DTIM beacon
  If STAs in WUR mode wake-up to receive DTIM beacon and group addressed frames, their stand-by power consumption is similar to STAs using legacy power save
To avoid unnecessary wake-ups to receive DTIM Beacons, the AP should transmit Wake-up frame to indicate whether it transmits group addressed frames

## Slide 4: Example of Wake Up frame and Group Addressed Frames Transmission
BroadcastWake-up frame
DTIM Beacon frame
Group addressed frames
Time
Time
Wake-up radio:
Primary communication radio (PCR):
PCR activation delay
Time
DTIM
Beacon
DTIM
Beacon
DTIM
Beacon

## Slide 5: Wake Up Frame Indicating Group Addressed Frames Transmission
The wake-up frame should indicate whether AP will transmit group addressed frames
  TIM bit 0 can indicate whether AP transmits group addressed frames. PCR activation can be skipped, if no group addressed frames are transmitted
STAs in WUR mode benefit if wake-up frames indicate the transmitted group addresses more precisely
  For instance, a STA may desire to only receive group addressed frames belonging to a service discovery protocol

## Slide 6: How to Select the Group Addresses that are indicated in wake-up frame?
The AP may not know from which group addresses the STAs are interested to receive frames
  STAs should be able to request the group addresses that are indicated in wake-up
The size of the wake-up frame is limited
  The AP should have means to indicate multiple group addresses through a single indicator in a broadcast wake-up frame
  The AP should select the group addresses indicated in a wake-up frame

## Slide 7: Different Wake Up Frame Types
Individual wake up frame
  AP wakes up a single STA
Multi user wake up frame
  AP wakes up multiple STAs
Multicast wake up frame
  AP indicates which multicast and broadcast addressed MPDUs are transmitted
Broadcast wake up frame
  AP indicates updated operating parameters and/or transmission of MMPDU targeted for all STAs

## Slide 8: Considerations, individual/ MU wake-up frame to indicate group addressed frames
802.11ba has discussed whether MU wake-up Frame, i.e. individual wake-up indication and Multicast wake-up frame can be combined
  If both indications are done through the same frame, the receiver needs to know whether PCR receives only group addressed frames or frames including individually addressed frames, see annex
  AP needs to process group addresses of obtained frames and detect which STAs desire to receive the frame
  If AP has multiple associated STAs, multiple individual/ MU wake-up frames may create signaling overhead to WUR and cause transmission delays

## Slide 9: Using individual wake-up frame to indicate group addressed frame transmission
If AP sends individual wake-up to a STA, the AP performs following operations to indicate group addressed frame transmission:
  AP detects which group addressed frame is received from Internet
  AP checks which STAs desire to receive the group addressed frame
  AP sends (individual/MU) wake-up frame(s) for all STAs desiring to receive the group addressed frame
    AP may need to send multiple wake-up frames if many STAs desire to receive the group addressed frames
    All wake-up frames should be transmitted before PCR transmits the group addressed frames

## Slide 10: Using multicast wake-up frame to indicate transmission of group addressed frame
If AP sends multicast wake-up frame for group addressed frames
  The AP detect which group addressed frame is received from Internet
  AP checks which multicast wake-up frame is used for the group address
  AP sends a multicast wake-up frame before the transmission of group addressed frame

## Slide 11: Wake-Up Frame Type Selection to Indicate Group Addressed frames Transmission
A multicast wake-up frame is needed to timely indicate transmission of group addressed frames to multiple STAs
If Individual wake-up frame are used to indicate also group addressed frames transmission, the frames should contain a field to indicate if PCR transmits only group addressed frames
  Receivers need to know whether AP expects them to send UL frame before AP sends buffered DL frames

## Slide 12: Summary
The group addressed frames reception causes many PCR activations to STA in WUR mode
  Group addressed frames reception increases severely power consumption
To meet the WUR power save goals, a multicast wake-up frame should be transmitted before DTIM beacon:
  Multicast wake-up frame indicates the group addresses that will be transmitted after DTIM beacon
Non-AP STAs should request the group addresses indicated in the wake-up frame

## Slide 13: Annex, Typical Transmission of a Individual and Group Addressed Frame
Group addressed frames are transmitted after DTIM Beacon:
  Transmitted one time at robust transmission rate; no acknowledgements or retransmissions
  AP just sends the frame after DTIM Beacon; STA does not transmit any indication
Individual addressed frames may be transmitted at any time
  Transmitted at link specific transmission rate; acknowledgements and retransmissions are used
  AP requires an UL indication from a STA before it sends buffered DL data to power saving STAs

## Slide 14: Straw Poll 1
Do you agree to add to 802.11ba SFD:
A WUR STA may request the group addresses which transmission is indicated to the WUR STA in a wake-up frame.

## Slide 15: Straw Poll 2
Do you agree to add to 802.11ba SFD:
A WUR STA detects from a wake up frame whether AP transmits only group addresses frames, i.e. AP has no buffered individual frames for the WUR STA.