## Slide 1: Wake Up Frame to Indicate Group Addressed Frames Transmission
Date: 2018-01-16
Authors:

## Slide 2: Abstract
Currently, the wake-up frame can indicate that AP will transmit group addressed frames. Details, how the Wake Up frame indicates buffered group addressed frames are TBD.
This submission discusses on the wake up frame type selection and options to for wake-up frame to indicate buffered group addressed frames.

## Slide 3: Wake Up Receiver Challenges to Receive Group Addressed Frames
WLAN transmits all group addressed frames after a DTIM Beacon
  STAs in power save mode wake up to receive DTIM Beacons and group addressed frames
STAs in WUR Mode should also to receive group addressed frames after the DTIM beacon
  If STAs in WUR mode wake-up to receive DTIM beacon and group addressed frames, their stand-by power consumption is similar to STAs using legacy power save
To avoid unnecessary wake-ups to receive DTIM Beacons, the AP should transmit Wake-up frame to indicate whether it transmits group addressed frames

## Slide 4: Example of Wake Up frame and Group Addressed Frames Transmission
BroadcastWake-up frame
DTIM Beacon frame
Group addressed frames
Time
Time
Wake-up radio:
Primary communication radio (PCR):
PCR activation delay
Time
DTIM
Beacon
DTIM
Beacon
DTIM
Beacon

## Slide 5: Wake Up Frame Indicating Group Addressed Frames Transmission
The wake-up frame should indicate whether AP will transmit group addressed frames
  TIM bit 0 can indicate whether AP transmits group addressed frames. PCR activation can be skipped, if no group addressed frames are transmitted
STAs in WUR mode benefit if wake-up frames indicate the transmitted group addresses more precisely
  For instance, a STA may desire to only receive group addressed frames belonging to a service discovery protocol

## Slide 6: How to Select the Group Addresses that are indicated in wake-up frame?
The AP may not know from which group addresses the STAs are interested to receive frames
  STAs should be able to request the group addresses that are indicated in wake-up
The size of the wake-up frame is limited
  The AP should have means to indicate multiple group addresses through a single indicator in a broadcast wake-up frame
  The AP should select the group addresses indicated in a wake-up frame

## Slide 7: Summary
The group addressed frames reception causes many PCR activations to STA in WUR mode
  Group addressed frames reception increases severely power consumption
To meet the WUR power save goals, a multicast wake-up frame should be transmitted before DTIM beacon:
  Multicast wake-up frame indicates the group addresses that will be transmitted after DTIM beacon

## Slide 8: Straw Poll 1
Do you agree to add to 802.11ba SFD:
A WUR STA may request the group addresses which transmission is indicated to the WUR STA in a wake-up frame.