## Slide 1: PCR service period in WUR Mode
Date: 2018-01-15
Authors:

## Slide 2: Introduction
According to the current SFD, when a non-AP STA enters WUR Mode
  The existing negotiated service period between AP and non-AP STA for the non-AP STA’s PCR schedule is suspended
    AP and STA maintains all negotiated parameters corresponding to the PCR schedule
  The service period suspension ensures WUR STA to have long-term sleep
The detail of how AP and STA suspend the service period hasn’t been discussed yet
In this contribution:
  discussing possible approaches of PCR service period suspension
  proposing to allow WUR STA to use service period in awake state

## Slide 3: Possible approaches for service period suspension
1) Postpone or cancel all scheduled SPs during WUR Mode
  Service period is not present until the STA exits WUR Mode
    Disabling all operations regarding the scheduling mechanism
  Upon Exit WUR Mode, AP and STA should reschedule the SP
2) Define behavior for AP and STA regarding SP suspension
  Allow to skip default behaviors for each SP
    Periodic wake-up of non-AP STA
    Scheduled transmission of AP
  Any scheduled service will not be provided during the service period
  No need to postpone or reschedule the service period
Option 1)
Option 2)

## Slide 4: Further discussion on option 2)
In terms of the operation of AP and STA, Option 1) and option 2) have the same effect
  STA could stay in doze state for a long time in WUR Mode
  AP doesn’t have to transmit unnecessary frames
Using option 2), however, the negotiated service period schedule could remain as it is
  AP and STA maintains all parameters of the negotiated PCR schedule in WUR Mode
Therefore, it is possible to allow STA to use the negotiated service period when it enters awake state

## Slide 5: TWT example (1)
According to the 11ax spec,
  STA may choose to send an awake indication if the STA wants to use a TWT SP
  If AP has received any awake indication from the STA, it shall transmit buffered BUs until the end of the TWT SP
If we apply this rule to WUR STA,
  In DL case, PCR frame transmission in response to WUP could be the awake indication for a TWT SP
  Also, STA could transmit an awake indication any time to use TWT SP for UL transmission

## Slide 6: TWT example (2)
Using TWT SP enables WUR STA:
  More efficient BU retrieving is possible compare to PSP or U-APSD
    During SP, STA could use enhanced BU retrieving mechanism overriding PSP or U-APSD
  Simple and efficient channel access for STA
    Channel contention can be reduced during TWT SP
    Using UL MU operation, STA might not access the channel
  TWT offers various options for SP negotiation
DL transmission
UL transmission

## Slide 7: Proposal
We propose to allow WUR STA to use the negotiated PCR schedule in the awake state
Advantages of the proposal
  Allow WUR STA to have more options on its PCR operation
  We don’t need to define how to suspend or resume PCR schedule
  Leave room for future extension
    11ba can be combined with future 802.11 standards with advanced scheduling mechanism

## Slide 8: Strawpoll
Do you support the following?
If a non-AP STA is in WUR mode, then:
  The non-AP STA is allowed to use the negotiated PCR service period in the awake state