## Slide 1: Response type indication in unicast WUR frame
Date: 2018-01-18
Authors:

## Slide 2: Introduction
The following MAC header structure of WUR frame has been agreed
  Fixed size
    Frame Control: 8 bits/Address: 12 bits/TD Control: 12 bits
  TD Control field contains type dependent control information
    The TD Control field of WUR Beacon contains the partial TSF
The use of TD control field in unicast/multicast WUF needs to be defined
In this contribution, we propose to have response type indication in unicast wake-up frame
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | 8 | 12 | 12

## Slide 3: 1) Active/Passive response
A part of TD control field in unicast wake-up frame can be assigned for control information on the recipient STA’s wake-up behavior
1) Active/Passive response (1 bit)
  In order to finalize the wake-up operation, a successful PCR frame exchange is required
  If this bit is set (Active), the STA access the channel using EDCA to transmit a PCR frame after wake-up
  If this bit is not set (Passive), the STA waits for a frame from the AP that solicits a response frame
    E.g., Trigger frame, RTS
    Empowering the scheduling of the AP in busy network
    Decreasing the channel access burden of non-AP STA
      Low capabilities/low power sensor STAs
TD Control
Active /Passive
1bit

## Slide 4: 2) Proactive/Reactive wake-up
2) Proactive/Reactive wake-up (1 bit)
  If this bit is not set (Reactive), the STA wakes up its PCR immediately after wake-up frame reception
  If this bit is set (Proactive), the STA decides the timing of the wake-up
    In U-APSD, non-AP STA decides the timing for retrieving BU
      U-APSD is designed for constant rate bi-directional traffic
      If WUFs always require the non-AP STA to wake-up for U-APSD traffic, the power consumption of the STA will increase drastically
    Using this information
      The STA can keep track the buffer status of AP without wake-up
        No need to send U-APSD trigger periodically
      The STA can manage the traffic flow
TD Control
Proactive/Reactive
1bit
Active /Passive
1bit

## Slide 5: Summary
We have proposed to have response type indications in TD Control field
  Active/Passive response
  Proactive/Reactive wake-up
Having the proposed information, WUR could reflect various properties of different schemes and environments

## Slide 6: Strawpoll 1
Do you agree to have the following 1 bit indication in the TD Control field of unicast wake-up frame
  Active/Passive response
    Active: The non-AP STA accesses the channel using EDCA to transmit a PCR frame after wake-up
    Passive: The non-AP STA waits for a PCR frame from the AP that solicits a PCR response frame after wake-up

## Slide 7: Strawpoll 2
Do you agree to have the following 1 bit indication in the TD Control field of unicast wake-up frame
  Proactive/Reactive wake-up
    Proactive: The non-AP STA may not wake up its PCR immediately after the wake-up frame reception
    Reactive: The non-AP STA wakes up its PCR immediately after the wake-up frame reception