## Slide 1: TSF Synchronization through WUR Beacon
Date: 2018-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Partial TSF Time in Low Power SYNC
Synchronization time in SYNC is partial TSF time.
  STA and AP do synchronization per TSF time, e.g. MSBs not shown in SYNC frame are also used.
STA needs to set TSF time correctly per the partial TSF time in SYNC frame.
SYNC
Marvell Confidential
SYNC
SYNC
SYNC
SYNC
SYNC
Type+other Ctl Info
BSS Color
Partial TSF
FCS
SYNC
Bits:
8
12
12
8
e.g. TSF [0 to 11] or TSF[4 to 15]

## Slide 3: Wrong TSF Setting By 12-bit Timestamp
AP’s TSF and STA’s TSF may have different value because of clock draft.
Example 1:
  When a SYNC is transmitted, AP’s TSF time is the combination of most significant part, e.g. 52-bit X and least significant 12-bit FF0 where 12-bit FF0 is put in SYNC.
  When a STA receives the SYNC, the STA’s TSF time is the combination of most significant 52-bit X + 1 and least significant 12-bit FF0.
Example 2:
  When a SYNC is transmitted, AP’s TSF time is the combination of most significant part, e.g. 52-bit X+1 and least significant 12-bit 00F where 12-bit 00F is put in SYNC.
  When a STA receives the SYNC, the STA’s TSF time is the combination of most significant 52-bit X and least significant 12-bit 00F.

## Slide 4: TSF Synchronization Solution
An AP decides the SYNC Tx intervals per the following rules:
  The time draft of each STA between two received adjacent SYNC frames that the STA receives is less than ½ of maximal partial TSF time that SYNC can carry.
    The missed SYNC frames should be considered, e.g. when at most 5 continuous SYNC frames can be missed, the time draft within the total time of between 6 SYNC Tx intervals is considered.

## Slide 5: TSF Synchronization Solution
A STA follows the following rules (assume the 12-bit timestamp in SYNC is 12-bit LSB of TSF time. If SYNC carries LSB of TSF time with other definition, the following rules are changed accordingly, e.g. 12-bit timestamp in SYNC is TSF time[4:15]):
  For 52-bit MSB TSF time in STA:
    if 1), the most significant bit of 12-bit Timestamp and the most significant bit of the least significant 12-bit TSF time are different, 2), 12-bit Timestamp in SYNC is larger than least significant 12-bit TSF time in STA 3), 12-bit Timestamp - least significant 12-bit TSF time in STA is larger than 2^11, most significant 52-bit TSF time is decreased by 1.
    if 1), the most significant bit of 12-bit Timestamp and the most significant bit of the least significant 12-bit TSF time are different, 2), 12-bit Timestamp is smaller than least significant 12-bit TSF time in STA 3), least significant 12-bit TSF time in STA - 12-bit Timestamp is larger than 2^11, most significant 52-bit TSF time is increased by 1.
    For all other cases, most significant 52-bit TSF time doesn’t change.
  For 12-bit LSBTSF time in STA:
    The STA copies the 12-bit TSF time in SYNC to its related TSF LSB part.