## Slide 1: MMWave Distribution Network Discovery
Date: 2018-01-13
Name | Affiliation | Address | Phone | Email
Mohamed Abouelseoud | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4027 | Mohamed.Abouelseoud@sony.com
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 | +1-408-352-4405 | kazuyuki.Sakoda@sony.com

## Slide 2: Agenda
Introduction
Problem description
OOB discovery trigger: what is available in the spec?
Potential solution
Conclusion

## Slide 3: Introduction (1)
Small cell
Wi-Fi AP
Fiber PoP (cabinet)
  WTTH
  WTTB
Small cell
  WTTB
  WTTH
Wi-Fi-AP
Alternative: Wireless inhouse
  WTTB
RGW
Use case c) WiFi AP / SC
  Mesh WBH
fiber
Provider
Network
mmWave DN
mmWave link
Use case a) WTTH
Use case b) WTTB
802.11ay D1.0 introduces TDD mode to accommodate Distribution Network, and they look to be attractive even for consumer devices [2]
New STA onboarding to a Distribution Network is triggered by OOB signaling [3]

## Slide 4: Introduction (2)
Small cell
Wi-Fi AP
Fiber PoP (cabinet)
  WTTH
  WTTB
Small cell
  WTTB
  WTTH
Wi-Fi-AP
Alternative: Wireless inhouse
  WTTB
RGW
Use case c) WiFi AP / SC
  Mesh WBH
fiber
Provider
Network
mmWave DN
mmWave link
Use case a) WTTH
Use case b) WTTB
If we consider to adopt TDD mode to consumer devices, onboarding trigger procedure should be specified in the standard
TDD mode should also be applicable to use cases other than Usage Model 10 in [4]
This presentation introduces approach to a potential resolution to CID1771

## Slide 5: Problem description (1)
Fiber PoP (cabinet)
  WTTB
fiber
Provider
Network
mmWave DN
mmWave link
Controller
  STA-A starts transmitting TX SLS equivalent signals
  The New STA receives SSW from STA-A and respond to it
  After beam training procedure, STA-A and new STA starts association & authentication process
  STA-B repeats the same sequence as 4. and 5. above
According to [3], a new STA joining to an existing Distribution Network will take the following steps:
  System Admin scans Bar-code of the new STA and transfer the information using out-of-band (OOB) signals
  The message is transferred to DMG STAs nearby through a controller (for example, STA-A, STA-B)
STA A
STA B
New STA

## Slide 6: Problem description (2)
In the example in the previous slide, new STA, STA-A and STA-B need to understand the discovery trigger events
If we consider to apply TDD mode operation to consumer devices, discovery trigger event needs to be transferred among STAs using a standardized protocol
In other word, a proper discovery trigger signaling enables successful onboarding of a new STA to TDD mode network, even for consumer devices

## Slide 7: mmW discovery trigger: what is available in the spec (1)
802.11ad introduced Multi-Band operation
MB capability should allow off-60GHz signaling

## Slide 8: mmW discovery trigger: what is available in the spec (2)
Close look on Multi-Band operation
  Multi-band capable device can manage operation over more than 1 frequency band/channel
  MM-SME can share information among STAs in the same device
  RSNA security credentials can be shared among STAs in the same device
  FST can be set up if necessary
  OCT is available to carry 60GHz management messages via sub 6GHz

## Slide 9: mmW discovery trigger: what is available in the spec (3)
It looks like there are plenty of tools to enable 60GHz discovery trigger using 802.11 protocols, if we can assume DMG STA is Multi-Band capable

## Slide 10: Potential solution
Option 1:
  Define Public action frame exchange in sub-6GHz
  New STA transmits “Discovery Trigger Request Action” to neighboring STAs
  Neighboring STAs respond with “Discovery Trigger Response Action”, and kick the TX SLS equivalent signaling on the 60GHz channel
Option 2:
  Signal MB and 60GHz TDD capability via Beacon/Probe Response in sub-6GHz
  Use On-Channel Tunneling on the sub-6GHz channel to kick TX SLS equivalent signaling on the 60GHz
Option 3:
  Something else, there should be many other ways to make it happen

## Slide 11: Conclusion
Discovery trigger scheme for TDD mode distribution network should be defined in the standard
Use of Multi-Band capability looks to be easy and feasible solution
2 options to enable discovery triggering leveraging existing Multi-Band capability are presented
A solution to this problem will solve CID1771

## Slide 12: Straw poll (1)
Do you think additional signaling for discovery triggering is needed for the TDD mode described in [*] to support consumer devices?
  Yes
  No
  Don’t care
[*] IEEE 802.11-17/1321r0 “Features for mmW Distribution Network Use Case”, Djordje Tujkovic, et.al

## Slide 13: Straw poll (2)
Do you think the use of Multi-Band operation would be feasible approach for OOB discovery signaling?
  Yes
  No
  Don’t care

## Slide 14: References
[1] Draft P802.11ay D1.0
[2] IEEE 802.11-18/xxxr0, “Distribution network use case for consumer devices”, Kazuyuki Sakoda, et.al.
[3] IEEE 802.11-17/1321r0 “Features for mmW Distribution Network Use Case”, Djordje Tujkovic, et.al.
[4] IEEE 802.11-15/625r7 “IEEE 802.11 TGay Use Cases”, Rob Sun, et.al.

## Slide 15: Backup Discovery Trigger Action Frames

## Slide 16: Backup MB and 60GHz TDD Capability Signaling via Probe Response

## Slide 17: Backup Sub-6GHz On-Channel Tunneling

## Slide 18: Device Provisioning Protocol (DPP)
Wi-Fi Alliance defined protocol
Provides a secure method for on- and off-boarding devices with limited user interface on a Wi-Fi network.
AP discovery and STA scanning are beyond what DPP is offering
DPP
AP
New STA
Scanning
Authentication
Association