## Slide 1: TSPEC and Persistent Scheduling for HE STAs—CID 18555 Comment Resolution
Date: 2017-12-18
Name | Affiliation | Address | Phone | Email
Guoqing Li | Apple Inc. |  |  | Guoqing_li@apple.com

## Slide 2: Introduction
802.11ax is the first 802.11 standard that defined DL/UL OFDMA and UL MU MIMO, which enabled Wi-Fi to really transition into a scheduling-based system
  In highly congested environment, centralized scheduling tend to yield better performance than distributed contention-based operation
To make scheduling system really work well, the 11ax AP needs to have accurate and timely information about STAs’ traffic
  DL is less of a problem since DL buffer info is directly available to the AP
  UL buffer status is more challenging since it’s based on STA’s feedback
For this purpose, the 11ax standard has defined two types of UL buffer status reports
  BSR in HE Control field
  BSR in QoS control field
However, this may not be enough for delivering high QoS service in future Wi-F networks

## Slide 3: Problem Statement
First, the STA can only report current queue sizes in BSR, and thus AP cannot allocate resources for STA for any future traffics which may come very soon
Secondly, the STA may experience long delay to send out BSR
  BSR can be sent either in UL MU PPDU which is scheduled by the AP or in SU PPDU which is sent by STA through contention (EDCA)
  If it is sent out through contention, since 11ax AP will likely lower STA’s contention priority, these BSRs may experience long delays to send out
  If it is sent out through UL MU PPDU, it is not guaranteed that AP will schedule STA to transmit BSR in a timely manner
As a result, STA’s BSR may not be delivered to the AP in a timely manner, and as a consequence the AP’s resource allocations may not satisfy STA’s QoS requirements

## Slide 4: Problem Statement (cont.)
Thirdly, even with a given Buffer Status Report, AP does not know what kind of allocations is better for the STA
For example, the following two allocations will deplete the STA’s buffer for a given buffer status report but result in different latency and some lead to buffer overflow risks
BSR received

## Slide 5: Problem Statement (cont.)
If implemented, a STA may set up an individual TWT agreement with the AP to allow the AP to poll the STA from time to time
However, there are still a few issues with using TWT to satisfy the QoS requirements
  Firstly, TWT is an optional feature for a STA so not every STA will implement it
    We need a mechanism for AP to identify and try to satisfy a STA’s QoS even if TWT is not implemented/enabled
  TWT parameters may not be honored by the AP unless it’s a “demand” TWT request
    A STA may be put in a TWT schedule together with other STAs based on AP’s scheduling algorithm which result in different TWT parameters
    STA can negotiate with the AP to get a more desirable TWT schedule, however this takes time and is still not guaranteed
In addition, the problem described in previous slides still apply
  Given a BSR, an 11ax AP does not have the knowledge regarding what would be a better allocation for the STA’s application

## Slide 6: Gaps in 11ax
We need a mechanism to allow the STA that has persistent traffic to inform AP its QoS requirement and/or traffic characteristics to facilitate a persistent schedule set up or persistent BSR polling by the AP that will most likely satisfy the STA’s QoS requirement

## Slide 7: Information to be conveyed
Some Essential Information
  Data rate information/Packet size information
  Traffic burst interval and latency
  Symmetric traffic indication
  Time out value that allows the AP to terminate the persistent schedule automatically
With the average data rate and interval info, the AP can allocate resources to match STA’s traffic requirements
  Unlike HCCA, an 11ax AP defines STA’s transmission rate and transmission time in UL MU transmissions
  Therefore, an11ax AP can schedule UL allocations to exactly match the STA’s application data rate
Such information is mostly useful and mostly needed for isochronous traffic such as FaceTime and Wi-Fi calling
  When an isochronous applications is initiated, such info can be derived and delivered to the Wi-Fi radio to be sent out to the AP
With slight modification, TSPEC will contain all the information needed

## Slide 8: Spec Changes
Modify TSPEC and related text to simplify its use for HE STAs including
  Remove the association between TSPEC and traffic streams/HCCA/admission control
  Clarify that TSPEC is only used as a means to convey traffic/QoS information to HE AP without requiring HE AP to perform admission control, TS management, packet classification and many complex TS operation
Define a new Control ID to convey the most critical info as a more efficient and fast notification mechanism
  Any application changes such as video rate adaptation can be informed to HE APs quickly to be taken into account into the scheduling
Please see 11-18-182-CID related to TSPEC.docx for the detailed spec text

## Slide 9: Summary
To have a more guaranteed QoS performance for Isochronous applications, the STA needs to inform the AP some essential traffic and QoS info
The essential information include
  Traffic bursty internal/latency
  Traffic rate/packet size information
  Timeout value which allows persistent scheduling be automatically terminated when there is no traffic within this timeout value
  Symmetric traffic indication
We propose to use TSPEC to convey such essential information and also define a new Control ID for the A-Control field to carry some most critical info
  Please see 11-18-xx-D2.0 CR for CID 18555-TSPEC and Persistent scheduling.doc for the detailed spec text