## Slide 1: Secure SU and MU Ranging Measurement Procedure
Date: 2018-01-18
Authors:

## Slide 2: Introduction
In previous discussions we agree on the following:
  The HEz and VHTz FTM modes, the fields over which range measurements are performed shall be protected against a VHT/HE Type B adversary attack.
  For the purpose of PHY Security Mode, the field used for channel/ToA measurement shall not include any form of repetition in time domain or structure that is predictable.
In this submission we will review possibilities of how to signaling between iSTA and rSTA that enables LTF protection.

## Slide 3: Proposed Key Exchange in Negotiation and LTF Randomization in SU Mode
Key or cipher sequence exchange and establishment for LTF generation between iSTA and rSTA in the non-time critical FTM negotiation phase
Sequence generation information for the first measurement instance is part of the IFTM
  The measurement phase only commences once the negotiation is successful
Negotiation/key exchange
NDPA (UL PN, DL PN)
UL NDP LTF = f(key, UL PN)
DL NDP LTF = f(key, DL PN)
LMR
ISTA
RSTA

## Slide 4: Secure SU Ranging Measurement Procedure
For SU operation, the Delayed sequence generation is preferred where sequence generation information is carried in the previous sounding sequence instance
  For normal operation of SU ranging
  The frame used to deliver subsequent LTF sequence generation information is the protected LMR frame
  The specifics of LTF sequence generation information is TBD, this information is associated with a Sequence Authentication Code (SAC)
  The NDPA carries the SAC indication, a specific reserved value indicates “New LTF generation information needed”. The SAC is also included in the iFTM for the first measurement instance and in the LMR for subsequent

## Slide 5: Secure SU Ranging Measurement Procedure
For normal operation of SU ranging
  The size of the SAC should be sufficiently long to prevent simple guessing
  An adversary doesn’t know the SAC and is unable to predict it and thus can’t trigger the measurement instance. In addition the SAC and its associated measurement results are carried in the LMR
  If an incorrect SAC is received by the RSTA, the RSTA discards the NDPA (no DL NDP) and keep the current SAC and associated LTF sequence generation information

## Slide 6: Secure SU Ranging Measurement Procedure
Secure SU ranging measurement example (Immediate LMR Report case)
SAC for sequence generation (SACN) | LTF sequence generation information
DL NDP
Protected LMR
NDPA
UL NDP
DL NDP
Protected LMR
SAC for measurement sequence (SACN-1) | Location measurement information
SAC for sequence generation (SACN+1) | LTF sequence generation information
SAC for measurement sequence (SACN) | Location measurement information
N-1 round sounding sequence
N round sounding sequence
SAC for sequence generation (SACN)
NDPA
UL NDP
Derive LTF sequence of UL NDP and DL NDP of Nth round sounding sequence
SAC for sequence generation (SACN-1)

## Slide 7: Secure SU Ranging Measurement Procedure
The LMR is an Action non ACK frame
  So, need a procedure for recovery the LMR reception failure
If the LMR was not correctly received:
  The iSTA comes back to the channel and transmit an NDPA indicating “New LTF generation information needed”. The previous LTF generation information is invalidated.
  For UL NDP the iSTA uses a known UL NDP LTF sequence (not suitable for measurement).
  For DL NDP the rSTA may use the secured DL NDP LTF sequence (not suitable for measurement).
  The rSTA sends a new protected LMR content (meas. are lost only for immediate).
  The iSTA may comeback to the channel and initiate a new sounding sequence minToaReady time after.

## Slide 8: MU Ranging Measurement Procedure
MU ranging measurement consists of one or more rounds of UL sounding followed by one round of DL sounding.
TF -> Location Uplink Sounding
UL NDP
UL NDP
UL NDP
TF -> Location Uplink Sounding
UL NDP
UL NDP
UL NDP
DL NDPA
DL NDP
Optional

## Slide 9: Secure MU Ranging Measurement Procedure
Assume that both UL ranging NDP and DL ranging NDP are designed with secure (e.g., randomized) LTF sequences.
But, when an attacker is a member of the MU ranging measurement,
  The attacker can transmit a Fake DL ranging NDP if a LTF sequence in a DL ranging NDP is common to all members of the MU ranging measurement.
TF -> Location Uplink Sounding
UL NDP
UL NDP
TF -> Location Uplink Sounding
UL NDP
DL NDPA
DL NDP
iSTA2 (Attacker)
iSTA1
Fake DL NDP
iSTA3

## Slide 10: Secure MU Ranging Measurement Procedure
So, the proposed secure MU ranging measurement procedure is limited to a single iSTA.
  Extension to the multiple iSTAs is TBD.
Basic principle of the secure MU ranging measurement procedure is very similar to the secure SU ranging measurement procedure.
  The delayed sequence generation where sequence generation information is carried in the previous sounding sequence instance.
DL NDP
Protected LMR
TF -> Location Uplink Sounding
UL NDP
DL NDPA
DL NDP
Protected LMR
TF -> Location Poll
Poll Response
…
Sequence generation information carried in LMR
Derive LTF sequence of UL NDP and DL NDP of the next round sounding sequence

## Slide 11: Secure MU Ranging Measurement Procedure
The keys or cipher sequence (if needed) for LTF sequence generation are the result of the FTM negotiation.
LTF sequence generation information for the first measurement instance is a part of an iFTM, the measurement phase only commences once the negotiation is successful.
The frame used to deliver subsequent LTF sequence generation information is the protected LMR frame.
FTM Request
FTM Response
TF -> Location Uplink Sounding
UL NDP
DL NDPA
DL NDP
Protected LMR
TF -> Location Poll
Poll Response
…
Sequence generation information carried in FTM Response
Derive LTF sequence of UL NDP and DL NDP of 1st round sounding sequence

## Slide 12: Secure MU Ranging Measurement Procedure
The specifics of LTF sequence generation information are TBD, but this information is associated with a Sequence Authentication Code (SAC).
The Trigger Frame (TF) -> Location Uplink Sounding indicates the SAC for the following NDP frame corresponding to the LTF generation information.
  After receiving the TF -> Location Uplink Sounding, iSTA shall uses the LTF generation information associated with the SAC.
The SAC is also included in the iFTM for the first measurement instance and in the LMR for subsequent measurement instances.

## Slide 13: Secure MU Ranging Measurement Procedure
An adversary doesn’t know the SAC and is unable to predict it and thus can’t trigger the measurement instance (DOS).
In addition the SAC and its associated measurement results are carried in the LMR.
If an incorrect SAC is received by the iSTA, the iSTA may respond with a known LTF sequence or with any other LTF sequence and discards the current SAC and associated LTF sequence generation information.
The size of the SAC should be sufficiently long to prevent simple guessing.

## Slide 14: Secure MU Ranging Measurement Procedure
Secure MU ranging measurement example
SAC for sequence generation (SACN) | LTF sequence generation information
DL NDP
Protected LMR
TF -> Location Uplink Sounding
UL NDP
DL NDPA
DL NDP
Protected LMR
TF -> Location Poll
Poll Response
…
SAC for measurement sequence (SACN-2) | Location measurement information
SAC for sequence generation (SACN+1) | LTF sequence generation information
SAC for measurement sequence (SACN-1) | Location measurement information
N-1 round sounding sequence
N round sounding sequence
SAC for sequence generation (SACN)
Derive LTF sequence of UL NDP and DL NDP of Nth round sounding sequence

## Slide 15: Secure MU Ranging Measurement Procedure
The LMR is an Action No ACK frame
  So, need a procedure for recovery the LMR reception failure.
If the LMR was not correctly received:
  For UL NDP, the iSTA uses a known UL NDP LTF sequence (not suitable for measurement).
  For DL NDP, the rSTA may use the secured DL NDP LTF sequence (not suitable for measurement).
  If two sided LMR is used, the iSTA indicates measurements are invalidated.
  The rSTA sends a new protected LMR content (measurement results are lost only for immediate sounding sequence).
  The iSTA may come back to the channel and participate in a new sounding sequence at the next availability interval by responding to a future TF Location -> Poll.

## Slide 16: Secure MU Ranging Measurement Procedure
Secure MU ranging measurement example
SAC for sequence generation (SACN) | LTF sequence generation information
DL NDP
Protected LMR
TF -> Location Uplink Sounding
UL NDP
DL NDPA
DL NDP
Protected LMR
TF -> Location Poll
Poll Response
…
SAC for measurement sequence (SACN-2) | Location measurement information
SAC for sequence generation (SACN+1) | LTF sequence generation information
SAC for measurement sequence (SACN-1) | Location measurement information
N-1 round sounding sequence
N round sounding sequence
SAC for sequence generation (SACN)
Error
Known LTF sequence is used since SAC is not matched.

## Slide 17: Straw Poll
Do you support the following SFD texts for secure SU ranging measurement (normal operation)?
  For normal operation of secure SU ranging,
  The keys or cipher sequence (if needed) for LTF sequence generation are the result of the FTM negotiation
  Sequence generation information for the first measurement instance is part of the IFTM, the measurement phase only commences once the negotiation is successful
  The frame used to deliver subsequent LTF sequence generation information is the protected LMR frame
  The specifics of LTF sequence generation information is TBD, this information associated with a Sequence Authentication Code (SAC)
  The NDPA carries the SAC indication, a specific reserved value indicates “New LTF generation information needed”. The SAC is also included in the IFTM for the first measurement instance and in the LMR for subsequent

## Slide 18: Straw Poll
Do you support the following the following SFD text for secure SU ranging measurement (SAC operation)?
  The size of the SAC should be sufficiently long to prevent simple guessing
  An adversary doesn’t know the SAC and is unable to predict it and thus can’t trigger the measurement instance (DOS). In addition the SAC and its associated measurement results are carried in the LMR.
  If an incorrect SAC is received by the RSTA, the RSTA discards the NDPA (no DL NDP) and keep the current SAC and associated LTF sequence generation information.

## Slide 19: Straw Poll
Do you support the following SFD texts for secure SU ranging measurement (LMR error recovery operation)?
  The LMR is an Action non ACK frame
  If the LMR was not correctly received:
    The iSTA comes back to the channel and transmit an NDPA indicating “New LTF generation information needed”. The previous LTF generation information is invalidated.
    For UL NDP the iSTA uses a known UL NDP LTF sequence (not suitable for measurement).
    For DL NDP the rSTA may use the secured DL NDP LTF sequence (not suitable for measurement).
    The rSTA sends a new protected LMR content (meas. are lost only for immediate).
    The iSTA may comeback to the channel and initiate a new sounding sequence minToaReady time after.

## Slide 20: Straw Poll
Do you support the following SFD texts for secure MU ranging measurement (general operation)?
  For normal operation of secure MU ranging,
  Secure MU ranging measurement procedure is limited to a single iSTA.
  The delayed sequence generation where sequence generation information is carried in the previous sounding sequence instance.
  The keys or cipher sequence (if needed) for LTF sequence generation are the result of the FTM negotiation.
  LTF sequence generation information for the first measurement instance is a part of an iFTM, the measurement phase only commences once the negotiation is successful.
  The frame used to deliver subsequent LTF sequence generation information is the protected LMR frame.

## Slide 21: Straw Poll
Do you support the following SFD texts for secure MU ranging measurement (normal operation)?
  The specifics of LTF sequence generation information are TBD, but this information is associated with a Sequence Authentication Code (SAC).
  The Trigger Frame (TF) -> Location Uplink Sounding indicates the SAC for the following NDP frame corresponding to the LTF generation information.
  The SAC is also included in the iFTM for the first measurement instance and in the LMR for subsequent measurement instances.
  An adversary doesn’t know the SAC and is unable to predict it and thus can’t trigger the measurement instance (DOS).
  In addition the SAC and its associated measurement results are carried in the LMR.
  If an incorrect SAC is received by the iSTA, the iSTA may respond with a known LTF sequence or with any other LTF sequence and discards the current SAC and associated LTF sequence generation information.
  The size of the SAC should be sufficiently long to prevent simple guessing.

## Slide 22: Straw Poll
Do you support the following SFD texts for secure MU ranging measurement (LMR error recovery operation)?
  The LMR is an Action No ACK frame
  If the LMR was not correctly received:
    For UL NDP, the iSTA uses a known UL NDP LTF sequence (not suitable for measurement).
    For DL NDP, the rSTA may use the secured DL NDP LTF sequence (not suitable for measurement).
    If two sided LMR is used, the iSTA indicates measurements are invalidated.
    The rSTA sends a new protected LMR content (measurement results are lost only for immediate sounding sequence).
    The iSTA may come back to the channel and participate in a new sounding sequence at the next availability interval by responding to a future TF Location -> Poll.