## Slide 1: Advertising WUR Discovery Frame Related Info for Fast Scanning
Date: 2018-01-17
Authors:
Name | Affiliation | Address | Email
Li Nan | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | li.nan25@zte.com.cn
Lv Kaiying |  |  | lv.kaiying@zte.com.cn
Roger Marks | Huawei | Denver, CO, USA | roger@ethair.net
Lyu Yunping (Lily) |  | Nanjing, PRC | lvyunping@huawei.com
Taewon Song | LG | 
Rojan CrOhitrakar | Panasonic | 

## Slide 2: Abstract
This contribution, intended for presentation to IEEE 802.11 TGba, proposes additional details to apply Usage Model 9 (“Smart Scanning”) of the WUR Usage Model Document (IEEE 802.11-17/0029r10), consistent with the Specification Framework for TGba (IEEE 802.11-17/0575r08).
The key point is advertisement of the WUR Discovery frame characteristics, including channel and information about discovered AP.

## Slide 3: Background
  Usage Model 9: Smart Scanning:
    mobile device passively scans through multiple channels using WUR, collecting basic information about nearby APs. The collected info can be used to facilitate roaming decisions and provide location information.
  “Since WUR is an ultra-low power receiver, offloading some of the passive background scans to WUR can significantly save even more power.”

## Slide 4: Usage Model 9: Smart Scanning
Use case 1: Ultra-low power location scan
Mobile devices sometimes scan through multiple channels for nearby APs, and use the measured Wi-Fi signal strength for improved location services. In addition, scanning on main radio has the risk of conflicting with regular data exchange.
In WUR-facilitated location scan, the mobile device scans through the channels using the WUR receiver, and uses the signal strength measured from WUR packets received from adjacent APs to provide additional information to the location services on the mobile device. In other words, some of the location scan on main radio can be offloaded to WUR radio.
Because WUR consumes much less power than main radio, WUR facilitated location scan provides an ultra-low power location scan mechanism.
Use case 2: Ultra low power roam scan
Mobile devices sometime scan for roaming purposes. These roam scan sometimes is triggered when link quality degrades. These roam scan takes time because the scan is typically done on multiple channels, and on each channel the device either conducts active scan during which it sends a probe request and typically stays awake until it receives a probe response, or passive scan during which it dwells on each channel for at least a Beacon interval to receive a Beacon. As a consequence, scanning through multiple channels introduces roaming latency and consumes power. Sometimes, it runs into conflict with regular data exchange.
In WUR-facilitated roam scan, the mobile device passively scans through multiple channels using WUR, and collects basic information about nearby APs. The collected info can be used to facilitate the devices’ roaming decisions.
Because WUR consumes much less power than main radio, WUR-facilitated roam scan provides an ultra-low power roam scan. In addition, due to the low power operation, WUR scan can be performed quite frequently in the background, and thus roaming information can be readily available whenever needed, i.e., it reduces roaming latency.

## Slide 5: Usage Model 9: Some Questions
What is the WUR discovery frame format… “that allows unassociated STAs to interpret the AP’s identity”? [see 802.11-18/0160r4 for details]
How does the mobile know where to find the desired WUR Discovery Frame?

## Slide 6: Proposed Method
WUR STA performs uses its wake up radio to scan for and read WUR Discovery Frames.
WUR Discovery Frame provides information about its own BSSs for the purpose of AP (re)selection.
To facilitate fast and efficient scanning for WUR Discovery frame, WUR should first learn which WUR Discovery Frames are in which WUR channels.
To implement scanning for WUR Discovery Frame, some information should be advertised:
  WUR Discovery Channel and SSID/compressed SSID are proposed.
  BSSID could be included.
STA can monitor WUR channel during ON windows and perform WUR scanning during OFF windows, for example.

## Slide 7: Key Proposed Information
WUR Discovery Channel
WUR scanning can be limited to identified WUR Discovery channels.
Compressed SSID
Compressed SSID can assist STA to choose which WUR Discovery Channel to scan.
STA can choose to scan only WUR Discovery Channels that point to SSIDs of interest.
STA may prefer to choose a candidate AP within the same ESS for fast BSS transition.

## Slide 8: Proposed Advertisement Method
Option 1: delivered by PCR in 802.11 frame such as beacon/probe response frame
  Pro: efficient delivery
  Con: STA will not learn of updates while asleep (but could be awakened for updates).
Option 2: delivered by WUR
  Pro: Change of WUR Discovery Frame information can be notified without waking up the STA
  Con: less efficient delivery
Option 1 is preferable

## Slide 9: Example A: using RNR from current standard
RNR: Reduced Neighbor Report
Neighbor/target WUR information when TBTT Information Field Type equals to 3

## Slide 10: Example B: using new Neighbor WUR Element
PCR
Operating Class
BSSID
Compressed
SSID
WUR Operationg Class
WUR Diiscovery Channel Number
PCR
Channel Number
Element ID
Length
Bitmap Control
neighbor AP/target AP Count
PCR Operating Class and channel number Present
BSSID
Present
Compressed
SSID Present
WUR Operationg Class and Diiscovery Channel Number Present
Reserved
Octets:
1 1 1 Variable
Bits:
Octets:
one or more
neighbor AP/target AP information
1 1 1 1 4b
1 1 1 6 TBD 1 1

## Slide 11: Summary
Advertisement of WUR Discovery Frame
  In 802.11 message, such as RNR, in beacon frame or probe response frame, or in WUR operation related frame on PCR.
  By using wake up frame such as WUR unicast /multicast packet, WUR beacon or WUR discovery frame.
Parameters of WUR Discovery Frame to reduce power latency, including:
  WUR Discovery Channel
  Compressed SSID

## Slide 12: Straw Poll 1
Do you support advertisement of WUR Discovery Frame by PCR?
  Y
  N
  A

## Slide 13: Straw Poll 2
Add to SFD:
R.4.8.B: WUR Discovery Channel, Compressed SSID of the neighbor AP, and other information TBD should be advertised by the PCR to WUR STA.
    Y
    N
    A

## Slide 14: References
[1] IEEE 802.11-17/0029r10 (“WUR Usage Model Document”)
[2] IEEE 802.11-17-0575r08 (“Specification Framework for TGba”)
[3] IEEE 802.11-17/1619 (“Consideration on WUR frame for Fast Scanning ”)
[4] IEEE 802.11-17/1644 (“Further Consideration on Smart Scanning Usage Model”)
[5] IEEE 802.11-18/0160 (“WUR Discovery Frame Content”)