## Slide 1: Advertising WUR Discovery Frame Related Info for Fast Scanning
Date: 2018-03-09
Authors:
Name | Affiliation | Address | Email
Li Nan | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | li.nan25@zte.com.cn
Lv Kaiying |  |  | lv.kaiying@zte.com.cn
Roger Marks | Huawei | Denver, CO, USA | roger@ethair.net
Lyu Yunping (Lily) |  | Nanjing, PRC | lvyunping@huawei.com
Taewon Song | LG | 
Rojan Chitrakar | Panasonic | 
Guoqing Li | Apple | 

## Slide 2: Abstract
This contribution, intended for presentation to IEEE 802.11 TGba, proposes additional details to apply Usage Model 9 (“Smart Scanning”) of the WUR Usage Model Document (IEEE 802.11-17/0029r10), consistent with the Specification Framework for TGba (IEEE 802.11-17/0575r09).
The key point is the advertisement of the WUR Discovery frame characteristics, including channel and information about discovered AP.

## Slide 3: Background
  Usage Model 9: Smart Scanning:
    Mobile devices passively scan through multiple channels using WUR, collecting basic information about nearby APs. The collected info can be used to facilitate roaming decisions and provide location information.
  “Since WUR is an ultra-low power receiver, offloading some of the passive background scans to WUR can significantly save even more power.”

## Slide 4: Usage Model 9: Smart Scanning
Use case 1: Ultra-low power location scan
Mobile devices sometimes scan through multiple channels for nearby APs, and use the measured Wi-Fi signal strength for improved location services. In addition, scanning on main radio has the risk of conflicting with regular data exchange.
In WUR-facilitated location scan, the mobile device scans through the channels using the WUR receiver, and uses the signal strength measured from WUR packets received from adjacent APs to provide additional information to the location services on the mobile device. In other words, some of the location scan on main radio can be offloaded to WUR radio.
Because WUR consumes much less power than main radio, WUR facilitated location scan provides an ultra-low power location scan mechanism.
Use case 2: Ultra low power roam scan
Mobile devices sometime scan for roaming purposes. These roam scan sometimes is triggered when link quality degrades. These roam scan takes time because the scan is typically done on multiple channels, and on each channel the device either conducts active scan during which it sends a probe request and typically stays awake until it receives a probe response, or passive scan during which it dwells on each channel for at least a Beacon interval to receive a Beacon. As a consequence, scanning through multiple channels introduces roaming latency and consumes power. Sometimes, it runs into conflict with regular data exchange.
In WUR-facilitated roam scan, the mobile device passively scans through multiple channels using WUR, and collects basic information about nearby APs. The collected info can be used to facilitate the devices’ roaming decisions.
Because WUR consumes much less power than main radio, WUR-facilitated roam scan provides an ultra-low power roam scan. In addition, due to the low power operation, WUR scan can be performed quite frequently in the background, and thus roaming information can be readily available whenever needed, i.e., it reduces roaming latency.

## Slide 5: Usage Model 9: Some Questions
What is the WUR discovery frame format… “that allows unassociated STAs to interpret the AP’s identity”?
  see 802.11-18/0160r7 for details
  note: Spec Framework (802.11-17/0575r9) says
      4.8 WUR Discovery
      Define a type of WUR frame as WUR Discovery frame to assist the STAs to discover the BSS.
How does the mobile know where to find “desired” WUR Discovery Frame in low latency?

## Slide 6: Proposed Method
WUR STA uses its wake up radio to scan for and read WUR Discovery Frames.
WUR Discovery Frame provides information about its own BSSs for the purpose of roaming or location services.
To facilitate fast and efficient scanning, WUR STA can leverage the information previously received on PCR to learn which WUR channels to scan for WUR Discovery frame.
WUR Discovery information of APs advertised on PCR should include:
  WUR Discovery Channel and compressed SSID.
  BSSID.
  Note: the computation of compressed SSID is TBD.
The WUR Discovery channel should be selected from a fixed subset of WUR channels to reduce the discovery latency
  The recommended WUR discovery channels allow a STA to focus scanning on these WUR channels, and thus can limit the maximum discovery latency
STA can monitor WUR frame during ON windows and perform WUR scanning during OFF windows, for example.

## Slide 7: Key Advertised Information
WUR Discovery Channel
WUR scanning can be limited to the advertised WUR Discovery channels.
Compressed SSID
Compressed SSID can assist STA to choose which WUR Discovery Channel to scan.
STA can choose to scan only WUR Discovery Channels that point to SSIDs of interest.
STA may prefer to choose a candidate AP within the same ESS for fast BSS transition.

## Slide 8: Advertisement Signaling Example A: Repurposing RNR from current standard

## Slide 9: Advertisement Signaling Example B: using new Neighbor WUR Discovery Element
BSSID
Compressed
SSID
WUR Operating Class
WUR Discovery Channel Number
Element ID
Length
Bitmap Control
Element ID Extension
BSSID
Present
Reserved
Octets:
1 1 1 Variable
Bits:
Octets:
one or more
neighbor AP/target AP information
1 7
1 1 1 variable
neighbor AP/target AP Count
neighbor AP/target AP
one or more
Number of APs using the same Discovery channel. Acts as an indication how busy a channel is.
One or more APs transmitting WUR Discovery frames on this WUR Discovery channel.
TBD 1 0 or 6
Octets:
Listing neighbor APs according to channels may have following benefits:
1) Since number of Discovery channels would be less than number of APs, channel information need not be repeated for each AP. saves #octets.
2) Grouping APs by channel makes it easier for a receiving WUR STA to quickly gauge which channel is busier and hence more attractive to scan.

## Slide 10: Summary
Advertisement method of WUR Discovery Frame
  In 802.11 message, such as RNR, in beacon frame or probe response frame, or in WUR operation related frame on PCR.
Advertised Parameters should include:
  WUR Discovery Channel
  Compressed SSID
  BSSID (optional)
The WUR discovery channel should be selected from a fixed subset of all possible WUR channels

## Slide 11: Straw Poll 1
Do you support advertisement of WUR Discovery Frame transmission parameters of an AP using a management frame using PCR ?
  Y
  N
  A

## Slide 12: Straw Poll 2
Add to SFD:
R.4.8.B: Following information about APs’ WUR Discovery frames may be provided by the PCR :
  WUR Discovery Channel:
    Should be selected from a fixed subset of all possible WUR channels
  Other information: TBD,
    Y
    N
    A

## Slide 13: Motion
Move to add the following text to the TGba SFD
R.4.8.B: Following information about APs’ WUR Discovery frames may be provided by the PCR :
  WUR Discovery Channel:
    Should be selected from a fixed subset of all possible WUR channels
  Other information: TBD,
Move:
Second:

## Slide 14: References
[1] IEEE 802.11-17/0029r10 (“WUR Usage Model Document”)
[2] IEEE 802.11-17-0575r08 (“Specification Framework for TGba”)
[3] IEEE 802.11-17/1619 (“Consideration on WUR frame for Fast Scanning ”)
[4] IEEE 802.11-17/1644 (“Further Consideration on Smart Scanning Usage Model”)
[5] IEEE 802.11-18/0160 (“WUR Discovery Frame Content”)