## Slide 1: 802.11ax for IMT-2020
Date: 2018-01-18
Authors:

## Slide 2: Abstract
This document provides an analysis of 802.11ax capabilities vis-à-vis the IMT-2020 requirements for the eMBB Indoor Hotspot and Dense Urban scenarios.
It also discusses the features in other unlicensed spectrum technologies like LAA and MulteFire.
It also discusses 802.11ax features with the proposed features in NR-Unlicensed in order to meet the IMT-2020 requirements.

## Slide 3: 802.11ax vs. IMT-2020 requirements
Parameter | Desired Range | Use Case | 802.11ax capability
Peak data rate | DL/UL: 20/10 Gbps | eMBB | 19.2 Gbps DL/UL (8x8 HE160)
Peak spectral efficiency | DL/UL: 30/15 bits/s/Hz | eMBB | 60 bits/s/Hz (8x8)
5%ile user spectral efficiency | DL/UL: 0.3/0.21 bits/s/Hz DL/UL: 0.225/0.15 bits/s/Hz | eMBB: Indoor Hotspot eMBB: Dense Urban | Expected to Meet
5%ile user experienced data rate | DL/UL: 100/50 Mbps | eMBB | Expected to Meet
Avg Spectral efficiency | DL/UL: 9/6.75 bits/s/Hz/TRxP DL/UL: 7.8/5.4 bits/s/Hz/TRxP | eMBB: Indoor Hotspot eMBB: Dense Urban | Expected to Meet
Area traffic capacity | 10 Mbps/m2 | eMBB: Indoor Hotspot eMBB: Dense Urban | Expected to Meet
User Plane Latency | 4 ms 1 ms | eMBB URLLC | Can meet
Control Plane Latency | 20 ms (Encourage 10 ms) | eMBB/URLLC | Can meet for STA initiated
Connection density | 106 connected devices/km2 | mMTC | Not in focus for eMBB
Energy efficiency | Efficient data transmission in high loads Low energy consumption in absence of data High sleep ratio and long sleep duration | eMBB | Can meet
Reliability | 1-10-5 success probability for transmitting a Layer 2 PDU within 1ms at coverage edge for Urban Macro-URLLC | URLLC | Not in focus for eMBB
Mobility (defined only for UL) | 1.5 bit/s/Hz UL @ 10 kph 1.12 bit/s/Hz UL @ 30 kph | eMBB: Indoor Hotspot eMBB: Dense Urban | Can meet
Mobility Interruption Time | 0 ms | eMBB and URLLC | ~ 2-3 ms
Bandwidth | Scalable: Min 100 MHz, up to 1 GHz |  | 160 MHz

## Slide 4: 802.11ax vs. LAA/MulteFire
Feature |  | 802.11ax | MuLTEfire / (e)LAA | Comments regarding 802.11ax
Common Features | Highest modulation | 1024-QAM | 256-QAM | 25 % higher peak data rate
 | Guard Interval length | 0.8us, 1.6us and 3.2 us | 4.69 us (fixed) | Flexible and dynamic adaptation of Guard Interval to suit the current operating environment
 | Symbol length | 13.6 us,14.4 us,16 us | 71.4 us | Shorter symbol length => Shorter RTT
 | Minimum transmission length | O(50) us | 1 ms | Finer control of transmission lengths => less padding => more efficient medium usage
 | Starting transmission granularity | 9 us | 0.5 ms (DL), 1 ms (UL) | 
 | Ending transmission granularity | 13.6 us,14.4 us,16 us | 214 us (DL), 1 ms (UL) | 
DL | Maximum transmission bandwidth | 80 + 80 MHz or 160 MHz | 80 MHz (unlicensed), 100 MHz (including licensed) | Higher transmission bandwidth
 | OFDMA | Yes | Yes | Comparable with respect to OFDMA/MU-MIMO/Beamforming. However 11ax supports higher bandwidth and higher modulation leading to higher data rates
 | MU-MIMO | Yes | Yes | 
 | Beamforming | Yes | Yes | 
 | OFDMA + MU-MIMO | Yes | Yes | 
UL | Maximum transmission bandwidth | 80 + 80 MHz or 160 MHz | 20 MHz (unlicensed), 60 MHz (including licensed) | 11ax UL supports higher bandwidth, MIMO with higher number of spatial streams, MU-MIMO and better beamforming.
 | OFDMA | Yes | Yes (SCFDMA) | 
 | MIMO | Yes, up to 8 spatial streams | Yes, up to 4 spatial streams | 
 | MU-MIMO | Yes (up to 8) | No | 
 | Beamforming | Yes, fixed and implicit codebook as DL | Yes, only with fixed codebook | 
 | OFDMA + MU-MIMO | Yes | No | 
 | Higher UL PSD | Yes | Yes | 

## Slide 5: 802.11ax vs. NR-Unlicensed
Standardization of NR-Unlicensed (NR-U) will start in Feb/2018.
The following table describes a possible list of features in NR-U which are enhancements over LAA. These have been compiled from submissions to 3GPP, NR-U workshops in 2016 and 2017.
NR-U specification does not yet exist. So, the potential feature list is hypothetical.
It is noted that numerous official contributions in 3GPP and other fora cite the performance advantage of specific features in 802.11 to argue for similar features in NR-U. Some of these documents are included as reference.
It is expected that NR-U will incorporate principles similar to 802.11 in order to close/reduce the performance gap, especially in uplink.
It is noted that many NR-U proponents oppose significant changes to NR-U over NR-licensed in order to reduce design complexity. So, there is a strong possibility that NR-U may not be as flexible as Wi-Fi.

## Slide 6: 802-11ax vs. NR-Unlicensed
Proposed NR-U Enhancements over LAA/MF | 802.11ax Capability
Standalone unlicensed operation | Yes
Operation in 5.0-7.1 GHz, 37-37.6 GHz, 57-71 GHz | Yes (5.0 – 7.1 GHz)
Scalable bandwidths, up to 400 MHz per component carrier (400 MHz for 240 kHz carrier spacing and high frequencies) | Scalable up to 160 MHz
Self-contained TXOP for faster turn-around | Yes
Short flexible symbol durations for lower latency | Yes (3.6us/4us/13.4us/14.4us/16us)/similar to shortest NR symbols
Front loaded reference signals for faster demodulation | Yes
“Mini-slots” for quick and short Tx-Rx exchanges and for channel contention and reservation | Yes (16 us RTT)/Faster than NR requirement
Grant-free UL transmission | Yes
Variable DL/UL split for dynamic TDD | Yes
Improved/updated CCA: Channel reservation optimized for high-order MIMO and mmW bands: Spatially directional channel sensing and reservation Omni-directional/Directional CCA for Tx w/ directional beam Signaling-based medium reservation: (W/in+across RATs) Universal signaling for channel reservation | Yes, except universal signaling for channel reservation across RATs, which is TBD between standards bodies
Better support for neutral host deployments | Yes

## Slide 7: Discussion
802.11ax already meets most of the IMT-2020 requirements for eMBB Indoor Hotspot and Dense Urban use cases. The gaps in the remaining few requirements for these two use cases are narrow.
It is more difficult for 802.11ax to meet the requirements for eMBB Rural due to the higher mobility criteria.
A possible Way Forward is to change scope and prioritize the requirements for eMBB Indoor and Dense Urban.
It will enable 802 take the position that 802.11ax is proven to satisfy all the requirements for these two important IMT-2020 use cases and let 802.11ax gain significant branding advantage.

## Slide 8: References
[1] Qualcomm: Radio Access Design
[2] Qualcomm: Gap analysis for standalone operation from licensed assisted system definition
[3] Samsung: Radio Access Design (Samsung_AI_3.pdf)
[4] Nokia: Radio Access Design
[5] Intel: Gap analysis for standalone operation from licensed assisted system definition
[6] LG: Radio Access Design
[7] Ericsson: Views on NR Unlicensed operation designs
[8] 3GPP TS 36.211, 36.213, 36.300 for LTE/LAA
[9] 3GPP TS 38.211, 38.213 for NR
[1] – [7] were presented at the 5G Workshop on NR-Unlicensed and Shared Spectrum