## Slide 1: Discussion on Maximum WUR PPDU Duration
Date: 2018-3-8
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Maximum WUR PPDU Duration in 11ba D0.1
The current aPPDUMaxTime for WUR PPDU is actually the same as HT/VHT/HE PPDU.
The aPSDUMaxLength should be 168 octets instead of 166 octets.
  Floor ((5.484-0.020-0.004-0.064)*250/8) =168
HDR WUR PPDU

## Slide 3
  WUR MPDU has a maximum size of 22 octets under the following assumptions:
    The maximum length of the Frame Body is 16 octets
Maximum WUR MPDU Size in 11ba D0.1 & SFD
The CRC field size of all WUR frames is 16 bits

## Slide 4
Problem Statement
There is a disparity between the maximum PSDU length and maximum MPDU size in 11ba D0.1 & SFD.

## Slide 5
Proposal: Maximum WUR PPDU Duration
Maximum Length of Frame Body (octet) | aPSDUMaxLength (octet) | aPPDUMaxTime (ms)
8 | 14 | 1.944
16 | 22 | 2.968
Maximum WUR PPDU duration (aPPDUMaxTime) shall be computed based on a PSDU which has a maximum length and is transmitted with LDR
Definitely less than the L-SIG LENGTH field limitation.

## Slide 6: Reference
Draft P802.11ba_D0.1
11-17-0575-09-00ba-spec-framework

## Slide 7: SP
Do you support to change Table 32-11 in 11ba D0.1 as follows?
  Y/N/A:
Table 32-11 WUR PPDU Time and Length Characteristics | 
Characteristics | Value
aCCAMinTime | TBD µs
aPPDUMaxTime | 5.484 TBD ms (see NOTE 1)
aPSDUMaxLength | 166 TBD octets (see NOTE 1)
aRxPHYStartDelay | 88 µs (see NOTE 2)
NOTE 1—This is the duration of a WUR PPDU with a PSDU which has a length of aPSDUMaxLength and is transmitted with LDR.This is the maximum length in octets for a WUR PPDU with HDR, single stream, and limited by 1332 possible data symbols in aPPDUMaxTime. This is the maximum PSDU length a WUR PHY could support assuming no restrictions in MAC. NOTE 2—This value arises from the time to the end of the WUR-Sync field with HDR. |