## Slide 1: Dynamically Changing WUR ID
Date: 2018-02-23
Authors:

## Slide 2: Abstract
Battery Draining Attacks may be a threat for ultra-low-power WUR devices.
Dynamically changing WUR ID address would help with the issue.

## Slide 3: Motivation
With static WUR ID, if a malicious user overhears one unicast wake-up frame, it can keep on waking the STA continuously (spoofing) and drain the battery of the STA
Also if the same WUR ID happens to be used in neighbouring BSS, then unnecessary wake-up can happen too often

## Slide 4: Dynamically changing WUR ID
Two potential ways on how to change the WUR ID dynamically for unicast wake-up frames
  Agree a random seed in the WUR negotiation phase and generate new temporal WUR ID each time from that
  Before going to WUR doze, always indicate the next WUR ID from WUR receiver to transmitter, using the PCR

## Slide 5: Summary
We discussed about dynamically changing WUR ID to help with malicious attacks
We also presented two ways to change the identifier