## Slide 1: Operation after Wake-up Frame Transmission and Reception
Date: 2018-03-04
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Daniel F Bravo |  |  |  | 
Noam Ginsburg |  |  |  | 
Robert Stacey |  |  |  | 

## Slide 2: Abstract
There has been discussions about the operation of AP (resp. non-AP STA) after transmitting (resp. receiving) wake-up frame
We think that the focus of 11ba should be on reusing the existing PCR operation as much as possible rather than defining new operation on top of different power save protocols
We propose simple spec language in this presentation toward this goal

## Slide 3: Review Indication in Wake-up Frame
There are three indications in wake-up frame
  Basic indication
  Group addressed MPDU(s)/MMPDU(s) are buffered at AP
  Check Beacon
Observation
  We view the Basic indication as indication of buffered BU(s)
  We think all 3 indications exist in the current PCR operation (TIM, DTIM, and Tim broadcast), and there are already existing well defined PCR operation to follow

## Slide 4: Review Method of Indication in Wake-up Frame
There are currently following 3 methods for a wake-up frame to address a specific non-AP STA for basic indication
  Individual addressed wake-up frame
  a wake-up frame that contains a group ID that identifies a group of non-AP STAs, which the non-AP is a member of
  a wake-up frame with a list of WIDs in frame body, where one of the WIDs identifies the non-AP STA
Some way to indicate buffered group addressed BUs of PCR
A field to indicate check beacon

## Slide 5: Proposal for non-AP STA
A non-AP STA that receives a wake-up frame that satisfies condition 1 shall follow existing PCR operation to retrieve individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
A non-AP STA that receives a wake-up frame with an indication of buffered group addressed BU(s) shall follow existing PCR operation to receive group addressed BU(s)
A non-AP STA that receives a wake-up frame with an indication to check PCR beacon shall follow existing PCR operation to attempt to receive the PCR Beacon information

## Slide 6: Proposal for AP
An AP that transmits a wake-up frame addressed to a non-AP STA and satisfying condition 1 shall follow existing PCR operation to deliver individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
  AP shall schedule for transmission through PCR to the non-AP STA if one of the following conditions is met:
    The PCR transition delay indicated by the non-AP STA in the WUR Capabilities elements following the most recent transmitted wake-up frame intended to the non-AP STA has expired
    The non-AP STA has indicated it is in awake state after transmitting a frame through the PCR to the AP

## Slide 7: Proposal for AP
An AP that transmits a wake-up frame indicating group addressed buffered BU(s) shall follow existing PCR operation to deliver group addressed buffered BU(s)
  AP shall schedule for transmission of group addressed buffered BU(s) through PCR if the following condition is met:
    The maximum PCR transition delay indicated by all the non-AP STAs in the WUR Capabilities elements, that are not in awake state and have negotiated WUR service with AP, following the most recent transmitted wake-up frame indicating buffered group addressed BU(s) of PCR has expired
    Note that a non-AP STA indicates it is in awake state by transmitting a frame through the PCR to the AP

## Slide 8: Conclusion
In this presentation, we propose
  Operation for non-AP STA after receiving wake-up frame
  Operation for AP after transmitting wake-up frame
We propose to reuse the existing PCR operation as much as possible rather than defining new operation on top of different power save protocols

## Slide 9: Straw Poll #1
Do you support the following:
A non-AP STA that receives a wake-up frame that satisfies condition 1 shall follow existing PCR operation to retrieve individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
A non-AP STA that receives a wake-up frame with an indication of buffered group addressed BU(s) shall follow existing PCR operation to receive group addressed BU(s)
A non-AP STA that receives a wake-up frame with an indication to check PCR beacon shall follow existing PCR operation to attempt to receive the PCR Beacon information

## Slide 10: Straw Poll #2
Do you support the following:
An AP that transmits a wake-up frame addressed to a non-AP STA and satisfying condition 1 shall follow existing PCR operation to deliver individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
  AP shall schedule for transmission through PCR to the non-AP STA if one of the following conditions is met:
    The PCR transition delay indicated by the non-AP STA in the WUR Capabilities elements following the most recent transmitted wake-up frame intended to the non-AP STA has expired
    The non-AP STA has indicated it is in awake state after transmitting a frame through the PCR to the AP
    Note that the transmission is not limited to the individually addressed buffered BU(s)

## Slide 11: Straw Poll #3
Do you support the following:
An AP that transmits a wake-up frame indicating group addressed buffered BU(s) shall follow existing PCR operation to deliver group addressed buffered BU(s)
  AP shall schedule for transmission of group addressed buffered BU(s) through PCR if the following condition is met:
    The maximum PCR transition delay indicated by all the non-AP STAs in the WUR Capabilities elements, that are not in awake state and have negotiated WUR service with AP, following the most recent transmitted wake-up frame indicating buffered group addressed BU(s) of PCR has expired

## Slide 12: Motion #1
Move to add the following into TGba SFD:
A non-AP STA that receives a wake-up frame that satisfies condition 1 shall follow existing PCR operation to retrieve individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
A non-AP STA that receives a wake-up frame with an indication of buffered group addressed BU(s) shall follow existing PCR operation to receive group addressed BU(s)
A non-AP STA that receives a wake-up frame with an indication to check PCR beacon shall follow existing PCR operation to attempt to receive the PCR Beacon information
Move: Po-Kai Huang
Second: Peter Loc

## Slide 13: Motion #2
Move to add the following into TGba SFD:
An AP that transmits a wake-up frame addressed to a non-AP STA and satisfying condition 1 shall follow existing PCR operation to deliver individually addressed buffered BU(s)
  (Condition 1) The wake-up frame is either an individual addressed wake-up frame that addresses the non-AP STA, or a wake-up frame that contains a group ID that identifies a group of non-AP STAs of which the non-AP STA is a member, or a wake-up frame with a list of WIDs in frame body where one of the WIDs identifies the non-AP STA
  If AP schedule a transmission to the non-AP STA, AP shall schedule the transmission through PCR to the non-AP STA if one of the following conditions is met:
    The PCR transition delay indicated by the non-AP STA in the WUR Capabilities elements following the most recent transmitted wake-up frame intended to the non-AP STA has expired
    The non-AP STA has indicated it is in awake state after transmitting a frame through the PCR to the AP
    Note that the transmission is not limited to the individually addressed buffered BU(s)

## Slide 14: Motion #3
Move to add the following into TGba SFD:
An AP that transmits a wake-up frame indicating group addressed buffered BU(s) shall follow existing PCR operation to deliver group addressed buffered BU(s)
  AP shall schedule for transmission of group addressed buffered BU(s) through PCR if the following condition is met:
    The maximum PCR transition delay indicated by all the non-AP STAs in the WUR Capabilities elements, that are not in awake state and have negotiated WUR service with AP, following the most recent transmitted wake-up frame indicating buffered group addressed BU(s) of PCR has expired
Move: Po-Kai Huang
Second: Alfred Asterjadhi