## Slide 1: Starting Time Indication of WUR Beacon and Duty Cycle Operation
Date: 2018-03-04
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Daniel F Bravo |  |  |  | 
Noam Ginsburg |  |  |  | 
Robert Stacey |  |  |  | 

## Slide 2: Abstract
For the non-AP STA to know the Target Wake-up Beacon Transmission Time (TWBTT), indication of starting time of TWBTT is required
We have agreed to let AP decide the starting point of the WUR Duty cycle schedule [1], but the indication is TBD.
We discuss these two TBDs in this presentation

## Slide 3: Method used by the PCR Beacon
For PCR Beacon, TSF 0 is one TBTT
For STBC Beacon, the TBTT is offset by half of the beacon interval
The beacon interval of PCR Beacon and STBC Beacon is the same.

## Slide 4: Consideration for WUR Beacon
WUR Beacon interval is likely to be much longer than PCR Beacon interval
  Except a maximum indicated value, there is no restriction on the WUR Beacon interval announced by the AP
If TSF 0 is one TWBTT, then AP may schedule WUR Beacon and PCR Beacon at the same time
  This can be argued to be acceptable or not acceptable
To separate TBTT, STBC TBTT, and TWBTT, some additional restriction is required
  Ex We need some relation of Beacon interval on PCR and WUR, and a fixed offset of TWBTT
We think we should leave the scheduling problem to the AP and should not mandate more rules, which may create problems in the future

## Slide 5: Proposal
We propose that AP indicates the offset of Target Wake-up radio Beacon Transmission Time (TWBTT) in WUR Operation element, which is the TSF time of the first TWBTT
  AP has full flexibility to decide TWBTT based on whatever criteria that exists now or may come in the future
  No additional rule on setting WUR Beacon interval
Note that originally WUR Beacon period is indicated in WUR Mode element, but during the offline discussion, the indication has been moved to a newly defined WUR operation element.

## Slide 6: Consideration for Duty Cycle Operation
We think the starting point indication of the WUR duty cycle schedule is similar to the indication used in TWT, where TSF time is used
Proposal: AP indicates the TSF time of the starting point of the WUR duty cycle schedule in WUR Mode element

## Slide 7: Conclusion
We propose to let AP indicate the starting time of TWBTT in WUR operation element
We propose to let AP indicate the WUR duty cycle schedule in WUR Mode element

## Slide 8: Straw Poll #1
Do you support that AP indicates the offset of Target Wake-up radio Beacon Transmission Time (TWBTT) in WUR Operation element, which is the TSF time of the first TWBTT?

## Slide 9: Straw Poll #2
Do you support that AP indicates the TSF time of the starting point of the WUR duty cycle schedule in WUR Mode element?

## Slide 10: Reference
[1] 11-17-0575-09 Spec Framework