## Slide 1: Classification of WUR frames
Authors:
Alfred Asterjadhi,
George Cherian

## Slide 2: Introduction
The Frame Control field contains Type field and Length/Misc field [1]
  Type field identifies the type of the WUR frame
Certain WUR frames (potentially of same type) contain Frame Body
  Length field indicates length of the Frame Body when this is present (VL frame)
    Reception of VL frames is optional
  Misc. field is present when Frame Body is not present (CL frame)
    Reception of CL frames is excepted to be mandatory
  Not explicitly stated if certain WUR frames contain Frame Body or not
    We propose to clarify this aspect for all currently defined WUR frame types
Certain WUR frames (post-association) embed BSSID info in the FCS
  Not fully clear which WUR frames are post-association
    We propose to clarify this aspect for all currently defined WUR frames

## Slide 3: WUR Beacon frame
WUR Beacon frame provides synchronization info to WUR STAs
  Expected to be mandatory in RX so that WUR STAs can keep clock sync
  Synchronization functionality is necessary for post-association operation
  11ba D0.1 defines it as WUR frame without Frame Body field
Proposal for WUR Beacon frame
  Does not have a Frame Body field
    Mandatory in RX for WUR STAs that want to update their TSF clock
  WUR Beacon frame is classified as a post-association frame
    I.e., Embedded BSSID is used for FCS computation

## Slide 4: WUR Wake Up frame
WUR Wake Up frame causes the WUR STA to wake its PCR
  Expected some form of it to be mandatory in RX to wake up PCR
  Wake up functionality is possible after association
    I.e., after WUR mode negotiation and WUR capabilities are exchanged
  11ba D0.1 defines it as WUR frame with/without Frame Body field
    Wake Up frame with no Frame Body is expected to be mandatory
    Wake Up frame with Frame Body is optional
Proposal for WUR Wake Up frame
  Mandatory in RX: Wake Up frame that does not have Frame Body field
  Optional in RX: Wake Up frame that does have Frame Body field
  Wake Up frame is classified as a post-association frame
    I.e., Embedded BSSID is used for FCS computation

## Slide 5: WUR Vendor Specific frame
WUR Vendor Specific frame contains vendor specific information
  Much of its content is mysterious (and is contained in the Frame Body)
  Functionality could be pre-association or post-association
  11ba D0.1 defines it as WUR frame with Frame Body field
Proposal for WUR Vendor Specific (VS) frame
  Does have a Frame Body field
    Optional in RX for WUR STAs
  WUR VS frame can be classified as either pre- or post-association frame
    Whether Embedded BSSID is used for FCS computation is Vendor Specific

## Slide 6: WUR Discovery frame
WUR Discovery frame contains discovery information
  Much of its content is expected to be contained in the Frame Body
    PCR operating channel, hash of SSID, etc.,
    However, there has been no conclusion on this and discussions are ongoing
  Functionality could be pre-association or post-association
    However much of discussions are targeting pre-association use-cases
  11ba D0.1 does not have any spec text on it
Proposal for WUR Discovery frame
  Frame Body field presence to be decided when fields are settled (TBD)
  WUR Discovery frame is classified as a pre-association frame
    I.e., Embedded BSSID is not used for FCS computation

## Slide 7: Straw Poll
Do you agree to add the following table to the SFD:
Type | Type description | Presence of Frame Body field | Use of Embedded BSSID in FCS computation
0 | WUR Beacon | NO | YES
1 | WUR Wake Up | YES or NO | YES
2 | WUR Vendor Specific | YES | YES or NO (Vendor Specific)
3 | WUR Discovery | TBD | NO
4-TBD | Reserved | N/A | N/A

## Slide 8: References
[1] 11-17/575r9 specification framework (P.K. Huang, et. al.)