## Slide 1: OOK Waveform Generation Follow-up
Date: 2018-03-05
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1], 2us and 4us on-signal generation methods were proposed for high and low data rates, respectively
  64 point (or 32 point) IFFT based method with 7 length sequence and Masking based method with 13 length sequence for 2us on-signal generation
  64 point IFFT based method with 13 length sequence for 4us on-signal generation
The authors of [2] verified PER varies according to the 7 length sequence and the 32 point IFFT based method can be better than the masking based method in terms of PER
The authors of [3] verified OOK symbols with low PAPR have good performance
In [4], a high modulation level (256 QAM) was used for coefficients of 13 length sequence
In this contribution, we consider the following methods
  64 point IFFT based method with 7 length sequence for 2us on-signal generation
  64 point IFFT based method with 13 length sequence for 4us on-signal generation
We investigate performance for high and low data rates by applying various modulation levels to the coefficients of 7 and 13 length sequences

## Slide 3: Design for 7 / 13 Length Sequences (1/2)
We consider modulation levels used in 11ac to build up sequences
  BPSK, QPSK, 16QAM, 64QAM, 256 QAM
Two approaches are applied to select coefficients
  Approach 1 : Random approach
  Approach 2 : PAPR minimization approach
Two options are employed for PAPR minimization approach
  Option 1 : exhaustive search
  Option 2 : fix one coefficient, then add next one coefficient which minimizes PAPR and repeat until sequences are constructed
 | Option 1 | Option 2
7 length sequence | BPSK, QPSK, 16QAM | 64QAM, 256QAM
13 length sequence | BPSK, QPSK | 16QAM, 64QAM, 256QAM

## Slide 4: Design for 7 / 13 Length Sequences (2/2)
7 length sequence for approach 2
  BPSK : [1, 1, 1, 0, -1, 1, -1] (PAPR : 2.2377dB)
  QPSK : [1+j, 1+j, 1+j, 0, -1-j, 1+j, -1-j] (PAPR : 2.2377dB)
  16QAM : [1+j, 3+j, 3-j, 0, -1+3j, -1-3j, 1+j] (PAPR : 0.7329dB)
  64QAM : [7+7j, -1+j, 1+j, 0, -1-j, -1+j, 1+j] (PAPR : 1.4432dB)
  256QAM : [15+15j, -1+j, 1+j, 0, -1-j, -1+j, 1+j] (PAPR : 0.8123dB)
13 length sequence for approach 2
  BPSK : [1, 1, 1, -1, -1, -1, 0, -1, 1, -1, -1, 1, -1] (PAPR : 2.0589dB)
  QPSK : [1+j, 1+j, 1+j, -1-j, -1-j, -1-j, 0, -1-j, 1+j, -1-j, -1-j, 1+j, -1-j] (PAPR : 2.0589dB)
  16QAM : [1+3j, 1+j, -1-j, 3+j, 1+j, 1-3j, 0, 1+j, 1+3j, -1+3j, 1-j, -3+j, 1-j] (PAPR : 3.2936dB)
  64QAM : [7+7j, -1-j, -1-j, -1-j, -1-j, -1-j, 0, -1-j, -1-j, -1-j, -1-j, -1-j, 1+j] (PAPR : 2.4671dB)
  256QAM : [15+15j, 1+j, -1-j, 1+j, -1-j, 1+j, 0, 1+j, -1-j, 1+j, -1-j, 1+j, -1-j] (PAPR : 1.3904dB)
Option 1
Option 2
Option 1
Option 2

## Slide 5: Simulation Assumption
Sync preamble for data rate signaling as well as packet detection and timing recovery
CFO of 200ppm
phase noise for 20uW power consumption as in [5]
Butterworth filter with 2.5MHz cut off frequency, second order
4MHz sampling rate and SNR defined in 20MHz bandwidth
TGnD and UMi NLoS channels in 2.4GHz

## Slide 6: Simulation Results
7 length sequence

## Slide 7: Simulation Results
13 length sequence

## Slide 8: Conclusions
We have shown PER performance for various 7/13 length sequences based on modulation levels used in 11ac
It seems that there is no performance difference among modulation levels when focusing on the random approach
However, for the PAPR minimization approach, we have verified that sequences computed by high modulation levels such as 64QAM and 256QAM can degrade the performance although it can further reduce the PAPR
Given the relatively high PAPR for the L-SIG, the WUR data field does not need to have a quite low PAPR, i.e., PAPRs for the sequences based on BPSK or QPSK may be sufficient
Thus, BPSK or QPSK may be proper for coefficients of 7/13 length sequences in consideration of their good PER and reasonable PAPR

## Slide 9: Straw Poll #1
Do you agree to add the following to the TGba SFD?
  The following process is applied to generate 2us on-signal for the high data rate
    Apply a 7-length sequence to every other subcarrier in contiguous 13 subcarriers, i.e. 1st,3rd,5th,7th,9th,11th and 13th subcarriers and set the others to zero
      The center coefficient of 7 length sequence is zero
    Perform 64-point IFFT and choose either the first or second 1.6us signal in a 3.2us signal with 1.6us periodicity
    Prepend 0.4us GI

## Slide 10: Straw Poll #2
Do you agree to add the following to the TGba SFD?
  The following sequences are examples of 7 length sequence used to generate 2us on-signal for the high data rate
    [1, 1, 1, 0, -1, 1, -1]
    [1+j, 1+j, 1+j, 0, -1-j, 1+j, -1-j]

## Slide 11: Straw Poll #3
Do you agree to add the following to the TGba SFD?
  The following sequences are examples of 13 length sequence used to generate 4us on-signal for the high data rate
    [1, 1, 1, -1, -1, -1, 0, -1, 1, -1, -1, 1, -1]
    [1+j, 1+j, 1+j, -1-j, -1-j, -1-j, 0, -1-j, 1+j, -1-j, -1-j, 1+j, -1-j]

## Slide 12: References
[1] IEEE 802.11-18/0072r0 OOK Waveform Generation
[2] IEEE 802.11-18/0097r0 2us OOK Pulse for High Rate
[3] IEEE 802.11-18/0143r2 OOK Symbol Design
[4] IEEE 802.11-18/0156r4 Waveform Design for SYNC Field
[5] IEEE 802.11-17/0326r0 WUR Phase Noise Model Follow-Up