## Slide 1: TBD clarification for TGba D0.1 (WUR Duty cycle)
Date: 2018-03-05
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We are working on specification draft from previous meeting
  However, there are still a lot of TBDs for us to work out
  So we will address TBDs related with WUR mode signaling

## Slide 3: Duty cycle signaling in Draft v0.1
ON Duration / Duty Cycle Period subfield in WUR Parameters field
  How to signal for duty cycle information is TBD

## Slide 4: Duty cycle time unit
Time unit for duty cycle period isn’t described in D0.1 from SFD
  [R.4.3.B] The period of the WUR duty cycle as shown below is a multiple of a basic unit. The basic unit is indicated by the AP. The on duration in each period for WUR duty cycle as shown below is larger than or equal to a minimum wake-up duration. The minimum wake-up duration is indicated by the AP.
This motion will be carried in D0.2 [Assigned to Po-Kai]

## Slide 5: Time unit for Duty cycle Period
We may use TU or define a new unit for WUR duty cycle period
  A unit of usec level will not be suitable for WUR duty cycle operation
We prefer reuse of TU for basic time unit
  We may use multiple of TU (e.g. 1 TU, 4 TU, 16 TU, etc...)
  If we allocate one octet for Duty Cycle Period Units field, maximum value of time unit will be 255 TU (261 msec)
    That value seems enough

## Slide 6: Duty Cycle Period subfield
Duty cycle period shall be long enough to support long sleep
  If we allocate one octet for Duty Cycle Period subfield, maximum period will be 65025 TU (66.5 sec)
  If we allocate two octets for Duty Cycle Period subfield, maximum period will be about 4.6 hours

## Slide 7: ON Duration subfield
There are two way to signal ON Duration subfield
  Use TU for unit
  Use duty cycle period unit
If we allocate one octet for ON Duration subfield, maximum value of On duration will be
  255 TU when we use TU for unit
  or 65025 TU (66.5 sec) when we use duty cycle period unit
We slightly prefer first option
  If we use duty cycle period unit, it may be difficult to signal detailed values

## Slide 8: Signaling for Non duty cycle mode
We can allocate some values for non duty cycle mode
  For example, the WUR STA will operate in non duty cycle mode (a.k.a. always WUR ON mode), when it received WUR Action frame with Duty Cycle Period subfield set to 0

## Slide 9: Summary
In this submission, we address TBDs in WUR duty cycle operation
We have proposed details of time unit, On duration, duty cycle period

## Slide 10: Straw poll 1
Do you agree to followings?
  Duty Cycle Period Units field is set to the time unit of the WUR duty cycle period, expressed in number of time units (TUs)
  The length of Duty Cycle Period Units field is 1 octet

## Slide 11: Straw poll 2
Do you agree to followings?
  The length of Duty Cycle Period subfield is 1 octet

## Slide 12: Straw poll 3
Do you agree to followings?
  On Duration subfield is set to the length of preferred On Duration that the WURx of the WUR non-AP STA will be in WURx awake state for each WUR duty cycle schedule, expressed in number of time units (TUs)
  The length of On Duration subfield is 1 octet

## Slide 13: Straw poll 4
Do you agree to followings?
  A WUR STA will operate in non duty cycle mode (a.k.a. always WUR ON mode), when it received WUR Action frame with Duty Cycle Period subfield set to 0