## Slide 1: Full Duplex Benefits and Challenges
Date: 2018-13-02
Authors:

## Slide 2: Background
Simultaneous Transmission and Reception (STR) is now being investigated as a candidate for Full Duplex (FD) technology for the next generation of 802.11 [1]
The idea to allow transmission and reception using the same time and frequency resources is not new for wireless communications; however it should be investigated deeply with application to 802.11 technology
We believe that FD can be a key technology for the next generation of Wi-Fi
Hence, we are trying to determine what has to be done in order to achieve the theoretical benefits of STR in Wi-Fi networks

## Slide 3: Major Potential Benefits of STR
The major benefits of STR technology are:
  Throughput gain – twice the amount of data transmitted on same resources
  Lower latency – we can reduce latency per specific STA or entire network (for example - ACK time, SIFS period reduction, etc.)
  Collision reduction – DL signal prevents potential hidden nodes from transmitting during UL
  Network issues relaxation – for example, a solution for relay-based networks (multiple relays supporting FD can transmit simultaneously)
Those are very promising theoretical benefits that can bring Wi-Fi technology to new heights
We are now trying to understand how to support it in practice!!!

## Slide 4: STR Aspects
Physical aspects:
  Self-Interference Cancellation (SIC) is the most complex problem to be solved for STR feasibility
Link Level Aspects:
  What are the conditions to achieve maximum gain?
  What information exchange is required to apply STR?
System Level Aspects
  Should non-AP STAs support STR?
  Which STAs can participate in STR transmission?
  Is there any relationship between STAs involved in STR?
  What is the system level overhead required for STR benefit?
Physical
Level
System Level
Link Level
Tx
Rx
STA Tx
STA Rx

## Slide 5: Self Interference Cancellation
Tx signal produces an interference that needs to be mitigated on Rx side to be below the expected noise level
The main interference components are:
  Internal reflections – 15-20dB lower than Tx signal
  Non-linear components – 30-40dB lower than Tx signal
  Multipath – 50-60dB lower than Tx signal
Most of the research papers (for instance [2]) divide the SIC problem into two parts:
  Analog SIC – reduces the strongest components
  Digital SIC – completes the action on sampled signal to reduce the interference below the noise floor
We also need to define an efficient SIC calibration procedures with minimum overhead
20dBm
5dBm
-15dBm
-35dBm
-90dBm
Interference Signal
Antenna Isolation
Nonlinearity
Multipath
Noise Floor
110dB
95dB
75dB
55dB

## Slide 6: SIC Research Challenges
Practical LNA can handle signal below -30dBm which means approximately 50-60dB should be removed in RF
In order to reduce the interference below the noise floor, we need additional digital cancellation of about 60dB
Moreover, we need to consider higher dynamic range due to the difference between the desired signal and the interference
We summarize the challenges of the self-interference cancellation as:
  Design of complex analog and digital blocks
  Minimize the SNR degradation (e.g. A/D with higher dynamic range)
  Define efficient calibration procedures (that do not degrade performance)

## Slide 7: Link Level Aspects
Assuming we solved the problem of self-interference cancellation, we need to know how to decide whether to apply FD or half-duplex?
The following aspects may impact link budget:
  Change in RF properties
  SNR is limited due to residual interference
  Noise floor is higher due to different RF settings
We need to know how to improve the throughput of the specific transmission compared to half duplex
An STR-related link budget definition is required to allow accurate decisions!
SNRHD
SNRFD
compare

## Slide 8: System Level Aspects
System level aspects should be considered in order to maintain the benefits of STR in the entire network
We recognize two main topics: overhead issues and system protocols
System level overhead questions (we want to minimize overhead)
  Which additional resources (frames/signal/fields) are needed to support STR?
  Which STAs can be involved in STR, what is required to make the right decision?
System level protocols (ensure the gain is maximized)
  Can we combine STR and MIMO/OFDMA?
  How we keep backward compatibility in presence of STR?

## Slide 9: Summary
This presentation explains which aspects have to be addressed to support the theoretical benefits of STR in the next generation of 802.11
We believe that fundamental aspects of research should be:
  SIC aspects
  Link level aspects
  System level aspects
We think that the main targets of the Full Duplex TIG should be:
  Focusing on identifying where full duplex indeed reaches its theoretical benefits with respect to fundamental aspects above
  Justifying the throughput gain compared with the existing Wi-Fi systems

## Slide 10: References
[1] IEEE 802.11-18/0191r0, 802.11 Full Duplex
[2] Brahadia, D., McMilin, E., Katti, S., SIGCOMM’13, August 12–16, 2013, Hong Kong, China, Full Duplex Radios